## Slide 1
BTOF loading
Dr. Simone M. Mazza (SCIPP, UC Santa Cruz)
For the BTOF/FTOF group

## Slide 2: Questions/Comments
What loading precision do we require?
When Jigs/Tooling need to be ready? Useful to have them while loading the 10 stavelets to develop process
Figure out the material budget impact and if it’s fine
Figure out right carrier for shipping (might know already)
Need to figure out importing if Japan pays for components

## Slide 3: Pickup jig
Vacuum jig to pickup loaded stavelet and assemble with stave
UIC first version almost ready
Glue to stave? Assemble with screws?
This step NOT at UCSC, Purdue or BNL? UV glue likely not working
Precision pin
Vacuum nozzles
Full stave
Glue?
screw?
Thermal paste

## Slide 4: Loading jig
Component loading jig
  Back support (vacuum) with pins
  Loading component that goes on pins
  Precision pins needed
Other option: pick and place loading
  Need pick and place machine
Back jig will stay with stavelet during wire bonding
ASIC
Sensor
Interposer FPC
Slots
Precision pin
Deposited glue
Component ‘press’ jig
Soft material

## Slide 5: Shipping jig
Houses multiple stavelets for shipping
Backside and frontside ‘clamping’ with soft material the components
Stavelet

## Slide 7: Backup

## Slide 8: TOF layout in ePIC
Off-Momentum Detectors (OMD)
Sensors: strips
Readout: FCFD
Sensors: pixels
Readout: EICROC
Sensors: pixels
Readout: EICROC
Divided in two halves
(outdated figures)
(mostly outdated schematics)

## Slide 9: Stave Assembling Steps (Opt1)
Sensor + ASIC
Interposer
FPC
Glue dispenser
Wire bonding
Module-to-Module bonding machine
Support structure (Carbon fiber)
Module Assembly Site
Final Construction Site
Glue dispenser
Cooling pipe and return (10-20C)
FPC
Stave Front/Back

## Slide 10: Stavelet demonstrator - 2025
Plan to demonstrate the assembly procedure and study the thermal characteristic of a stavelet
First prototype of interposer board produced
Using non-working detectors from the HPK production
Si heaters to simulate ASIC
Fully load a double-sided stavelet with active pipe cooling and check thermal dissipation in prototype

## Slide 11: Data Transmission
Front-side
Back-side
8 x 2 x 288 =4608
Half-Stave = 8 x Modules = ~ 1320 [mm]
Module (Stavelet) ~ 160 [mm]
3 x 8 x 2 x 288
=13824
2 x 8 x 2 x 288
=4608
21 [mm]
Service Hybrid
33 [mm]
lpGBT
VTRx
x4
FPC
Interposer
Sensor
CFDROC
(ASIC)
X/X0 < 3% (including support structure)
DCDC
Backend
32 (front-side) + 32 (back-side) = 64 CFDROCs
600 [mm]