## Slide 1: pfRICH Sensor Plane
Simon Snydersmith, Sushrut Karmarkar, Andreas Jung
23 March, 2026

## Slide 2: End Ring Hole Check
Hole pattern based on probe points from end ring 3
3-part waterjet-cut ring to check end ring hole alignment before cutting final sensor plate
Price from Xometry:
  1/8 in aluminum $94
  ¼ in aluminum $167
  ¼ in HDPE $136
Sourcing properly sized stock likely more expensive

## Slide 3: References to hole location, marks on test parts

## Slide 4: Outer Mirror Backer
Thickened uprights to allow for 0.225 inch 10-32 inserts
Flattened back of uprights for mounting
Problem of mirror backer interference with cylinder
Requires top mounting hole to move or removable section of backing

## Slide 5: Mirror Manufacturing updates
One outer mirror with Lexan bonded
One 24x12 in flat plate ready to cut to sample size
Ordered more 0.03 in thick lexan for 2nd outer mirror and inner mirrors

## Slide 6: Current Dimensions and Features
Outer radius: 1300 mm
Bolt hole placement derived from End Ring 3 scan
15, 120.5 mm sensor frames
Center circle and air ports derived from Alex CAD
3 mm combined wall thickness
1/8 in radius on square holes

## Slide 7: Sealing Thickener
H-design, 2 o-rings
Unglued spacer allows for:
  Independence of sealing from bonding precision
  Simpler machining and assembly
1/8 in O-rings require 7 mm thick spacer

## Slide 8: Outer Mirror
NPT ports moved outward radially by 5 mm
Slot Modified to fit bulkhead fittings
Easy to change 3D printed part
6 Mounting holes added to mirror backer, 6.23 in spacing
Inserts for 10-32 screws?