## Slide 1
RCDAQ organization
We will be running O(4) RCDAQs, 2 for the 2 KCUs (0/1), one Astropix (2), one for the 2 CAENs (3)
Independent RCDAQ servers are started with (I already made the scripts in ~/rcdaq_scripts ) rcdaq_server n, like “rcdaqserver 3”
The rcdaq_client commands by default talk to server 0.
In order to talk to another server (just for one command), do
If in your session you will continue to work on a particular server (like Henry did this morning), set the session up with
While we are running as individual RCDAQs (not as one cohort with Run Control yet), be very careful not to mess with the wrong one
$ RCDAQHOST=localhost:3 daq_status
$ export RCDAQHOST=localhost:3
… commands …
Reminder

## Slide 2
RCDAQ Elog interactions
I added the elog updates to the RCDAQ setup scripts
Later today or tomorrow I’ll set up our Run Control so that >1 (or all 4) RCDAQs can act as a coherent unit
Some “un-sPHENIX-ing” still going on to unravel the tie-in with our trigger and timing units. (ePIC branch in git)

## Slide 3
AstroPix success
Bobae and I got the Astropix readout to work yesterday.
According to Bobae the data make sense.
I have started with an onl. monitoring skeleton but it needs some more knowledge from Bobae to cash in what already exists
(base) mep@carbon:~$ ddump -e3 -n 5 /scratch/data/AstroPix/junk/junk_AstroPix-00000051-0000.evt
Packet 13001 10 -1 (ePIC Packet) 350 (IDASTROV1)
Nr of units: 2
# | layer id payload location iscol ts ToT fpga_ts
0 | 1 3 4 15 0 168 90 1734872274
1 | 1 3 4 14 1 168 68 527043794
Packet 13001 10 -1 (ePIC Packet) 350 (IDASTROV1)
Nr of units: 2
# | layer id payload location iscol ts ToT fpga_ts
0 | 1 3 4 15 0 242 57 -2086039851
1 | 1 3 4 14 1 242 36 1001098965
Packet 13001 10 -1 (ePIC Packet) 350 (IDASTROV1)
Nr of units: 2
# | layer id payload location iscol ts ToT fpga_ts
0 | 1 3 4 11 0 126 131 -912007978
1 | 1 3 4 13 1 126 108 -2119836458
Packet 13001 10 -1 (ePIC Packet) 350 (IDASTROV1)
Nr of units: 2
# | layer id payload location iscol ts ToT fpga_ts
0 | 1 1 4 10 0 151 439 1225466839
1 | 1 1 4 11 1 151 417 17638359
Packet 13001 10 -1 (ePIC Packet) 350 (IDASTROV1)
Nr of units: 2
# | layer id payload location iscol ts ToT fpga_ts
0 | 1 1 4 16 0 109 981 2044672727
1 | 1 1 4 22 1 109 961 836844247
Some polishing still needed… time stamps shouldn’t be a) negative and b0 not so far apart?

## Slide 4
AstroPix
What I showed on the last slide is with a super-low rate, currently making one hit = 1 Event.
Normally it’s many hits / RCDAQ Event (or TimeFrame)
Nr of units: 181
# | layer id payload location iscol ts ToT fpga_ts
0 | 1 3 4 15 0 192 113 -855090086
1 | 1 3 4 14 1 192 90 -2062918566
2 | 1 3 4 24 0 16 67 -56292259
3 | 1 3 4 28 1 15 46 -1264120739
4 | 2 3 4 21 0 202 73 -472371105
5 | 2 3 4 27 1 202 52 -1680199585
6 | 1 3 4 21 0 47 464 355706722
7 | 1 3 4 17 1 47 440 -852187294
8 | 1 3 4 15 0 79 84 -62235037
9 | 1 3 4 14 1 79 61 -1270063517
10 | 1 2 4 18 0 162 101 -1559535005
11 | 1 2 4 15 1 162 78 1527603811
12 | 1 3 4 11 0 28 145 1204474212
13 | 1 3 4 13 1 28 121 -3419804
14 | 2 0 4 0 0 229 2789 -2117345436
15 | 2 0 4 32 1 229 2773 969793380
16 | 1 3 4 24 0 143 73 -151573915
17 | 1 3 4 28 1 143 52 -1359402395
18 | 1 3 4 11 0 177 203 -1272401563
19 | 1 3 4 13 1 177 179 1814737253

## Slide 5
Things still in progress
I mentioned Run Control
A “Billboard Online Monitoring” setup (look at the manual) (presumably on the upper monitor for starters, but best in another VNC session I think)
Where are we remote MPOD control?
And the power strip?
File transfers (need a destination, ANL? BNL? )
Also need to think of backups – if that carbon home disk croaks, we’ll start over…
There was a lot of confusion when you go my route and log in with “ssh carbon” b/c you need 3 different passwords – hallgw (cannot be changed), the bnl-daq, then carbon
I’m proposing that I make the bnl-daq pw the same as carbon for mep to avoid confusion