## Slide 1: RHIC – The heavy ion story
9 July 2026, RHICfest
Wolfram Fischer
(Only a short while ago: System Commissioner – Injection; Commissioner – A Team)
Notes: 30 min = 30 slides

## Slide 2
Relativistic Heavy Ion Collider
New York City

## Slide 3: Contents
Before RHIC:
  The Alternating Gradient Synchrotron (AGS) and Isabelle/CBA
RHIC
  Design choices – more from Steve Tepikian, Jie Wei
  Performance evolution
  Accelerator Science and Technology legacy
  (Polarized beam story – presentation by Thomas Roser)
After RHIC:
  The Electron-Ion Collider

## Slide 4: Before RHIC: AGS and Isabelle/CBA

## Slide 5
[Y.Y. Lee, ”50 years of the BNL AGS”, 14th Intl. Conf. on Accelerator and Beam Utilization, Gyeongju, Korea (2010).]
No 200 MeV Linac yet (1970) No 1.5 GeV Booster yet (1990)
1959: CERN PS

## Slide 6: ISABELLE collider proposal
Early 1970 studies for 200+200 GeV proton-proton collider superconducting magnets (enough to see W, Z – discovered at SppS with 270+270 GeV in 1983)
3.8 km circumference, 6 intersections, AGS as injector
At the same time Fermilab started working on the Tevatron
Tunnel, office building, He cryo plant built (updated and in use for EIC)
Only one working dipole prototype (Mark V) – sc cable issues
In 1982 Isabelle became CBA (Colliding Beam Accelerator), with working magnets
1983 canceled in favor of SSC – W and Z were discovered at SppS (SSC itself canceled in 1993)
BNL quickly build a heavy ion physics program with AGS Ions from Tandem Van de Graaff, transfer line to AGS 1986
Ernest Courant 1920-2020
[Ernest D. Courant, “Accelerators, colliders, and snakes”, Annu. Rev. Nucl. Sci. 2003. 53:1-37]

## Slide 7: Heavy ion program at AGS
RF
Tandem Van de Graaff
Completed in 1970 for NP studies
RHIC pre-injector until 2011 (now EBIS)
2 electrostatic accelerators
32 MV (= 2x16 MV) voltage
>40 ion species p to Au
Fixed target experiments
Heavy Ion Transfer Line (HITL), operational 1985
Notes: No EBIS, NSRL, AtR, Tandems pic

## Slide 8: RHIC Design energy – luminosity – flexibility

## Slide 9: Relativistic Heavy Ion Collider
1984 began to think about heavy ion collider
~100 GeV/nucleon, dipoles ~3.5 T (5 T for ISABELLE/CBA)
transfer line from Tandem, develop heavy ion beams in AGS, with heavy ion experiments
1991 construction begins
2000 first collisions
[Ernest D. Courant, “Accelerators, colliders, and snakes”, Annu. Rev. Nucl. Sci. 2003. 53:1-37]
Satoshi Ozaki
Mike Harrison
Tom Ludlam

## Slide 10: Relativistic Heavy Ion Collider – main parameters
RF
RHIC
NSRL
LINAC
Booster
AGS
Tandems
STAR
(s)PHENIX
(PHOBOS) Electron lenses
Polarized Jet Target
(BRAHMS) Electron cooling
EBIS
BLIP
TPL
Collisions : 12 Jun 2000 – 6 Feb 2026
Circumference : 3.8 km
Max dipole field : 3.5 T Energy : 255 GeV polarized p : 100 GeV/nucleon Au
Species : ph to U (incl. asymmetric) Experiments : BRAHMS, PHOBOS, pp2pp, AnDY,
RHICf, PHENIX, STAR, sPHENIX
DOE Under Secretary for Science Dario Gil ending last RHIC store (oxygen-oxygen)

## Slide 11: RHIC Design Manual
reached Lavg = 88×1026 cm-2s-1 (44x design)
reached Lavg = 24.8×1031 cm-2s-1 (25x design) with Pavg = 57%

## Slide 12: Important design choices
2 rings (almost independent) => flexibility
Dipole first IR => flexibility (only 6 common magnets, ran at burn-off limit, more focusing not very helpful)
3.5 T dipole field => high enough to create QGP (wasn’t really known), low enough to control cost/performance risk
Crossing transition => was a risk with sc magnets (issue with electron clouds, could be resolved)
Nested IR PS (ok but not easy)
(Stainless steel pipe not coated => was ok for RHIC, not EIC)
Notes: New slide, 9 Apr 2026

## Slide 13: RHIC Design Manual (July 1998)
IR design with beam splitting DX dipoles first
DX dipole
D0,Q1—Q3
DX dipoles
Lmag = 3.7 m, Bmax = 4.3 T
large aperture (18 cm coil ID)
only magnets that need training (~5 for IR6/8 only)
 Interaction Point
Notes: MAKE REAL CALCULATION FOR DX MOVE

## Slide 14: Transition crossing – with sc magnets
[M. Harrison, S. Peggs, and T. Roser, “The RHIC accelerator”, Annu. Rev. Nucl. Sci. 2002. 52:425-369]
Topic of Jie Wei’s PhD thesis (1989)
Did limit intensity for some time:
Initially no gamma-t quads
Electron clouds
Instabilities

## Slide 15
Claudia Ratti,
University of Houston
RHIC CDR, 1986

## Slide 17: RHIC performance evolution luminosity

## Slide 18: Luminosity limits – ions, high energy
Bunch intensity Nb, limited by injectors EBIS, bunch merges in Booster and AGS transition instability
Intrabeam scattering luminosity lifetime stochastic cooling
Lattice with small b* and large off-momentum dynamic aperture with hourglass factor ≈0.5 at end of store limits potential ran with b* = 0.7 m vs. 1.0 m design
Goal is to have burn-off as the dominant beam loss mechanism.

## Slide 19: Au bunch intensity evolution
Main limits: - injectors output - e-cloud in RHIC
transition instability incoherent effects
Final Run-25
AGS 12g6g2 merge
EBIS, Booster 4g2g1, AGS 8g4g2 merge
scrubbing with protons
111 bunches
43 bunches
gt-jump, octupoles at transition
44x Lpeak (all other things equal)

## Slide 20: Electron clouds
E-clouds limited RHIC intensity beginning in 2001 through: dynamic pressure rise, tune shifts, transition instabilities, and possible emittance growth
Electron detector signals tracked DP; measured DQ + simulations => cloud densities of ~1011–1012 m-3
Mitigations
• Large scale NEG-coated warm beam pipes (most effective) • In-situ baking • Solenoids (local) • Optimized bunch patterns • Pre-pumped cold sections • Beam scrubbing • Longer bunches
Outcome
• Reduced DP by orders of magnitude
• Remained an operational consideration, (transition, locations that could not be baked or coated)
DP
Bunch intensity in train with intentional gaps before and after crossing transition energy

## Slide 21: Early interest in cooling for RHIC
Simon Van der Meer, 1984

## Slide 22: 3D stochastic cooling for heavy ions
M. Brennan, M. Blaskiewicz, F. Severino, PRL 100 174803 (2008); K. Mernick PRSTAB, PAC, EPAC
longitudinal kicker cavity (half side with waveguides)
horizontal kicker (open)
horizontal and vertical pickups
longitudinal pickup
5-9 GHz, cooling times ~1 h
vertical kicker (closed)
Notes: Frequency range: 5-8 GHz transverse, 6-9 GHz longitudinal

## Slide 23: RHIC Run-14 Full 3D Cooling
2007, Beginning of stochastic cooling upgrade
2014, End of stochastic cooling upgrade
Increase in initial luminosity result of larger bunch intensity
Increase in luminosity lifetime result of 3D bunched beam cooling, >90% burn-off
More detail in presentation by Mike Blaskiewicz

## Slide 24: Operation at burn-off limit in U+U
97% of intensity burned off at Lmax
Burn-off dominated operation allows for determination of total U+U cross section – and comparison with calculation (mostly QED) (published in Phys. Rev. C) =>

## Slide 25: How did stochastic cooling change heavy ion collider operation?
Increased in luminosity lifetime from ~2.5 h Au+Au up to infinite
Allowed for increase in bunch intensity L ~ Nb2
Increased optimum store length from 4 to 8 h for Au+Au, resulting in more time in collision, less time refilling
Can tolerate emittance growth during acceleration (from IBS, transition instabilities) as long as no intensity is lost
Operation close to burn-off limit, full use of accelerated intensity
Allowed flat luminosity for alternating species (Ru+Ru/Zr+Zr)

## Slide 26
15 weeks Run-1 could be done later in 1/2 day (200x faster)
Final Run-25

## Slide 27
LRHIC, Au  LLHC, Pb with gLHC, Pb ~ 27x gRHIC, Au

## Slide 28: RHIC performance evolution flexibility

## Slide 29: RHIC performance – flexibility
Medium heavy (Cu+Cu, O+O)
Asymmetric collisions (p+Au, d+Au, h+Au, Cu+Au)
U+U (non-spherical)
Zr+Zr / Ru+Ru (same A = 95, max different DZ = 4)
Au+Au luminosity at 3.85 to 9.8 GeV/nucleon (Beam Energy Scan, including a fixed target program)
only ion combination shared between
RHIC and LHC are O+O and p+p (polarized in RHIC)

## Slide 30: Beam control – x,y + Q/Q’ feedbacks on ramp
Blue orbits
xmean
ymean
xrms
yrms
M. Minty, A. Marusic et al.
Qx
Qy
Qy = 2/3
DQy = 0.006
x,yrms ≈ 20 mm, 5% of arc beam size (!)
Orbit feedback on every ramp allows for
Smaller yrms (smaller imperfection resonance strength)
Ramp reproducibility (have 24 h orbit variation)
Tune/coupling feedback on every ramp allows for
Acceleration near Qy = 2/3 (better P transmission compared to higher tune)
0.7
0.66
-0.2
0.3
Orbit [mm]
Tune
Notes: Fillno 15443, one of best stores

## Slide 31: Run-18 Zr+Zr/Ru+Ru – same A, different Z (CME) Zr-96/Ru-96
Extraordinary help from DOE, ORNL, RIKEN for source material and preparation
Ru isotopes

## Slide 32: Run-18 Zr+Zr/Ru+Ru at 100 GeV/nucleon
Run Coordinator: Greg Marr
Zr+Zr
Ru+Ru
Zr+Zr
Ru+Ru
Ru+Ru
Zr+Zr
Ru+Ru
Zr+Zr
CeC PoP dedicated
scheduled maintenance
Store-by-store species change and flat luminosity of 21.5×1026 cm-2s-1
20 h nominal store length (WEEK: 30-Apr-18 to 07-May-18)

## Slide 33
L design
nominal injection
L design
Used stochastic or electron cooling in 1 or 2 beams

## Slide 34: RHIC performance evolution energy – down to 30% of design injection energy
Notes: Design dipole current 568 A for GeV/n 97 GeV/n Au injection; dipole current at 190 A for 3.85 GeV/n Au injection; nominal injection lowered to 470 A dipole current

## Slide 35: Low-Energy RHIC electron Cooling (LEReC) for the Beam Energy Scan I and II (BES-I, II)
[2015 NSAC Long Range Plan for Nuclear Science]
BES-I in 2010/11/14
BES-II: 10x increase in the number of events
Au+Au collisions down to 3.85 GeV/n (40% of CoM energy at nominal injection, 30% of design)
Luminosity really low:
Space charge Intrabeam scattering Magnetic field errors (also time dependent) Large beam with losses
BES-II goal of 4x luminosity over 3.85 – 9.8 GeV/n (highest energy is nominal injection)
Designed cooler for 2 lowest energies
Notes: Picture from 2015 NSAC long-range plan

## Slide 36: LEReC Accelerator (100 meters of beamlines with the DC Gun, high-power fiber laser, 5 RF systems, including one SRF, many magnets and instrumentation)
COOLING
in Blue RHIC ring
COOLING
in Yellow RHIC ring
High-Power Beam Dump
Extraction beam line
DC e- Gun
704 MHz SRF
Booster Cavity
2.1 GHz Cu Cavity
9 MHz Cu Cavity
704 MHz Cu Cavity
Injection beam dump
RF Diagnostic Beamline
RHIC TRIPLET
RHIC DX
180°
Bending
Magnet
e-
e-
e-
* NOT to scale
Cathode
loading system
LF solenoid
HF solenoid
Transport solenoid
ERL solenoid
Quad corrector
Trim corrector
Corrector 3.8 ID
Corrector 6.0 ID
BPM 2.4 ID
BPM 4.8 ID
Bellows
Ion pump
Merger
Beamline
Transport
Beamline
704 MHz Cu Deflector Cavity
More in presentation by Alexei Fedotov

## Slide 37: Low Energy RHIC electron Cooler
A.V. Fedotov et al., “Experimental demonstration of hadron beam … “, PRL 124, 084801 (2020)]
LEReC operational electron cooler:
  utilizes RF-accelerated electron bunches
  uses non-magnetized electron beam (no magnetization at the cathode and no continuous solenoidal field in cooling section)
LEReC approach to cooling is directly scalable to high-energies – pre-cooler in EIC at injection

## Slide 38: BES-I vs BES-II luminosity
Run Coordinator: Chuyu Liu (Run-19 to 21)
3rd year
1st year
2nd year
Goal was
Lavg (BES-II) = 4x Lavg (BES-I)

## Slide 39: Run-25 … to the finish line

## Slide 40: Final Run-25 Au+Au
[mb-1]
damaged 69 kV power line
repair shut off Central Cryo Plant
required managing helium inventory
15 days
unsynchronized beam abort
Yellow abort vacuum repair
14 days
Run Coordinator: Travis Shrey
short in superconducting bus
repair required partial warm-up
opened several cryostats
65 days

## Slide 41: Run-25 STAR and sPHENIX event rates
Maintenance day
STAR 0 mrad crossing angle
sPHENIX 1 mrad crossing angle
Oct/Nov 2025

## Slide 42: From RHIC to EIC
Protons: 40 – 275 GeV
Electrons: 5 – 18 GeV
RHIC
EIC
p – U
Au: 3.85-100 GeV
p 60% polarization

## Slide 43: RHIC’s 25 years of physics …
Great design – allowed for significant upgrades
Evolving physics program, strong community and funding agency support – DOE NP
Full energy Au+Au Lavg = 44x design New: bunched-beam stochastic cooling
Only p+p collider, Lavg = 1.3x design, P ~ 57% (70% design) New: p polarization preservation to high energy
12 species combinations (incl. asymmetric), 18 center-of-mass energies, low-abundance isotopes New: built-in flexibility, high-intensity high-brightness ion/p sources, x,y+Q/Q’ feedbacks
Extended energy range slightly above; and significantly below nominal injection New: electron cooling with RF accelerated e-beam
RHIC operation concluded 6 February 2026 Most of RHIC complex will be re-used for the Electron-Ion Collider Hadron injectors, RHIC tunnel, Yellow ring (part of Blue), Technical Infrastructure, New technologies above
Nominal injection
[APS DPB Newsletter on RHIC: https://engage.aps.org/dpb/resources/newsletters/25-newsletter/2025-f7]