## Slide 1: Ion Sources: Enabling 25 Years of RHIC Operations (2000–2025) and the Path to the EIC
RHICfest
July 10, 2026
Deepak Raparia

## Slide 2: Acknowledgements
Contributors:
J. Alessi, G. Atoian, E. Beebe, C. Carlson, B. Coe, A. Cannavo , C. Ianzano, S. Ikeda, A. Kponou, T. Kanesue, S. Kondrashev, T. Kubley, T. Lehn, V. Lodestro, G. London, M J. Maxwell (JLAB), R. Milner (MIT), S. Pikin, A. Poblaguev, J. Ritter, R. Schoepfer, B. Snyder D. Steski, A. Sukhanov, P. Thieberger, S. Trabocchi, R. Vorbach, N.B. Wuerfel (MIT). A. Zelenski
Collaborators
Retired
D. Raparia, CAD Seminar 24/09/13

## Slide 3: Outlines
Introduction
Light and Heavy ions
-Tandem
-EBIS
Polarized
-OPPIS
-He-3 in progress
Conclusions

## Slide 5: Evolution of RHIC Sources
Year | Source
2000 | Tandem begins RHIC operation
2001 | First polarized proton collisions (OPPIS)
2012 | EBIS as primary heavy-ion injector
2025 | Final RHIC operations
2026 | Transition to EIC era- addition of Pol He-3
Three sources supported one collider.
Each source solved a different challenge

## Slide 6: Tandem

## Slide 7: BNL Tandem Van de Graaffs
Commissioned 1970
1983: P. Thieberger et al. demonstrated that the Tandem could produce pulsed beam using a Cs Sputter Ion Source
RHICfest: Raparia 260710
D. Steski

## Slide 8: HITL and TtB direct injection into AGS and Booster
May 19, 1986, Oxygen beam circulated in AGS
1992: first acceleration of Au beam in the Booster and AGS
RHICfest: Raparia 260710
D. Steski

## Slide 9: Highlights
Tandem begins operation. 1970
First heavy ions from Tandem to AGS via HITL 1986
Booster replaces direct HITL injection 1991
First circulating Au beam (1999)
2000 First RHIC Au+Au collisions
Collision of asymmetric masses d-Au using both MP6 and MP7 (2003, 2008, 2016, 2021)
Cu-Cu collisions (2005)
Isobar experiment 96Ru from Tandem 96Zr from EBIS (2018)
Final ion beam O-O supplied from Tandem (2026)
RHICfest: Raparia 260710
D. Steski

## Slide 10: EBIS

## Slide 11
Advantages of the new preinjector:
Simple, modern, low maintenance
Lower operating cost
Can produce any ions (U, He3)
Higher Au injection energy into Booster
Fast switching between species
Short transfer line to Booster (30 m)
Few-turn injection
No stripping needed before the Booster
Expect future improvements to lead to
higher intensities
860 m transport line to Booster
Stripping foils at terminal and high energy
  lead to intensity & energy spread variations
Injection over > 40 turns is required
Limitations on ion species (must start with
negative ions)
High maintenance, manpower
Low Momentum spread
Higher beam current
Tandem as preinjector

## Slide 12: EBIS as Preinjector
1994
RHICfest: Raparia 260710
1979

## Slide 13: EBIS Test Stand
RHICfest: Raparia 260710

## Slide 14
Received at 10th International Conference on Ion Sources (Dubna)

## Slide 15
Ions | He - U
Q / m | ≥1/6
Current | > 1.5 emA (20 s)
Pulse length | 10-40 s
Rep rate | 5 Hz
Output energy | 2 MeV / u
Time to switch species | 1 second
EBIS Preinjector (2 MeV/u)
EBIS
RFQ
IH LINAC
BEAM TRANSPORT LINE
BIG BEND
BOOSTER
EBIS
RFQ
IH LINAC
LION
HCIS2
HCIS1
TOF
HCIS2
HCIS
LION
17 keV/u
300 keV/u
2 MeV/u
RHICfest: Raparia 260710
BNL Science and Technology Award

## Slide 16: LION (Low charge state LIS)
Target for NSRL
Target for RHIC
(Rotating Au, 2.2 mm/5 sec)
Successful operation since 2014
Fast species switching - within several seconds (positions of target materials)
Keep high vacuum - good for EBIS operation
Controllable beam current - solenoid plasma guide control without effecting pulse timing
Good emittance - beams extracted from cold plasmas
Robust operation - since commissioning, almost no down time
M. Okamura, T. Kanesue, S. Ikeda , C.J, John (Halinski)
RHICfest: Raparia 260710
2016 Science & Technology Award

## Slide 17
EBIS beams run to date on RHIC EBIS
D, 3He2+, 4He1+,2+, Li3+, C5+,6+, O7+, Ne5+, Al5+, Si11+,12+, Ar11+, Ca14+, Ti18+, Fe20+,24+, Cu11+, Kr18+, 90Zr15+, 96Zr16+, Nb16+, Xe27+, Ta38+, 184W31+, Au32+, Pb34+, 232Th39+, U39+
1 second switching between species (2, or more), alternating
<30 second switching among almost any 10, if loaded into external sources
RHICfest: Raparia 260710

## Slide 18: Extended EBIS
E. Beebe, B. Coe, S. Ikeda, T. Kanesue, S. Pikin, S. Kondrashev, D. Raparia, J. Ritter, R. Schoepfer , R. Vorbach
Dual Trap Regions: EEBIS introduced a pioneering design, making it the world's first ion source with two trapping regions. This innovative configuration enhances ionization and trapping processes, demonstrating the potential for significant advancements in ion source technology.
Efficient Gas Delivery: The integration of a pulse valve enables precise and efficient gas supply directly into the trapping regions. This optimization improves overall functionality, contributing to the successful operation of EEBIS.
External drift tube construction with differential pumping stages and custom pump out manifold to provide space for gas reservoir high field polarization cell
An innovative pulsed valve: Valve operating on the Lorentz force mounted to the gas ionization cell drift tube via a compact insulator
Polarized He-3: High field 3He polarization cell and purification system (tested in a separate solenoid)
RHICfest: Raparia 260710

## Slide 19: Timeline of EBIS
29 Jun 2010 — First EBIS beam transported to Booster
2 Jul 2010 — First EBIS beam circulating in Booster
2011 — First EBIS Au and U beams commissioned through AGS and RHIC
2012 — First RHIC physics run using EBIS ions (U+U, Cu+Au)
2023 --- EBIS upgrade with two solenoid
2026 -- He-3, gas cell installation and commissioning
Highest Au intensity 2e-9 per bunch in RHIC in 2016
RHICfest: Raparia 260710

## Slide 20: OPPIS

## Slide 21
STAR
PHENIX
AGS 24 GeV
LINAC
BOOSTER 2.5 GeV
H- polarize source OPPIS
Spin Rotators
Strong and Partial
Siberian Snakes
200 MeV polarimeter
RHIC pC “CNI” polarimeters
RHIC
Absolute H-jet
polarimeter
AGS pC “CNI” polarimeter
The world’s only polarized proton collider: 60% proton polarization , L max=1.61032 s-1cm-2; 50<√s <510 GeV
Polarization facilities at RHIC
Siberian Snakes
Siberian Snakes
RHICfest: Raparia 260710

## Slide 22: BNL pulse polarized H- source (1982)
Atomic Beam
Pulse Ground state atomic beam line with an RF Disassociator (pulse), Nozzle thermalized at 100 K
Sextupole for electron polarized beam
RF transition for polarization transfer to Nuclear Pulse to pulse basis
Density of H0 beam 2-3 1011 atoms /cm3
Charge Exchange
Surface ionization of cesium on a hot porous
Tungsten button , 30KeV 15 mA Cs+
Neutralized by cesium vapor (pulse)
6-10 particle mA,30 cm long
Charge exchange ionization
H↑ +Cs0 -> H- ↑+ Cs+
H- ↑ , 25 uA, 75% polarization,
emittance 0.065 pi cm mrad
500 𝜇s
J. Alessi , etal, “ A 25 uA Pulsed Polarized H- ion source, 6th internation Symp. On high energy Spin Physics, France, 9/12-19, 1984

## Slide 23
The source has been upgraded several times and continuously improves polarization, intensity and emittance.
Prior to Run-12, the ECR-type source was used to generate the primary proton beam.
In 2012, the ECR-source was replaced by a high-brightness OPPIS source FABS-type (Fast Atomic Beam Source).
Unlike the ECR-type source, the FABS-type source operates in pulsed mode and is located outside the SCS magnet.
In 2022, the length LEBT was reduced by about 5feet, and modified part of OPPIS (FABS, Rb-cell and Na-cell) and the extractor-transformer system.
This new source has enabled improvements in beam parameters such as current density, emittance, and stability.
The OPPIS polarized proton source for RHIC.
The OPPIS technique for polarized H− ion beam production was developed in the early 1980s at KEK (Japan), INR(Russia), LAMPF (USA), and TRIUMF (Canada).This particular OPPIS has a long development history. In the 1980s, it was first developed at KEK. In the 1990s, it was transferred to TRIUMF for further upgrades for RHIC in collaboration with INR. In 2000, it was brought to BNL
G. Atoian, A. Cannavo, T. Lehn, V. Lodestro, A. Kponou, D. Raparia, J. Ritter, B. Snyder, A. Zelenski
OPPIS evolution
RHICfest: Raparia 260710

## Slide 24: OPPIS in 2012
81-85% polarization @200 MeV , 0.5 mA
RHICfest: Raparia 260710
Anatoli Zelenski 2006 Veksler Award from the Russian Academy of Sciences
Anatoli Zelenski won the Brightness Award in 2019 for his development of the high-current, optically pumped polarized H− ion source (OPPIS).
Anatoli Zelenski Science and Technology Award in 2004.

## Slide 25: OPPIS Layout
D. Raparia, CAD Seminar 24/09/13
95%
60%
70%
8%
OPPIS: Six steps: (1) Atomic beam, FABS, (2) Ionization of atomic beam, He-Cell, (3) Rb-electron polarization, Rb-Cell, (4) Rb-electron transfer to H, Rb-cell (5) nuclear polarization, Sona Transition and (6) ionization, Na cell
RHICfest: Raparia 260710

## Slide 26
Rb
H+
H0
Proton
source
Laser-795 nm
Optical pumping
Rb: NL(Rb) ~1014 cm-2
Sona
transition
Ionizer
cell
H-
Laser beam is a primary source of angular momentum:
10 W (795 nm) 4•1019 h/sec 2 A, H0 equivalent intensity.
Superconducting solenoid 2.5T
1.5 kG field
Charge-exchange collisions: ~1014 cm2
Na-jet ionizer cell:
NL(Na)~ 3•1015 cm-2
Electron to proton polarization transfer
Н+ He cell
Rb+
Spin-Exchange polarization in P-Rb Collisions
RHICfest: Raparia 260710

## Slide 27
Optically Polarized proton source (OPPIS)
Laser room
Pumping laser
Prob laser
SCS
Plasmatron
Acceleration
4-grids
(5-7) keV
Neutralization H-cell
Ionization He-cell
Deceleration 3-grids ~3-4keV
Neutralization Ru-cell
Ionization Na-cell
Solenoid
Extractor 35kV
LEBT
Magnet
23.70
Spin rotator
Switching Magnet (50 ms)
MEBT
Sona transition
Correction coil system
RFQ
To LINAC
SCS Magnet 23.70 Spin rotator
Spin transfer: longitudinal transverse(horizontal) vertical
RHICfest: Raparia 260710
G. Atoian, A. Cannavo, T. Lehn, V. Lodestro, A. Kponou, D. Raparia, J. Ritter, B. Snyder, A. Zelenski

## Slide 28
OPPIS
LINAC
Booster
AGS
RHIC
2.5∙1011 p/bunch, P ~65%
9∙1011(maximum 40∙1011) polarized H- /pulse.
7.6∙1011 polarized H- /pulse at 200 MeV, P=80-82%
2.75∙1011 protons /pulse at 2.3 GeV
410 𝞵 A X 350 𝞵 s
Scraping in Booster
Polarized beams in RHIC
~2∙2 1011 p/bunch, P~60-65% at 100GeV
P ~ 50% at 250 GeV
410 𝞵A X 350 𝞵 s
Notes: 28

## Slide 29
Beam performance at 2012-2026
AGS Pol Study 2025
Run-2026
RHICfest: Raparia 260710
G. Atoian, A. Cannavo, T. Lehn, V. Lodestro, A. Kponou, D. Raparia, J. Ritter, B. Snyder, A. Zelenski

## Slide 30
Comparative Summary
Parameter | Tandem | OPPIS | EBIS
Mission | Heavy ions | Polarized protons | Heavy ions
First RHIC use | 2000 | 2001 | 2012
Technology | Electrostatic | Optical pumping | Electron beam ion source
Major legacy | First RHIC beams | First polarized collider | Multi-species collider
RHICfest: Raparia 260710

## Slide 31: Polarized He-3

## Slide 32: Polarized 3He++ Source development
U. S. Department of Energy
Office of Science | Nuclear Physics FY 2018
Research and Development for Next Generation Nuclear Physics Accelerator Facilities
… A doubly polarized electron-ion collider (EIC) is the best way to examine the internal structure of the proton and neutron. The technology to accelerate polarized proton beams has been well established at RHIC. However, studying the structure of the neutron requires the acceleration of polarized 3He++, which carries ~90% of its polarization in the neutron, and to match the unprecedented statistical precision an EIC will provide, it is indispensable to have high precision measurements of the hadron beam polarization. For this reason, development of a polarized 3He ion beam has been identified as an R&D priority by the EIC Advisory Committee in 2009 and the Office of Nuclear Physics Community Review in 2017.
In 2003 A. Zelenski, J. Alessi proposed a production polarized 3He++ beam in EBIS.
(A. Zelenski, J. Alessi, “Proposal of production of polarized 3He++ beam in EBIS” , ICFA Beam Dynamics Newsletter 30, p.39, (2003)
Polarized 3He++ source is a part of the ongoing EBIS upgrade project.
The development of the polarized 3He ion source is being done as a collaboration between BNL and Massachusetts Institute of Technology (MIT).
J. Alessi, G. Atoian, E. Beebe, C, Ianzano, S. Ikeda, S. Kondrashev, J. Maxwell, M. Musgrave, R. Milner, M. Okamura, A. Poblaguev, D. Raparia, J. Ritter, A. Sukhanov, N. B. Wuerfel, A. Zelenski,
RHICfest: Raparia 260710

## Slide 33: The 3He++ Source at BNL
Requirement
Intensity ~ 5∙1011 3He++ ions in 40 us pulse ~5.0 mA-peak
Maximum polarization > 70%
Compatibility with the operational EBIS for heavy ion physics.
Spin flip for every source pulse in the beam transport line.
Polarized 3He++ production
3He polarization by optical pumping and metastability-exchange technique inside the EBIS in high (5.0T) magnetic field. No polarization losses in 3He+ state.
EBIS is used for efficient ionization and accumulation of polarized 3He++ ions to the full capacity of about (2.5-5.0)∙1011 , 3He++ ions.
RHICfest: Raparia 260710

## Slide 34
3He-cell inside the EBIS SC Solenoid-1
Procedure to polarize the 3He gas at high magnetic field:
Prepare the 3He gas for polarization by the purification system; Valve1-open/ Valve2-close
Polarize the 3He gas inside the glass-cell by a MEOP technique; Valve1-close/ Valve2-close
Continually control the polarization of the injected 3He gas by using the Optical Probe polarimeter;
Inject a polarized 3He portions into drift tube (beam line) through the pulsed valve ( ~2-3*1012 atoms/pulse); Valve1-close/ Valve2-open
Ionize the polarized atoms of 3He by electron beam (~10 A).
3He-cell
3He Filling Valve1
3He Injection pulse Valve2
HV isolator
Drift tube (20-40 kV)
e-beam ~10A
To the purification system
Rf –discharge

## Slide 35: Innovations
Modified Cryo-pump for 3He
purification and storage
The pump also absorbs quite a significant amount of 3He gas (of about 100 scc).
The absorbed gas is released by the pump vessel heating ~20K.
Fast Pulsing Gas Valve
Lorentz (Laplace) force moves the flexible conducting plate in the high (~ 3-5 T) magnetic field.
For I=10 A, L=5 cm, F=2.5 N. Current pulse duration ~100-500 us
RHICfest: Raparia 260710

## Slide 36
Polarization Measurements by the Probe Laser Absorption
Closed cell
Open cell
89% polarization in. sealed
3He cell at 3 Torr pressure
Polarization build-up time .
0-4 min: Valve open
5-27 min: valve closed
29 min: laser off and valve opened
(3 Torr valve closed)
RHICfest: Raparia 260710

## Slide 37: Current setup in the Test Lab
We achieved higher (65%)
RHICfest: Raparia 260710
Open cell
Closed cell

## Slide 38: 3He++ Spin-Rotator in the at 6.0 MeV Beam Energy
After acceleration by EBIS LINAC, the polarized 3He++ beam will have an energy of 6MeV with a longitudinal spin direction.
The longitudinal polarization of beam is at first rotated to transverse direction using the 21.5 deg bending magnet (Dipole-1) and after
The Spin- solenoid will change the spin direction to the vertical . It is a pulsed solenoid with reversible field to enable spin-flip on an EBIS pulse-by-pulse basis.
Vertically polarized beam will return to the straight HEBT line by the system of dipole magnets.
Chicane has been commissioned with He-4 with about 90% transmission
The polarimeter will be install in the straight section after the Dipole-3 magnet. measurement of polarization with a standard configuration of left/right symmetric Si-strip detectors).
1
2
3
4
RHICfest: Raparia 260710

## Slide 39: Conclusions & Outlook
25 Years of RHIC Ion Sources
Heavy-ion injector evolution
Tandem Van de Graaffs successfully launched the RHIC heavy-ion program (2000–2011).
EBIS replaced the Tandems in 2012, providing greater flexibility, reliability, and support for all RHIC and NSRL ion species.
Extended EBIS (EEBIS) represents the second generation of the RHIC heavy-ion injector, with increased trap capacity, internal gas injection, and improved infrastructure for future operation.
Polarized proton program
OPPIS enabled RHIC to become the world’s first polarized proton collider.
Continuous upgrades over more than two decades established the world’s highest-intensity polarized H⁻ source.
Legacy
RHIC successfully accelerated virtually every ion species from protons to uranium.
The combined Tandem, OPPIS, and EBIS programs enabled 25 years of world-leading nuclear and spin physics.
RHICfest: Raparia 260710

## Slide 40: Looking Forward
Electron-Ion Collider (EIC)
Development and commissioning of the polarized ³He²⁺ source based on the Extended EBIS are underway.
The high-field optical-pumping polarization cell will be installed inside the upstream 5 T solenoid following completion of RHIC operations, enabling production of polarized ³He beams for the EIC.
EEBIS will remain the primary heavy-ion injector for NSRL while serving as the platform for the future polarized ³He program.
From the Tandem era, through EBIS, to the future polarized ³He source for the EIC, Brookhaven ion sources have continuously evolved to meet the scientific needs of each new generation of nuclear physics.
RHICfest: Raparia 260710

## Slide 41: Backup slides

## Slide 42
RHIC Species Timeline
2000 Au
2001 Au + p↑
2003 d+Au
2005 Cu+Cu
2012 U+U, Cu+Au
2014 3He+Au
2015 p+Au, p+Al
2018 Ru+Ru, Zr+Zr
2025 Final RHIC operations

## Slide 43
Single Event Upset
NASA Space Radiation Lab
Relativistic Heavy Ion Collider
Brookhaven Linac Isotope Producer
Magnetron (Linac)
OPPIS (Linac)
Cs sputter (Tandem)
EBIS (Heavy Ion Linac)
H-
H-
Au, Fe, etc.
H to U,
All sources can serve all users simultaneously
D. Raparia, CAD Seminar 24/09/13
#H- 2.5e15/s
#H- 1e12/s
#ion 1e10/s
#Charge 5e11/s
Laser Ion sources for the new application

## Slide 44: EBIS commissioning timeline
Date | Milestone
June 19, 2010 | First beam accelerated through the RFQ/Linac.
June 24, 2010 | Beam transported around the bend after the Linac.
June 29, 2010 | First beam from EBIS transported to the Booster (He⁺). The slide explicitly states “He¹⁺ – first beam from EBIS transported to Booster (June 29).”
June 30 – July 2, 2010 | Helium beam circulated in the Booster during commissioning.
July 2, 2010 | First beam from EBIS circulating in the Booster. The slide explicitly states “First beam from EBIS circulating in the Booster (7/2/10)!”
August 17, 2010 | Au³²⁺ transported to the middle of the bend at CD-4 intensity.
August 29, 2010 | Fe²⁰⁺ transported to the middle of the bend at CD-4 intensity.
RHICfest: Raparia 260710

## Slide 45: Extended EBIS
Long Trap
Short Trap
Gas Trap

## Slide 46
RHIC Discoveries Enabled by Its Ion Sources
Ion Source | Species Delivered | Physics Enabled | 
Tandem (2000–2011) | Au, Cu, d | Heavy-ion collisions | 
OPPIS (2001–2025) | Polarized p | Spin physics | 
Tandem + EBIS | d, p, ³He, Al, Au,Ru | Small-system collisions | 
EBIS (2012–2025) | U, Zr, ³He, Au, Al | Precision heavy-ion program | 
From the first QGP discovery to proton spin measurements and small-system collectivity, RHIC’s scientific achievements were enabled by the evolution of its ion sources: Tandem → OPPIS → EBIS.
RHICfest: Raparia 260710

## Slide 47: EBIS inside the high voltage cage

## Slide 48
EBIS during installation
11 Racks of power supplies for EBIS, all pulsing to 100 kV along with the EBIS, during ion extraction.

## Slide 49: EBIS Status

## Slide 50
Principle of EBIS Operation
Radial trapping of ions by the space charge of the electron beam.
Axial trapping by applied electrostatic potentials at ends of trap.
The total charge of ions extracted per pulse is ~ (0.5 – 0.8) x ( number electrons in the trap ~1.0∙1012 )
Ion output per pulse is proportional to the trap length and electron current.
Ion charge state increases with increasing confinement time.
Output current pulse is independent of species or charge state!
10A, 10-20 keV
D. Raparia, CAD Seminar 24/09/13
Notes: 50

## Slide 51
Circular polarized
Laser light at 1083 nm
D. Raparia, CAD Seminar 24/09/13

## Slide 52: Optical Pumping and Probe Lasers Layout
Pumping laser
Probe laser, Toptica, DL-100, diode laser
Detector
laser-Keopsys 10 W 1083 nm- fiber laser
D. Raparia, CAD Seminar 24/09/13