## Slide 1: Radio Frequency Systems
RHICfest
July 10, 2026
Freddy Severino & Kevin Mernick on behalf of the RF Group over the years

## Slide 2: Outline
The Early Years
  Identifying and Fixing Problems
Pushing the Intensity
  A Constant Struggle Effort
A Well-Oiled Machine
  Digital LLRF
  New Cavities
  Efficient, Flexible, High-Intensity Operation
  This talk could probably also be titled
  “A Bunch of Good Ideas that Mike Brennan Had”

## Slide 3: Early LLRF Experience
Initial system was largely a digitally-controlled analog system with many modules
Phase data scrambled to DSP and other glitches
Ring-to-ring synchro complications
No closed loop amplitude/phase control on cavities
Noise in RF drive

## Slide 4: Early HLRF Experience
Direct RF feedback around cavities
Upgrades to tetrode PAs
Debugging and upgrades to driver amplifiers
Experience dealing with operational issues
  Multipacting
  Vacuum bursts
  Tuners
  …

## Slide 5: Early Cavity Experience
Major issue encountered early in RHIC operation was with storage (197 MHz) cavity windows
Rebuild of accelerating (28 MHz) cavity tuners due to wear from constant motion from thermal cycles
Beam loading of 197 MHz cavities before/during rebucketing
  Nick Laloudakis and Mike Myers working on 28 MHz tuner.
  This is a later rebuild. Like many things, there were multiple iterations.

## Slide 6: Early Cavity Experience
  This is the closest thing I could find to a picture of Alex working
  Cracked ceramic

## Slide 7: Rebucketing
Mike Brennan, RHIC Retreat 2003
  The 4 common storage cavities were also removed and relocated (2 each) to the blue and yellow rings due to the heavy beam loading around 2009 - 2010

## Slide 8: Injector Merges
Mike Brennan, RHIC Retreat 2000
Single bunch transfer ameliorates residual emittance growth induced by the frequency mismatch that necessarily exists with multi-bunch transfers using a stripping foil.
Bunches are frequency matched to AGS RF, but their incoming spacing (phase) remembers the Booster frequency. --Kevin Smith, RHIC Retreat 2012

## Slide 9: Injector Merges (2)
Mike Brennan, RHIC Retreat 2006
  Merges would become routinely configurable after Booster and AGS LLRF upgrades ~2013
  Things I’m still learning from Mike:
“Bricolage.” Merriam-Webster.com Dictionary, Merriam-Webster, https://www.merriam-webster.com/dictionary/bricolage. Accessed 8 Jul. 2026.

## Slide 10: L10 Cavity
Kevin Smith, RHIC Retreat 2009
  Richard Spitz

## Slide 11: 9 MHz Cavities
As intensity and number of bunches increased, needed proton bunches to be long on the ramp to prevent e-cloud
Initially accomplished by mismatch of injected beam in 28 MHz, but this irreversibly blew up the longitudinal emittance
9 MHz cavities allowed long bunches with low longitudinal emittance, which could then be rebucketed to provide short bunches for collision
Proposed in 2006, tested in 2009, operational in 2011+
Mike Brennan, “Shorter Proton Bunches,” RHIC Retreat 2006
Mike Brennan, “9 MHz Cavity for Protons,” RHIC Retreat 2007

## Slide 12: 9 MHz Cavities (2)
2009 common cavity only
2011 common & bouncers
2012-13+ upgrade & stable operation
Replacement with dedicated blue/yellow 9 MHz cavities for BES-II / LEReC era (and later)
Common 9 MHz cavity
Burned up spring fingers, 2011
9 MHz bouncer cavity

## Slide 13: Digital LLRF Upgrade
Kevin Smith, RHIC Retreat 2013
Kevin Smith, LLRF Workshop 2011

## Slide 14: Digital LLRF Upgrade (2)
Tighter integration enabled new applications, significantly reduced hardware, sped up development

## Slide 15
C-AD Complex LLRF Installation
LEReC
CeC
RF
LEReC LLRF
CeC-PoP LLRF
BBB Long. Damper
RHIC LLRF
BBB Trans. Damper
AGS LLRF
Booster LLRF
Systems Linked via Update Link
EBIS LLRF
H- Linac LLRF
SRF Test Facility LLRF
Standalone Systems
LLRF Lab
17+1
26+3
13+1
13+1
5+1
6+1
2
~4
  ~100 installed systems

## Slide 16: Bunch-by-bunch damper
Distributed system made possible by LLRF upgrade (pickup @ 4:00, kicker @ 2:00)
Kevin Mernick, RHIC Retreat 2013
Kevin Smith, LLRF Workshop 2013

## Slide 17: 28 MHz Ferrite Tuners
Reduced wear from thermal cycles
Provided fast tuner response at transition and rebucketing
Operational from Run15 on
Mike Brennan, RHIC Retreat 2005
Sal Polizzo, Richard Spitz

## Slide 18: Other Developments
Landau cavities
  First used one of the 197 MHz storage systems (h = 2520)
  Then ~2004 an unmodified CERN 200 MHz system (h = 2563)
  Then ~2012 a dedicated 201.5 MHz system (h = 2580)
  Various enhancements to fight beam loading and support higher intensity
56 MHz SRF cavity
CeCPoP experiment support
Beam Energy Scan 2 and LEReC
  6 new RHIC 9 MHz cavities
  5 (later 6) RF cavities for LEReC e- accelerator
  Support and diagnostics for various LEReC
    subsystems (laser timing, energy diagnostics,
    energy feedback, etc.)
And many more

## Slide 19: RF Group Through the Years
R. Anderson
T. Artusa
D. Baudier
D. Bianco
O. Biletskyi
M. Blaskiewicz
M. Brennan
J. Brodowski
C. Brutus
J. Butler
A. Campbell
F. Carlino
K. Chen
R. Connolly
Z. Conway
J. DeLong
S. Deonarine
R. DiFranco
H. Dorr
N. Duong
S. Ellard
J. Errante
S. Farooq
K. Figueroa
W. Fischer
J. Fite
J. Genco
B. Gingrich
D. Goldberg
J. Greco
J. Guercio
H. Hahn
T. Hammil
P. Harvey
T. Hayes
F. Heistermann
K. Hernandez
M. Hoffmann Wallner
D. Holmes
A. Hubert
J. Joseph
T. Juarez
J. Keane
R. Kellermann
B. Kellwick
C. Klassert
P. Koello
P. Kolb
R. Kuruca
S. Kwiatowski
N. Laloudakis
T. Le
W. Legaz
D. Livoti
V. LoDestro
M. McCooey
K. Mernick
P. Moore
M. Myers
S. Naase
G. Narayan
G. Nembhard
J. Neto
C. Neyland
E. Onillon
T. Orobello
B. Palacios
R. Perez
S. Polizzo
C. Ramirez Lockward
A. Ratti
M. Rivera
K. Rogers
J. Rose
S. Seberg
T. Seda
F. Severino
K. Smith
M. Sowinski
R. Spitz
S. Valentino
K. Vetter
M. Witte
Q. Wu
B. Xiao
T. Xin
C. Xu
W. Xu
S. Yuan
A. Zaltsman
S. Zheng
C-AD from 1999 – present
C-AD/EIC from 1999 - present
plus a few mechanical “friends”

## Slide 20
John Butler,
2013 Open B Volleyball Champion,
Super Tech
M. Myers
M. Brennan,
M. Blaskiewicz,
K. Mernick
K. Smith, P. Paul,
A. Campbell, E. Onillon, J. DeLong, M. Brennan
F. Severino,
K. Smith
K. Smith, Z. Conway

## Slide 21
J. DeLong, J. Byrd (LBNL/ANL), K. Smith, A. Ratti
F. Severino, T. Hayes, S. Verdu Andres, Q. Wu, K. Smith
M. Sowinski
W. Xu
W. Fischer
W. Legaz
T. Orobello
S. Farooq
R. Connolly
R. Anderson
R. Kuruca
V. LoDestro
M. McCooey
J. Neto
J. Guercio
J. Jobin
J. Genco
B. Palacios
H. Dorr
D. Bianco
D. Baudier
D. Livoti
C. Neyland
B. Kellerman
T. Artusa
F. Carlino
R. DiFranco
D. Goldberg
K. Hernandez
P. Harvey
P. Moore
S. Yuan
S. Deonarine
T. Xin
C. Ramirez Lockward
B. Xiao

## Slide 22
S. Seberg, 2011 Brookhaven Award
A. Zaltsman, 2009 Engineering Award
K. Smith, 2012 Engineering Award
T. Hayes, 2012 Engineering Award
F. Severino, 2016 Engineering Award
F. Severino, 2009 Luminary Award
M. Blaskiewicz, 2007 S&T Award
2010 APS Fellow
J. Rose (NSLS-II), 2015 Engineering Award

## Slide 23
K. Mernick, 2018 Engineering Award
S. Polizzo, 2018 Engineering Award
G. Narayan, 2025 Engineering Award
N. Laloudakis, 2025 Outstanding Technician Award

## Slide 24
A Tour of the RHIC RF