## Slide 1
Date July 10, 3:25pm

## Slide 2: RHIC CRYOGENICS Roberto THAN Acknowledgement page
Date July 10, 3:25pm
RHIC CRYOGENICS DESIGN: Dan BROWN, Jim RANK, Chou LAC, Jack SONDERICKER, Dean CAMPBELL, Jim OSTERLUND, Austin GWILT, Willam DEVITO, K.C. WU, Jim BENSON, Alonzo WERNER Sr., Mike HARRISON, plus many others not mentioned. Those that stayed on for operations are named in operations.
RHIC CRYOGENICS OPERATIONS
Russel FEDER, Roberto THAN, Joseph TUOZZOLO, Andy MCNERNEY, Michael IAROCCI
Dewey LEDERLE, Anthony NICOLETTI
Eric O’CONNER, Andrew WEISMANN, Chintan SHETH, Pratik PATEL, Ashish SHUKLA, Kenneth HWANG, Ed QUIMBY, Ahmed SIDI-YEKHLEF, Lin JIA, L. WANG, Y.FARAH, Gregory CITVER,
Bernard YATAURO, Andreas WARKENTIEN, R. PICINICH
Nicholas STIVALA, Nicholas SCOTT, Jovanny ALAMO, Josiah GRUBBS, Kenneth RIKER, Thomas WOZNIAK, Jeffery STEWART, Louis TENREIRO, Gary POLONSKI, Daniel MARTIN,
Mark SARDZINSKI, Matthew DIETRICH, Alonso WERNER, George MEADE, Frank CULLEN, Glen ANDERSON, Mark MCNEIL, Willem DEJONG, Chris SALAT, C. WHITE, John STEHLE, James BIANCAROSA, D. MILLDANTRI, S. SAKRY, E. VARRICHIO, G. HERBST, R. OVERTON, William MCKEON
Thomas TALLERICO, Ann REUTER
Patrick TALTY, Brian VAN KUIK, Adam ZARCONE, Yi ZHANG, Dieter ZANTOPP, R. PRIEST
Leonard MASI, W. KOLLMER
Nils DANIELSON, David NACE II, Ryan WEISS, James CURLEY, John MOORE, Ron MEIER, David DERRYBERRY, Warren HIRZEL,C. Dudley, Will THEMANN, L. MAZARAKIS, M. O’DONNELL, K. SAWICKI
Thanks to all who have served the RHIC Cryogenics group over the years! July 10, 2026.

## Slide 3: CENTRAL PLANT IMPROVEMENTS HELIUM (Story of) COLLIDER PROJECTS

## Slide 4: IMPROVEMENTS & PROJECTS
CENTRAL PLANT IMPROVEMENTS
Helium Use
10:00: E-LENS SC SOLENOIDS {@4.5K}
56MHZ STORAGE CAVITY {@4.3K} 4:00
CEC 2:00 {112MHz@4.4K} + {704MHz@2.0K}
LEReC 2:00
SPHENIX 8:00
912 PLANT & LVTF Vertical Test Facility  39” Dewar for 56MHz
912 ERL
Notes: Will go over the central plant improvements done over the years.
I thought it would be interesting to helium production and cost.
Recap some designs implemented for the cryo systems for the experiments.

## Slide 5: CENTRAL PLANT IMPROVEMENTS
Rao Ganni (Jlab)
Gas Management & Plant Control
Controls: CRISP SCADA (VaxVMS)HMI to Modern SCADA:Indusoft(Aveva)
Stop using Mechanical Bearing Cold Compressor 4.3K to 4.6K
  Repiping because of no cold compressor operation
Stop using Liquid helium circulator pumps on the Magnet lines
  New control logic to “forced” flow through magnets without circulating pumps
Add MLI to coldbox 5 liquid helium vessels
Cold End Upgrade (Expander turbine 7 +HXs) to match RHIC Loads
Corrector flow control  3 sizes of orifices to Needle valves
Reduce LN2 use from 11 to 5 trucks /week for magnet rings 80K mode cooling during shutdown
Add bulk liquid helium truck offload line into coldbox #5 midpot
Flow balancing HX: HP inlet valves

## Slide 6: POWER CONSUMPTION TIMELINE
6.4MW
E-lens: 2011-2012
56MHz:2012-2014
CEC: 2012-2015
LEREC: 2015-2017
sPHENIX:2015-2023

## Slide 7
COLD END
Expander T7 &HXS
DeActivate
Cold Compressor
4.25K  4.65K

## Slide 8: Forced Flow Supercritical Helium
Liquid Helium Pumps

## Slide 9
STOP USE OF LIQUID HELIUM CIRCULATOR

## Slide 11: HELIUM SOURCING Federal Helium Reserves Helium Stewardship Act of 2013

## Slide 12: HELIUM EXTRACTION IN USA
CLIFFSIDE STORAGE
CRUDE
HELIUM
PIPELINE

## Slide 13
Federal Helium Reserves @ Cliffside Field

## Slide 14
HELIUM
FOR SALE
2013
EST.1996
Helium Stewardship Act

## Slide 16: HELIUM PRODUCTION & PRICE
 | 2005 x Million Sm3 | 2010 x Million Sm3 | 2020 x Million Sm3 | 2025 x Million Sm3
Helium from Natural Gas | 84 | 75 | 76 | 74
Withdraw from storage | 50 | 53 | 7 | N/A
Helium Sales | 134 | 128 | 83 | 81
Imports | - | - | 7 | 8
Exports | 49 | 77 | 50 | 38
Consumption, Apparent | 85 | 51 | 40 | 51
Federal User Crude He price | $5.45/Liq.Gal | $6.47/Liq.Gal | $10/Liq.Gal | No more
Federal user purchase price | $10.8/Liq.Gal | $16/Liq.Gal | $32/Liq.Gal | $69.5/Liq Gal.
USA DOMESTIC NEW HELIUM OPERATION 2025 | STATE
2 {LittleWater, WestPecos} | New Mexico
1 {Las Animas} | Colorado
1 {Fort Dodge} | Kansas
1 {KevinDome} | Montana

## Slide 17: WORLD HELIUM PRODUCTION
[x Million Sm3] | 2024 | 2025
USA | 80 | 81 + New
QATAR | 11 | 11
RUSSIA | 17 | 18
ALGERIA | 11 | 11
CANADA | 3 | 3 [1 new coming]
POLAND | 3 | 3
CHINA | 3 | 3
SOUTH AFRICA |  | New (0.5)  5
AUSTRALIA | 4 (2021) 1 (2023) | 2025 (Darwin field depleted)

## Slide 18: Projects around Collider Circle

## Slide 19: 4:00: 56MHz QWR CAVITY {@4.4K}
Large: Folded QWR
Low design pressure!  5 PSIG RELIEF!
Requirements: ± 1Hz.  5Hz?
STIFF CAVITY, except the “tuning plate”
Bath cooled @ 4.4K
MICROPHONICS
Isolation using a condenser / boiler

## Slide 20: 4:00: 56MHz QWR CAVITY {@4.4K}
Vapor inlet
Liquid outlet
Condenser fully submerged in Liquid Helium

## Slide 21: 10:00: E-LENS SC SOLENOIDS {@4.5K}
Bath cooled @ 4.4K
5 Tesla
Blue solenoid had a bad layer: bypassed.
Added inside diameter annular gap channel for cooling.

## Slide 22: CEC
112MHz
4.4K: Isolate from rest of cryo system using Condenser/Boiler
{Same as 56MHz}
Cold Cathode
Power coupler: Coaxial
Water Blowdown system to get water out if cooling water fails
704MHz 5-Cell: 2.0K
112MHz
704MHz

## Slide 23: 704MHz @ 2K

## Slide 24: LEREC: 2K 704MHz ½-Cell
704MHz ½-Cell

## Slide 25: sPHENIX

## Slide 26: sPHENIX

## Slide 27: HIGH CURRENT TEST

## Slide 28: The End