## Slide 1: Projections for Run-18 and BES-II Wolfram Fischer
8 August 2017
RHIC Retreat, BNL
Notes: 09:20, 20 min (incl. questions), 15 slides

## Slide 2: Contents
Performance in Run-17 p+p 255 GeV, RHICf Au+Au 27.2 GeV/nucleon CeC and LEReC commissioning
Projections for Run-18 and Run-19/20 Run-18 (Zr+Zr, Ru+Ru, Au+Au 100 GeV/nucleon) Run-19/20 (Au+Au 3.85 – 9.8 GeV/nucleon) → Beam Energy Scan II (BES-II); most of BES-I in Run-10
Ongoing and planned upgrades RHIC 9 MHz RF, LEReC, Extended EBIS Linac (vacuum, Intensity Upgrade Phase II)

## Slide 3: Run-17 p+p at 255 GeV ∫Ldt and P
Run Coordinator: Vahid Ranjbar
STAR Lmax limited to ≈ 1.4x1032 cm-2s-1 => 1st p+p run with L-leveling Lavg = 0.83 Lmax with b*-squeeze 2.0→1.5 m after 3 h (Lavg = 0.90 Lmax planned)
ramp-up faster than planned
slope as planned
Run-13: Pavg = 53%
Run-17: Pavg = 55% (H-jet average over intensity, time, stores, Blue and Yellow)
Special run for RHICf:
5 stores with b* = 8.0 m

## Slide 4: Run-17 p+p at 255 GeV Notable items
all DX magnets moved back to symmetric position
only one experiment STAR (PHENIX being converted to sPHENIX)
STAR experimental beam pipe changed (from 4 cm ID Be NEG coated to 8 cm ID Be without coating; adjacent Al pieces are NEG coated on both cases); PHENIX experimental beam pipe changed (from 4 cm ID Be to 12.2 cm ID SS, both NEG coated)
1 of 3 new 9 MHz cavities installed in each ring and made operational (60 kV/cavity design, operated at 26 kV/cavity)
new ion optical system increases OPPIS beam by 20% (03/01/2017)
lens cryo upgrade - both superconducting solenoids run stably at 6 T
use of dual harmonic acceleration in AGS to reduce space charge near injection
MPS upgrade with additional permit inputs: RF, orbit correctors, 10 Hz orbit feedback, fast BPM readings (coherence signal); also lowered BLM thresholds at store
only transversely polarized beams at IP6 (no rotators)
8 h nominal store length
many Yellow quenches after 4 of 5 new mechanical serial switches failed to close after beam dump (03/13/2017); as a result yi7-d6 shows small bypass current in a quench protection diodes - reduced ramp rate by factor of 2 to reduce the bypass current
β* squeeze from 1.5 to 1.2 m nominally 3 h into the store (beginning 03/13/2017)
special Yellow Au ramp for CeC PoP (γ = 29.229); 90 h or dedicated CeC PoP time
beam from LEReC DC gun to gun line beam dump

## Slide 5: Run-17 Au+Au at 27.2 GeV/nucleon ∫Ldt
Run Coordinator: Greg Marr
slope as planned
Operation concurrent with CeC commissioning
used 197 MHz RF,
no stochastic cooling (only 18 d of physics – too short)
bunch intensity limit from Landau cavities at transition resolved => presentation by Darryl Goldberg

## Slide 6: Operational efficiency availability reported to DOE
Availability = beam time / scheduled beam time (denominator excludes scheduled maintenance)
Availability goal: 80%
Typical times:
50K to 4K cool-down : 0.5 weeks
Initial set-up : 2 weeks
Changing species : 0.5 weeks
Beam studies (APEX): 16h / 2 weeks
Maintenance : 14h / 2 weeks
Warm-up : 0.5 weeks
=> Met availability goal now 6 years in a row

## Slide 7: Operational efficiency setup time
TRANSPARENT: low energy
INTRANSPARENT: high energy
BLUE: heavy ion runs
RED: polarized proton runs
Setup time: - for 1st species in run: from both rings cold to 1st physics store - for following species: from beginning of setup to 1st physics store
Run-17
12 days for p+p
≤ 3.8 days for Au+Au

## Slide 8: Operational efficiency store-to-store, time in store
BLUE: heavy ion runs
RED: polarized proton runs
TRANSPARENT: low energy
INTRANSPARENT: high energy
Time in store = store time / calendar time Goal: 60% (denominator includes scheduled maintenance, failure, setup, beam experiments)
Run-17

## Slide 9: RHIC – all running modes to date 2001 to 2017
nominal injection energy
2019/20 BES-II with LEReC
2017
2018
2017
2000

## Slide 10: Outlook RHIC Run-18 and Run-19/20
PAC recommendations (STAR only while PHENIX => sPHENIX):
Run-18
Zr+Zr 100 GeV/nucleon 3.5 wks
Ru+Ru 100 GeV/nucleon 3.5 wks
Au+Au 13.6 GeV/nucleon 3.0 wks
Au+Au 3.85 GeV/nucleon 2 days (fixed target)
LEReC and CeC commissioning
STAR Spokespeson Zhangbu Xu, 05/09/2017:
“STAR is interested in looking into the luminosities at BES energies for isobars: Zr and Ru.

## Slide 12: Run-18 Zr+Zr, Ru+Ru, Au+Au
Important issues in Run-18:
Sources for Zr-96 and Ru-96 => presentation by Deepak Raparia
Stochastic cooling => essential, intensity low compared to Au
Fast setup and reliable operation => only a few weeks in all modes
MPS upgrades => minimize downtime due to commissioning
LEReC and CeC commissioning in parallel
Run Coordinator: Greg Marr

## Slide 13: Run-18 Ru-96 and Zr-96
Why Ru-96 and Zr-96? Same number of nucleons => same Quark-Gluon-Plasma system Different number of charges => different magnetic field
Zr-96
natural abundance: 2.78%
From LION/EBIS (sintered ZrO2) => M. Okamura et al.
Enriched ZrO2 commercially available, processing using RIKEN technology
Ru-96
natural abundance: 5.52%
From Tandem (metallic) => P. Thieberger et al.
Provided by DOE using new isotope separation facility at ORNL
More details by Deepak
ZrO2 tablet made at RIKEN
Ru-96 metal flakes from DOE inventory

## Slide 14: Run-18: 96Zr + 96Zr, 96Ru + 96Ru Luminosity estimates
Based on 2016 and 2017 tests at EBIS and Tandem, and note by C. Gardner (08/03/2017)
2x the L that fills the STAR bandwidth

## Slide 15
COOLING
in Blue RHIC ring
COOLING
in Yellow RHIC ring
64 m to IP2
Beam Dump
20° Bending Magnets
DC e- Gun
704 SRF
Booster Cavity
2.1 GHz Cu Cavity
9 MHz Cu Cavity
704 MHz Cu Cavity
Commissioning
Diagnostic Line 1
Commissioning
Diagnostic Line 2
RHIC TRIPLET
RHIC DX
180° Bending Magnet
e-
e-
LEReC Solenoids
Compensating (LF)
Matching (HF)
Merger/Transport
e-
Low Energy RHIC electron Cooling (LEReC)
(not to scale)
Energies E : 1.6, 2.0 MeV Avg. current Iavg : 27 mA Momentum dp/p : 5×10-4
Luminosity gain : 4×
A. Fedotov
1st bunched beam electron cooler planned operation in 2019/2020

## Slide 16: BES-II 2019/2020 BES-I and BES-II luminosities
4x increase in Lavg with e-cooling
3x increase in Lavg without e-cooling

## Slide 17: LEReC Physics integration BES-II required events
General strategy to maximize integrated luminosity:
Cooling at the 3(2) lowest energies (4x gain in Lavg), no cooling at the 2(3) highest energies (3x gain in Lavg) => demonstrated at √sNN = 19.6 GeV in Run-16
Increase cryo-time from 22 to 24 weeks/year
Start BES-II at highest energies (machine ready w/o cooling)
Interleave cooling commissioning with physics operation
Finish BES-II at lowest energies (largest gain in Lavg and time)
RHIC Beam Energy Scan II (BES-II) for search of critical point in QCD phase diagram
center-of-mass energy √sNN | GeV | 7.7 | 9.1 | 11.5 | 14.6 | 19.6
events BES-I, actual | M | 4.3 |  | 11.7 | 24 | 36
events BES-II, min goal | M | 80 | 100 | 150 | 200 | 300
events BES-II, full goal | M | 100 | 160 | 230 | 300 | 400
Notes: STAR vertex acceptance: +- 1m
STAR contacts: Zhangbu Xu (spokesperson), Bill Christie, Paul Soerensen, Daniel Cebra

## Slide 18: RHIC Upgrades Overview
Low-Energy RHIC electron Cooling (LEReC) Details in presentation by Alexei Fedotov
RHIC 9 MHz RF Upgrade 1/3 cavities per ring in Run-17 (60 kV/cavity) 2/3 in Run-18, 3/3 in Run-19
Extended EBIS 2nd superconducting solenoid completion for Run-19/20
Linac Upgrades Vacuum upgrade Intensity Phase II: 2x pulse length (for BLIP, applied for funding) => received funding for PS prototypes
trap length extension

## Slide 19: RHIC hadron complex infrastructure 25+ years
Need to update list of upgrades to maintain RHIC hadron complex for 25+ years (last time done for all areas in 2011 for 10+ years)
What systems? When? How much?
Basic assumptions for estimate (reality will differ):
RHIC operation with A+A, p+A, p+p until 2024
eRHIC construction for 3 years, followed by 15 years of operation
Only the Yellow RHIC ring and 2 Blue arcs are maintained operationally for eRHIC (also have a rough estimate for both rings maintained)
RHIC modifications for eRHIC excluded

## Slide 20: Summary
Run-17 met L and P goals for p+p 255 GeV first p run with leveled L (b* squeeze) quench protection diode damage again met L goals for Au+Au 27.2 GeV/nucleon Maintained high operational efficiency reduced p+p 255 GeV setup time again (2013: 21 d → 2017: 12 d) 86% availability (goal: 80%), 62% of calendar time in store for all p+p 255 GeV, 68% for Au+Au 27.2 GeV/nucleon
Preparation for next runs Run-18: Zr+Zr, Ru+Ru 100 GeV/nucleon, Au+Au 13.5 GeV/nucleon LEReC beam commissioning, CeC commissining Run-19/20: Beam Energy Scan II (5 energies, 2 lowest with LEReC)
Ongoing and planned upgrades RHIC 9 MHz RF, LEReC, Extended EBIS, Linac (vacuum, Intensity Phase II)
Pavg = 55%

## Slide 22: RHIC ultimate luminosity and polarization goals
parameter | unit | achieved |  | goals | 
Au-Au operation |  | 2016 |  | ≥ 2021 56 MHz SRF + AGS + 9 MHz RF | 
energy | GeV/nucleon | 100 |  | 100 | 
no colliding bunches | … | 111 |  | 111 | 
bunch intensity | 109 | 2.0 (1.6) |  | 2.5 (2.0) | 
avg. luminosity | 1026 cm-2s-1 | 87 |  | 175 2× achieved | 
p-p operation |  | 2015 |  | ≥ 2021 OPPIS + 9 MHz RF + e-lenses | 
energy | GeV | 100 | 255 | 100 | 255
no colliding bunches | … | – 111 – |  | – 111 – | 
bunch intensity | 1011 | 2.25 | 1.85 | 3.0 | 3.0
avg. luminosity | 1030 cm-2s-1 | 63 | 160 | 175 2.8× achieved | 600 3.8× achieved
avg. polarization* | % | 55 | 52 | 60 | 55
*Intensity and time-averaged polarization as measured by the H-jet. Luminosity-averaged polarizations, relevant in single-spin colliding beam experiments, are higher.

## Slide 23: RHIC 9 MHz RF Upgrade
Scope
3 cavities per ring (60 kV per cavity) [existing 9 MHz RF: 22 kV (p+p)]
3 areas of benefit:
Larger bucket and ramp speed for protons (avoids squeeze out on early part of ramp, faster crossing of spin resonances)
Lower peak current for transition crossing (increase in bunch intensity)
Operation with long bunches at low energy ions (enhancement to LEReC)
Cost and funding
Schedule
started: 08/2013
planned completion: 12/2018 (begin of beam commissioning)
Status
installation of 1 cavity per ring for Run-17,
Installation of 2 cavities per ring for Run-18, and 3 per ring for Run-19
FY2014 | 2015 | 2016 | Total
$675k (A) | 700k (A) | 625k (A) | 2.0M
A. Zaltsman, S. Polizzo
Notes: Mar-2015: install first article in RHIC ring
Nov-1016: complete installation in RHIC
Oct-2017: start commissioning with beam

## Slide 24: STAR luminosity request
Dependence of useful event rate R(t) on instantaneous luminosity L(t):
R(L(t)) = if (L < 22x1026 cm-2s-1) { L(t) * 4.3x10-24 cm2 * 0.16 }
else { 1500 Hz }
General RHIC setup strategy:
(Long) stores with L(t) > 22x1026 cm-2s-1 throughout the store => STAR bandwidth always filled
Initial luminosity Linit = 3x22x1026 cm-2s-1 = 66x1026 cm-2s-1 => stochastic cooling ensures L(t) > 22x1026 cm-2s-1
Initial bunch intensity Nb ≥ 1.3x109 for both 96Zr and 96Ru => can be done with enriched 96Zr and 96Ru
96Zr natural abundance 2.81% => 50% enriched 96Zr available, ops from EBIS
96Ru natural abundance 5.54% => DOE working on finding/producing enriched 96Ru 10% abundance sufficient in target material, ops from Tandem

## Slide 25: Run-18: 96Zr + 96Zr, 96Ru + 96Ru – at lower energies
Zhangbu Xu, 05/09/2017:
“STAR is interested in looking into the luminosities at BES energies for isobars: Zr and Ru. At: 39, 27, 19.6 and 14.6”
Response, 06/15/2017:
We should not run lower than sqrt(sNN) = 39 GeV. At this energy stochastic cooling still works.
If we don’t have stochastic cooling, the source consumption goes up significantly, which is particularly problematic for Ru-96.
Using the same bunch intensity as we project for sqrt(sNN) = 200 GeV the luminosity would drop by a factor ~20 going from 200 GeV to 39 GeV.