## Slide 1: Cluster update

## Slide 2: What’s new
Current (Old):
  Pixel pitch is 1/5 physical size.
  GEANT -> Reco algorithm is just taking pixel center + random time smearing.
Why change: Want to return to realistic pixel pitch
Proposed (New):
  Pixel pitch is the physical size.
  GEANT -> Reco algorithm is GEANT->Charge sharing->Clustering->Reco
Compare efficiency and resolution of the “new” cluster algorithm

## Slide 3: Efficiency
Old algorithm discard hits if edep < threshold.
  Default threshold = 6 keV
Before: Narrow pixel, old algorithm. After: wide pixel, new clustering
Threshold = 3keV
Threshold = 6keV
Threshold = 12keV
Threshold = 18keV
Total number of clusters in all events

## Slide 4: Efficiency
Old algorithm discard hits if edep < threshold.
  Default threshold = 6 keV
Before: Narrow pixel, old algorithm. After: wide pixel, new clustering
Threshold = 3keV
Threshold = 6keV
Threshold = 12keV
Threshold = 18keV
Total number of clusters in all events
Why do we get less clusters in the new algorithm?

## Slide 5: Efficiency (cont.)
Cluster lost due to overlapping clusters being merged into 1.
New result if sigmax=sigmay= 0 (no charge sharing)
Total number of clusters in all events
Threshold = 3keV
Threshold = 6keV
Threshold = 12keV
Threshold = 18keV

## Slide 6: Conclusion
Resolution of new algorithm (with realistic pixel width) = that of old algorithm (but with wrong pixel width)
Source of efficiency lost is NOT understood.
Propose that we replace the old clustering algorithm with the new one.

## Slide 7: Update 4/11/2026

## Slide 8: Reason for missing clusters: Cell segmentation with wrong offset
When I increase the pixel size to be the sensor size (i.e. each sensor has only one pixel), offset were incorrect.
Hits are located at the corner, which confuses neighbor finder.

## Slide 9: No cluster lost after fixing offset
One sensor only has one pixel.
Thresholds are applied BEFORE charge sharing.
Threshold = 30keV
Threshold = 60keV
Threshold = 120keV
Threshold = 180keV
MC particle gun:
  1 < theta < 2
  2pi azimuth uniform
  0.1 < |p| < 1 GeV/c
  Pi+ only
Reco thresholds:
  Before charge sharing = (see plot)
  After charge sharing = 0 (no threshold)
  Not threshold applied before charge sharing ONLY to verify if there are bugs in the program, NOT to realistically simulate detector response
Total number of clusters in all events

## Slide 10: Cluster performance after correction
Phi resolution is too good.
Ave. NO pixel per hit = 3.25
Charge sharing still too wide?
Total number of clusters in all events
MC particle gun:
  1 < theta < 2
  2pi azimuth uniform
  0.1 < |p| < 1 GeV/c
  Pi+ only
Reco thresholds:
  Before charge sharing = (leftmost: see plots. Right 2 figures: 60keV)
  After charge sharing = 6keV (all 3 plots)
Charge sharing:
  Sigmax = 0.5 mm = pixel pitch
  Sigmay = 0.5 cm = 0.5*pixel width
Threshold = 30keV
Threshold = 60keV
Threshold = 120keV
Threshold = 180keV

## Slide 11: Cluster performance after correction
Sigmax is varied to match expectation
MC particle gun:
  1 < theta < 2
  2pi azimuth uniform
  0.1 < |p| < 1 GeV/c
  Pi+ only
Reco thresholds:
  Before charge sharing = 0keV (no threshold)
  After charge sharing = 6keV
Charge sharing:
  Sigmax = 0.25 mm = 0.5*pixel pitch
  Sigmay = 0.5 cm = 0.5*pixel width
Threshold = 30keV
Threshold = 60keV
Threshold = 120keV
Threshold = 180keV
Total number of clusters in all events

## Slide 12: Conclusion
Proposed:
  Fix pixel offset.
  Revert pixel size to realistic size (0.5mm * 1 cm)
  Enable clusters with sigmax = 0.4 mm
  Upload them in a pull request.
To be done:
  Same analysis on ETOF.