## Slide 1: AC-LGAD Study in Japan
Satoshi Yano
Hiroshima University & RIKEN
AC-LGAD meeting
2026/05/01

## Slide 2: Positioning Resolution of BTOF Sensor
The first test of BTOF sensor (real full-size strip sensor) at DESY shows nice positioning resolution of σ < 20 um (3 sensors x 2cols each = 6 areas)
A long-standing question for BTOF sensor: “How much positioning accuracy is required?”
  Sensor#0 - col0
  Sensor#0 – col1
  Sensor#1 - col0
  Sensor#1 – col1
  Sensor#2 - col0
  Sensor#2 – col1

## Slide 3: Signal Delay (Charge Sharing Time)
We observed large signal propagation time, a few μm/ps at middle of strips
  This includes not only sensor but also readout board delay
This means ”Hit position determination on sensor surface is crucial for timing measurement”
Leading Strip
Sub-leading Strip

## Slide 4: Assembly Site Preparation
Many equipment have been installed in Hiroshima University and RIKEN
Clean room at Hiroshima University will be ready in May

## Slide 5
Extra

## Slide 6: Setup for Strip-Type AC-LGAD
DIGITIZER
TLU
DIGITIZER
COINCIDENCE
TRIGGER
TRIGGER
EUDRBs
Telescope DAQ PC
DUT DAQ PC
~4 mm
Wire-Bonded Area
20 mm
32 mm
MIMOSA Area Tracker
~11 mm
Scintillator
AC-LGAD
AC-LGAD
AC-LGAD
Scintillator
Scintillator
BUSY
Used fully independent DAQ is used
Synchronized them by NIM Modules

## Slide 7
MIMOSA26
DUT
TRIGGER1
Beam
MIMOSA26
TRIGGER2＆3

## Slide 8: Readout Strategy
2 configuration modes are used for focusing on hit position resolution and timing resolution measurements, respectively
  Timing resolution mode (pattern-1): use three sensors with 10 (5+5) channels each
  Positioning resolution mode (pattern-2): use two sensors with 15 (7+8) channels each readout
  (Rough) Timing reference: Trigger raw signal into each digitizer
Beam penetrates one digitizer
↓
Remove jitter between two digitizers
Digitizer0
Digitizer1
Digitizer0
Digitizer1
One sensor readout by one digitizer
↓
Remove mis-calibration between two digitizer
5 rows
5 rows
7 rows
8 rows
Pattern-1
Timing Measurement
Pattern-2
Positioning Measurement

## Slide 9: Clustering
Exclude event with the leading strip on edge
  Hit beam outside of the acceptance
  Timing calibration is not enough for timing resolution measurement
    Trigger signal is used as timing reference
Timing Window
Cut for leading strip
After leading strip cut
Noise
Pedestal Peak

## Slide 10: Simple Hit Position Reconstruction
Weighted (Σwx/Σw) and Squared-weighted (Σw2x/Σw2) method has been performed
Top-2 amplitude (leading and sub-leading) strips are used
Weighted
Squared-Weighted
  Sensor#0 - col0
  Sensor#0 – col1
  Sensor#1 - col0
  Sensor#1 – col1
  Sensor#2 - col0
  Sensor#2 – col1
  Sensor#0 - col0
  Sensor#0 – col1
  Sensor#1 - col0
  Sensor#1 – col1
  Sensor#2 - col0
  Sensor#2 – col1
The charge distribution is not linear with respect to the distance to the strip!!!!

## Slide 11: Track-Based η Correction
Charge share is not linear → Simple-weighting method doesn’t work
Eta v.s. utrack (leading and sub-leading strips)
  η = Qright / (Qleft + Qright)
  utrack = (ytrack - yright) / strip-pitch
Qleft
Qright
ytrack
yleft
yright
Strip Pitch
  Sensor#0 - col0
  Sensor#0 – col1
  Sensor#1 - col0
  Sensor#1 – col1
  Sensor#2 - col0
  Sensor#2 – col1
Sensor0
Sensor1
Sensor2

## Slide 12: Reconstructed Hit Position
  Sensor#0 - col0
  Sensor#0 – col1
  Sensor#1 - col0
  Sensor#1 – col1
  Sensor#2 - col0
  Sensor#2 – col1

## Slide 13: Hit Positioning Resolution
Residual (Track position – ACLGAD position) as a function of global position has been calculated
  Track-Based η correction has been applied
Positioning resolution (including tracking resolution) achieves <20 um
  Resolution of Sensor0 > Sensor1 > Sensor2 due to multiple scattering in the front DUTs
  Sensor#0 - col0
  Sensor#0 – col1
  Sensor#1 - col0
  Sensor#1 – col1
  Sensor#2 - col0
  Sensor#2 – col1

## Slide 14: Signal Arrival Time Delay Inter Strips
Signal delay is observed in row direction
  Between Leading and Sub-leading is ~0.5 ns delay
TOAleading
TOAsub-leading
ytrack
yleading
ysub-leading
TOAleading - TOAsub-leading [ns]
Ytrack [mm]
  Sensor#0 - col0
  Sensor#0 – col1
  Sensor#1 - col0
  Sensor#1 – col1
  Sensor#2 - col0
  Sensor#2 – col1