## Slide 1
ePIC SRO WG Meeting
Agenda:
  Intro (Me)
  SVT Calibrations (Jo Schambach)
Notes / Information:
  Meeting Notes: ePIC Streaming Computing WG Meetings - Google Docs

## Slide 2: Intro to ITS2 Calibration Details
Jo presented a superset of this information in March at E&DAQ Meeting (https://indico.bnl.gov/event/31841)
The ITS2 calibrations give a really good idea of the types of calibrations detectors need at the detector level
  Often only known to detector groups themselves
  Often require super-specialized run modes
  Often do not use anything remotely like the physics analysis chain to analyse
  Often produce specialized data / data formats
  Often done infrequently or only once or twice as part of commissioning the detector
  Other detectors will have similar detailed calibrations / scans
Streaming DAQ will have some particular issues:
  Trigger DAQ can usually disable pedestal subtraction, zero-suppression, tail suppression and read out empty events at a low rate. In ePIC, ITS2 is dependent on low pixel occupancy. Even in an artificial triggered mode it can’t read out all 15 Billion pixels at once.
  Scans of individual un-zero-suppressed sensor behavior must be done by disabling sections of the chips in order to readout only certain sections at a time or by adding artificial deadtime
  Some scans may take a very long time
    May need creative applications. Eg. Continous calibration of small portion of the detector?

## Slide 3: Intro to ITS2 Calibration Details (continued…)
When operations begin, detector groups likely to ask for
  Access to raw data from a series of runs with specific characteristics
  Resources to run specialized programs on this data
  Access to all software tools available during analysis, but not the constraints of running the standard reconstruction software…
  Changes to procedures, or at least incorporation of new ideas arising out of the problems / success’s of the initial data
    We shouldn’t be surprised 
Things to think about regarding the calibration tasks:
  What tools do we provide to make these tasks easier
  What tools do we provide to make these tasks transparent to the collaboration
  What tools do we provide to make use of the results of these calibrations
  Are all of these calibrations part of SRO calibration infrastruction?
    To make it successful we need to make the SRO calibration infrastructure easier to use than having detector groups do it themselves
      Simple Data Access
      Simple programming tools for incorporating stand-alone codes
      Simple access to hardware / “batch tools”  or in our case to streaming/orchestration tools