## Slide 1: TOF
Satoshi YANO
Hiroshima University & RIKEN

## Slide 2: Impact on the ePIC PID Performance
The BTOF PID focuses on low-momentum particles at mid-rapidity
Continuous PID coverage requires seamless operation in conjunction with other PID detectors, avoiding PID gaps
  Minimum timing required for the sensor to eliminate the PID gap is ~95 ps
A stretch goal of sensor ~40 ps would provide substantial overlap (Δp ≈ 0.5 GeV/c) for robust cross-calibration
  To achieve the stretch goal, < 30 μm positioning resolution is desired
hpDIRC
BTOF
dRICH
FTOF
HRPPD
pfRICH
Decay products from D-meson in ep DIS @ √s = 141 GeV
Charge #1
σelec = 20ps
σT0 = 25ps
hpDIRC limit
hpDIRC limit
Overlap disappear
point
Overlap
~ 0.5 GeV/c
~95 ps
Overlap
~ 0.5 GeV/c

## Slide 3: Required Positioning Resolution
Nonnegligible signal propagation time has been observed
Propagation speed is approximately 0.8 μm/ps
<30 μm positioning resolution is required to reach 30~40 ps timing resolution
Charge #3
Charge #1
Strip#1
Strip#2
Δt1
Δt2
Hit time t0
Ts1 = thit + Δt1
Ts2 = thit + Δt2
Nonnegligible propagation time

## Slide 4: Position v.s. ΔTRL (=TR - TL)
TR(u)= t0 + (d0 + u)/veff + aR
TL(u)= t0 + (d0 - u) /veff + aL
ΔT(u)=TR(u)- TL(u) = 2u/veff + (aR - aL)
d{ΔT(u)}/du = 2/veff
veff = 2{dΔT(u)/du}
SR
d0
d0+u
Hit time t0
SL
d0-u
u
Example: DUT1 COL1

## Slide 5: Propagation Time Correction

## Slide 6: Positioning Resolution
Positioning resolution achieves σ ~ 10 μm
Sensor: S0
Sensor: S1
Sensor: S2
Charge #3

## Slide 7: Position Reconstruction
Weighted method (ampw), squared weighted method (sqw) and tracked-base eta correction (etac) method are compared
Bending residual can be seen in ”raw” of ampw and sqw reconstructed position
However, this can be corrected by simple method
ampw method
sqw method
etac method

## Slide 8: Positioning Resolution
”Resolution” point of view, ampw and sqw are better than eta-correction
Which resolution—ampw or sqw—is better depends on the distance from the strip
The best positioning resolution is ampw and sqw combined results
Eta = QL/(QL+QR) is a key tool to switch ampw and sqw

## Slide 9: Positioning Resolution v.s. Eta