## Slide 1: LUME VA/DT Tutorial
Ryan Roussel
rroussel@slac.stanford.edu

## Slide 2: Nomenclature
Virtual accelerator
Users
Digital twin
Applications
Live machine readings / archived states
Various interfaces (EPICS, python, etc.)
Various interfaces (EPICS, python, etc.)
EPICS

## Slide 3: Applications of Virtual Accelerators / Digital Twins
Virtual diagnostics (VA / DT)
Online control (DT)
Model calibration (VA / DT)
Accelerator design / operating routines (VA)
Controls software testing / continuous integration (VA / DT)
Operator / algorithm training (VA / DT)

## Slide 4: Current State of Affairs
Beam dynamics codes
Analytical calculations
Surrogate models
“Simulators”
Python wrappers
LUME-Impact,
PyTao, ad-hoc
LUME-Torch
IOC serving (i.e. EPICS)
PCASpy
Implementation barriers (custom/ad hoc implementations per use case)
IOC read/write

## Slide 5: Implementation Goals
Create a standardized Python API / toolset for arbitrary simulators w/ multiple entry points
Simulator
Simulator
LUME-Model
Simulator 2
Simulator 1
Simulator 3
Simulator
Simulator
LUME-pva
Simulator API
(LUME-Impact, PyTao)
Standardized LUME-Model API
(dicts, IOC names / units)
IOC Interface
(EPICS)

## Slide 6: LUMEModel Structure
LUME-Base
LUMEModel
set
Set control variables by name and run the sim/model, then update the model’s state
get
Read back model state by variable name
reset
Restore model to initial state
any simulator can implement these methods
supported_variables
Dictionary of named variables that the model supports

## Slide 7: LUMEModel Structure
LUME-Base
LUMEModel
set
Set control variables by name and run the sim/model, then update the model’s state
get
Read back model state by variable name
reset
Restore model to initial state
any simulator can implement these methods
supported_variables
Dictionary of named variables that the model supports
Variables define types, units, read/write permissions for model inputs and outputs + validate inputs / outputs
ScalarVariable: float-like scalar variables (individual parameters, etc)
NDVariable: array-like multi-dimensional variables (screens, wire scans, etc)
ParticleGroupVariable: openpmd-beamphysics ParticleGroup variables
TorchScalarVariable: torch version of ScalarVariable
TorchNDVariable: torch version of NDVariable

## Slide 8: Example Interactions via Python API
Once a LUMEModel instance is defined, users interact with it via set(), get() methods in control/model name parlance and/or object properties
Initialize model
Set model parameters via PV name/units
Get model parameters via PV name/units
Get model parameters provided by simulation

## Slide 9: Example Interactions via Python API
Once a LUMEModel instance is defined, users interact with it via set(), get() methods in control/model name parlance and/or object properties
Interact with underlying simulator + PV
Interact with underlying simulator
Get beam distribution
(openPMD-beamphysics ParticleGroup)

## Slide 10: LUME Package Structure for Simulation Codes
LUME-pva
Simulator agnostic
Facility agnostic
Facility specific
EPICS PV serving
LUME-Cheetah
LumeCheetahModel(LumeModel)
LUME-Genesis
LumeGenesisModel(LumeModel)
LCLSCuHxrModel(StagedModel)
CUInjector
CULinac
HXRUndulator
LUME-Bmad
LumeBmadModel(LumeModel)
LUME-Torch
LumeTorchModel(LumeModel)
(under development)
LUME-Impact
LumeImpactModel(LumeModel)
LUME-Base
LUMEModel
StagedModel(LUMEModel)

## Slide 11: LUME Actions
LUME Actions enhances LUME variables with set() and get() methods that act on simulators
Good place for facility specific conversion logic
Stack actions to build large-scale virtual accelerators inside LUMEActionModel subclass

## Slide 12: Example Implementation: LCLS CU HXR (Bmad)
PyTao initialization + lattice slicing

## Slide 13: Example Implementation: LCLS CU HXR (Bmad)
Generate action variables based on lattice

## Slide 14: Example Implementation: LCLS CU HXR (Bmad)
Create LUMEModel instance

## Slide 15: Example Implementation: Staged Model
LCLSCuHxrModel(StagedModel)
PyTorch
PyTao
LUMETorchModel
LUMEBmadModel
Set PV in injector NN surrogate
ParticleGroupVariable
Read screen PV in linac Bmad sim

## Slide 16: Example: Running in EPICS w/ LUME-pva
Subclasses of LUME-Model can immediately be used to create an EPICS PV server by using the LUME-pva Runner class
Utilizes LUME-Variable types to create PVs
Multi-threaded collection of PV commands and simulation running
Could be subclassed / extended to other IOC systems (DOOCS, etc.)

## Slide 17: Virtual Accelerator / Digital Twin Interactions
Machine snapshot
Virtual accelerator in python
Virtual accelerator in container
Python instance
User
Python
User
EPICS
Container instance
Digital twin in container
User
EPICS
Container instance
Machine snapshot
Digital twin in global server
Machine snapshot
Machine snapshot
Visualization

## Slide 18: Badger Environment Testing / Continuous Integration
Use VA to perform nightly testing / validation of code used to interact with the machine
Badger GUI
LCLS Badger Environment class
EPICS
LCLS Virtual Accelerator
EPICS
Nightly testing workflow
Class instance
not available for software testing
LCLS Machine
Testing report

## Slide 19: VA for Model Calibration / Phase Space Meas.
Black-box (Impact / Bmad) and differentiable simulators (Cheetah, surrogates) can be used inside VAs to perform model calibration, phase space reconstruction
Ex: LCLS-II DIAG0 beamline
Machine state
Predicted meas.
Experimental measurements
Loss function
Simulator
Simulator
LUME-Model
Update internal simulator
Improved VA
Reconstructed beam distribution
Post-optimization

## Slide 20: Digital Twin Live Deployment
Slide from Sara M.
https://ard-modeling-service.slac.stanford.edu/live-monitor/w3/

## Slide 21: Interactive VA Mode from Live State
Slide from Sara M.

## Slide 22: Online applications of VA/DT
Badger training tool:
https://ard-modeling-service.slac.stanford.edu/badger/
Live accelerator VA/DT
https://ard-modeling-service.slac.stanford.edu/live-monitor/

## Slide 23: Conclusion
LUMEModel, and subclasses provides a standardized, extendable way to run virtual accelerators with realistic IOC names / units
Modular approach allows both interactions via python API and with LUME-pva, IOC serving (necessary for satisfying multiple use-cases)

## Slide 24: Tutorial Link
https://colab.research.google.com/drive/1H-yOSBj3mmbEOqK7-zSloEFnINVEDjfl?usp=sharing

## Slide 25: Backup

## Slide 26: A Note On PALS
Ultimately PALS will aim to handle a lot of this, future LUME-PALS may look like:
LUME-Base
LUMEModel
LUME-PALS
LUMEPalsModel(LUMEModel)
LUME-Pals allows for the selection of different simulator backends
LUME-Impact
LUME-Bmad
LUME-Cheetah

## Slide 27: LUME-Model Class
Defines fixed Python API for IOC (and other parameters)
get(list[str])
set(dict(str,Any))
reset()
supported_variables defines dict of IOC names that are supported by the model

## Slide 28: Basic LUME-Model Implementation
Agnostic to simulations / EPICS etc.  useful for software dev / testing, CI, etc.

## Slide 29: Considerations for Simulator-Specific LUME-Model Subclasses
Some observations
  Each code has a specific way for running, modifying, extracting data from simulations – LUME-Model subclasses serve as an abstraction layer to unify this
  Each facility has a different way of defining control names, units, custom behavior
Bmad
Impact
SLAC IOC
BNL IOC
Current: Each connection is unique
Bmad
Impact
SLAC IOC
BNL IOC
PALS
Where we are headed:
Each facility will map their unique infrastructure to PALS
LUME can provide abstraction logic to run / modify simulations based on PALS info
LUME-Bmad
LUME-Impact
Parallel Strategy: Implement facility-specific transformers with common patterns for each code, then transition to PALS-based transformers for each code type, LUME-Model subclasses remain the same
SLAC-mapping
BNL-mapping