## Slide 1: TWINAC: A Digital Twin Framework For PIP-II At FERMILAB
Abhishek Pathak, Tia Miceli, and Erik Gottschalk
September 2, 2026
4th EIC-BeamAI Collaboration Meeting

## Slide 2: Contents

## Slide 3: Abbreviations Used

## Slide 4: Terminology & Key Definitions
01

## Slide 5: A Virtual Accelerator
A virtual accelerator is a computer-based representation of an accelerator that combines beam-dynamics and equipment models with emulated control-system interfaces to reproduce machine behavior without affecting the real machine.
Reproduces beam and equipment responses
Presents realistic control-system interfaces
Supports studies, software testing, and operator training

## Slide 6: A Virtual Accelerator

## Slide 7: A Digital Twin
A digital twin is created when the virtual accelerator is continuously connected to and synchronized with the real accelerator.
Receive measurements, settings, and machine status.
Compare measured and predicted observables.
Estimate the current machine state.
Recalibrate and update the model via continuous learning.

## Slide 8: From Virtual Accelerator to Digital Twin

## Slide 9: Why Do We Need a Digital Twin?
02

## Slide 10: Why build a virtual accelerator?

## Slide 11: Proton Improvement Plan-II at Fermilab
03

## Slide 12: Proton Improvement Plan-II at Fermilab
PIP-II is an essential upgrade to Fermilab’s accelerator complex, enabling the world’s most intense neutrino beam for LBNF/DUNE and a broad physics research program for decades to come.
12
PIP-II Capabilities
Beam Power
Leading to 1.2 MW from MI
Upgradeable to multi-MW
PIP-II Scope
800 MeV SRF linac
Linac to Booster Transfer Line
Accelerator Complex Upgrade
SSR-1
10-32 MeV
325 MHz
SSR-2
475
32-177 MeV
325 MHz
HWR
112
2.1-10 MeV
162.5 MHz
HB-650
971
516-800 MeV
650 MHz
LB-650
65
177-516 MeV
650 MHz
BEAM
TRANSFER
LINE
BOOSTER
WARM FRONT END
Ion source → RFQ → MEBT

## Slide 13: PIP-II Lattice Optimization & Beam Dynamics
04

## Slide 14: Simulation-Tool Requirements

## Slide 15: HELIX at a Glance
3 engines
One lattice
Envelope, full 3-D PIC and exact backward tracking.
DC → 6-D
Beam regimes
Continuous beams, automatic bunching and generated 6-D inputs.
RFQ + maps
Fields and acceleration
RFQ plus 1-D, 2-D and 3-D field-map support.
Backtracking
Exact inverse
Reverse the machine, then validate by tracking forward.
Envelope
Linear space charge
Fast covariance transport, centroids and matching.
3-D PIC
Collective physics
Nonlinear space charge with deterministic kernels.
SCC + Monte Carlo
LEBT compensation
Statistical compensation and uncertainty studies.
Hofmann
Instability chart
Tune ratios, depression and resonance risk.
Multibunch
Beam loading + BBU
Chopped pulse trains, resonators and cumulative HOM wakes.
Element errors
Misalignment
Offsets and rotations of machine elements.
Beam errors
Input misalignment
Centroid, angle and 6-D mismatch.
H⁻ stripping
Distributed losses
Lorentz stripping, residual-gas stripping, and blackbody photodetachment.
Failures
Element response
Off, detuned and partially functioning devices.
Anomalies
Detection + analysis
Physics-based tests of unexpected behavior.
Scans
Parameter studies
Reproducible sweeps, tolerances and UQ.
Matching
Multiple strategies
Twiss, orbit, diagnostics and constrained objectives.
Surrogates
Replace costly models
Guarded learned models with traceable provenance.
CLI · API · GUI
Three interfaces
Script, integrate or interact with one physics core.
Multi-code
Lattice import
TraceWin plus MAD, NMAD and SCINMAD lattices.
Beam I/O
Distribution interop
Import external beams or generate DC and 6-D inputs.
53 tools
AI + MCP
Tiered actions, confirmations and deterministic replay.
3,917 tests
Validation
380 files, analytic pins and full-linac checks.
21 + 47
Elements + keywords
A broad lattice catalogue with strict parsing.
HDF5 + openPMD
Reproducible output
Results, configuration and provenance travel together.
Public ≠ dev
Explicit maturity
Public, opt-in, experimental and held features stay labeled.
https://github.com/Accel-Toolkit/HELIX

## Slide 16: PIP-II Digital Twin Architecture
05

## Slide 18: TWINAC at a Glance

## Slide 19: A Digital Walk-Through of the Lattice
06

## Slide 20: HELIX at a Glance
Survey-accurate 3D model of PIP-II: hover for element cards, jump to sections, fly the beamline.
Live beam overlay: envelope, orbit and losses from the DT updated every run, with the assistant's beacons.

## Slide 21: From Fly-Through to an Operations Display
The lattice viewer proves the concept. The next step is a general-purpose 3D operations display. Same beam, deeper machine model, built to live in the control room.
TODAY — THE LATTICE VIEWER
NEXT — THE OPERATIONS DISPLAY
Schematic lattice elements
Geometrically accurate model of the warm front end, including LEBT solenoids, RFQ, MEBT doublets and triplets, bunching cavities, choppers and diagnostics
Beam envelope computed by the simulation's optics model
Beam envelope and trajectory derived from control-system parameters, as physics-meaningful quantities
Color identifies element type
Color carries physics: instantaneous beam current and loss density
Interactive fly-through
Deterministic, scriptable views. Any view can be saved, replayed, and synchronized across a wall of screens.
Built for the PIP-II lattice
One display engine: other accelerators as well as detector geometry and data display
GPU-accelerated prototype (VisPy + PySide6) showing the Fermilab Booster lattice, built directly from its MAD-X description.
NEAR TERM
— Quantify visualization requirements
— Prototype the interface to the control system
— Evaluate the software stack: open-source options vs. commercial alternatives
Collaborative effort. If you're working on this too, come talk to us.
Notes: Companion to the previous slide. Abhishek's lattice viewer already exists — this slide is about what the joint effort adds on top of it.
Three points to land:
1. The middle layer. The visualizer consumes physics-meaningful quantities — phase advance, normalized rms emittance, matched Twiss, machine-state snapshots.
2. Geometric fidelity. Not schematic lattice elements but the as-built warm front end, so a loss pattern is a place on the machine rather than a row in a table.
3. Generality. The rendering engine (VisPy + PySide6, GPU depth testing, command-string control layer). The Booster image is the current prototype reading a MAD-X lattice.

## Slide 22: TWINAC COPILOT
07

## Slide 23: An Operations Copilot

## Slide 26: The Twin Tracks the Machine

## Slide 27
27

## Slide 28: Virtual Accelerator — Sign-In

## Slide 29: Virtual Accelerator — Overview

## Slide 30: Virtual Accelerator — Beam Phase Space

## Slide 31: Virtual Accelerator — Device Controls