## Slide 1: Polarized beams at the Hadron Injector Complex
Eiad Hamwi
EIC-BeamAI Collaboration Meeting

## Slide 2: Outline
The HIC
Polarized protons at the HIC
  Polarized protons at the RHIC
  Polarized protons in the Booster
  Polarized protons in the AGS
Polarized Helium-3 at the HIC
  Polarized Helium-3 in the Booster
  Polarized Helium-3 in the AGS
  Polarized Helium-3 development schedule
Current endeavors to support high polarization
Conclusion and outlook

## Slide 3: The Hadron Injector Complex
The Hadron injector complex will use the hadron injectors of the former RHIC complex.
The AGS began polarized proton transport more than 30 years ago.
The Booster upgrade came on in 1991 to serve as an injector for the AGS.
The Optically Pumped Polarized Ion source and the Electron Beam Ion source are the primary ion sources and pre-injectors for the Booster.
Tandem van de Graaff
HIC Injector Requirements | Injection rigidity (Tm) | Bunch intensity (1010) | (mm) | Polarization (%)
Protons | 79.3 | 32 | 2.5 | 72
Helium-3 | 55.3 | 13 | 2.0 | 72
HIC Injector Requirements | Injection rigidity (Tm) | Bunch intensity (1010) |  | Polarization (%)
Protons | 79.3 | 32 | 2.5 | 72
Helium-3 | 55.3 | 13 | 2.0 | 72

## Slide 4: Polarized Protons at the RHIC
by V. Schoefer
4
PHENIX
AGS
LINAC
BOOSTER
Pol. H- Source
200 MeV Polarimeter
Helical Partial
Siberian Snake
Spin Rotators
(longitudinal polarization)
2 Siberian Snakes/ring
Spin Rotators
(longitudinal polarization)
Strong AGS Snake
RHIC pC Polarimeters
Absolute Polarimeter (H jet)
STAR
AGS Polarimeter
Spin flipper
 | Max Energy [GeV] | Pol. At Max Energy [%] | 
Source +Linac | 0.2 | 82-84 | 
Booster | 2.5 | ~80-84 | 
AGS | 23.8 | 67-70 | p-Carbon
RHIC | 255 | 55-60 | Jet, full store avg*
 | Relative Ramp Polarization Loss (Run 17, full run avg)
AGS | 17 %
RHIC | 8 %
* Includes both ramp loss and store decay

## Slide 5: Polarized Protons in the Booster
by K. Hock

## Slide 6: Polarized Protons in the AGS
by V. Schoefer
Frequency of particle motion in the focusing magnets is (mostly) ENERGY INDEPENDENT
Precession frequency of spin motion is in general ENERGY DEPENDENT
If particle samples fields with a frequency equal to the spin precession frequency, depolarization can occur
“Snakes”, helical dipoles, help manipulate the spin motion with local rotations to avoid that condition (at the cost of complicated fields/optics distortion)
6
Injection
Extraction
Spin tune gap
Hor resonance crossings
Tune
jump
(pause tune jump near transition)

## Slide 7: Resonance compensation via coupling
≅ Gɣ = N +/- Qx
Depolarizing resonances from partial snakes and betatron coupling have the same frequencies
Every skew quadrupole represents a complex resonance driving term (calculated using SPRINT algorithm)
Place a collection of skew quadrupoles in the ring to cancel the partial snake driving term.
“Just” linear algebra
Spin resonance terms from skew quads in AGS
Gɣ = 43.72

## Slide 8: Partial snake resonance suppression with betatron coupling
BUT:
There are 82 such linear algebra problems to solve
AND:
Phasing between skew quadrupole terms and snake terms varies wildly resonance to resonance
AND:
Correction vectors are frequently parallel, especially near strong vertical intrinsic resonances
We have 15 skew quad ‘knobs’ to form independent corrections at each energy
Skew quad correction vectors (last six hor resonances)
Phase offset chosen so that snake drive term is purely real
Red circle marks the same skew quad in each frame, phase changes rapidly from resonance to resonance
In principle minimizing resonance strength (calculated with SPRINT) and coupling (two complex numbers) takes 4 skew quads

## Slide 9: Magnets and locations
A set of 15 skew quadrupoles with integrated skew quadrupole gradient at least 0.2 T meets the physics requirements
  9 placed at narrow locations in the AGS adjacent to sextupoles
  6 locations in longer (mostly empty) straight sections
  Locations determined largely by brute force optimization from the available ~30 locations
  Note: At top energy one AGS main magnet causes ~70° of spin precession
    Geographically close != close in phase
A10
F07
Tune kicker
Main magnet
Chrom sext
AGS ring
Skew quad locations
Magnet Param |  | unit
Length (mech.) | 0.17 | m
Bore diameter | 0.16 | m
Pole tip field (max) | 0.15 | T
Int grad (max) | 0.32 | T
Current (max) | 275 | A
Current (rms,max) | 60 | A
Lamination thick. | 0.635 | mm
4-Stranded coils
17 turns

## Slide 10: Calculated correction waveforms
Pulsing the skew quads with 1 ms rise, 1.3 ms flattop and 1 ms fall allows changing currents quickly to accommodate new correction vectors every resonance
  Also avoids having skew fields during strong vertical intrinsics (tracking showed small polarization losses at these with skew quads powered)
Calculated resonance strength reducible to zero at almost every resonance
  Tune shift from coupling < 0.005
10
1.3 ms
1.0 ms
Each trace= 1 skew quad
1.0 ms

## Slide 11: Ramp implementation and Polarization
Correcting only resonance above transition
Skew quad current
Early attempts:
  High energy pulses only (avoids difficult low energy optics)
  Omitting several pulses with too large orbit excursions
  Within statistical error of model in terms of gain factor over uncorrected polarization
Each trace= 1 skew quad

## Slide 12: Low energy resonance correction
Benefit from low energy pulses (GƔ < 15) expected to be ~3-4%
Measured benefit ~1%
In some cases negative, less reliable correction
Intentionally omit
Near transition
Correcting scaling, full cycle
Skew quad currents
Orb correction also enables broader scans
Each trace= 1 skew quad

## Slide 13: Skew quadrupole operation: ramp and polarization
Enabling more pulses via
  Incremental orbit improvements
  Fixing bug in resonance calculation for low energy resonances when Qy not in spin tune gap
  Included model-predicted orbit response of the skew quads in the optimization to minimize resulting vertical rms
    Resonance strength, |ε| = 0
    Tune shift from coupling, ΔQy< 0.005
    Vertical |Morm*(kskew*xskew)|max < 1 mm
Skew quad currents
13
Skew quads ON
Skew quads OFF
Polarization ratio
Skew Quads ON/OFF
Polarization comparison
Mysterious decline in base polarization
1.08-1.1 typical of jump quad performance

## Slide 14
Skew quadrupole operation: Current status
Resonance correction with skew quads has demonstrated higher polarization gain than jump quads
Up to 15%, relative to 8-10% from jump quads
But not reliably
Where is the rest?
KNOWN horizontal resonance issues
  ~1-2% in the gap around transition  surmountable modeling issue, no further discussion
  2% in the ‘low energy’ resonances  more difficult modeling issue, orbit problems
UNKNOWN horizontal resonance issues
  Unknown skew quadrupole fields  fixable with survey + TBT BPMs
    Main magnet roll
    Vertical closed orbit in sextupoles
  These create resonances exactly like the skew quads
    I.e. there are really three resonance vectors: a known snake term, a known applied skew quads term, an unknown skew quadrupole error term
    This unknown term would cause residual depolarization even in the case where the applied skew quad correction for the snake is perfect.
UKNOWN vertical resonance issues Needs exploratory model work to suggest further experiments
  Some experimental evidence suggests the vertical resonance situation is not totally addressed by the spin tune gap.

## Slide 15: Polarized Helium-3 at the HIC
Polarized He-3 will facilitate polarized neutron collisions for the Electron Ion Collider.
Polarized He-3 beams will be produced at the Electron Beam Ion Source (EBIS) with an expected intensity of 2.5 × 1011 ions/pulse and 85% polarization.
EBIS accelerates the beam to 2 MeV/u (|Gγ|=4.1932).
Booster accelerates up to |Gγ|=7.5 or 10.5 to match stable spin directions with AGS.
AGS accelerates up to |Gγ|=49.5, avoiding the strong |Gγ|=60−νy intrinsic resonances.
HSR will accelerate and store the beam up to |Gγ|=820.
This is significantly higher than polarized protons with Gγ=487 (RHIC, achieved) and Gγ=525 (HSR, planned).
The EIC requires He-3 with a store intensity of 0.8×1011 ions/bunch and 70% polarization.
by K. Hock

## Slide 16: Polarized Helium-3 in the Booster
by K. Hock

## Slide 17: Polarized Helium-3 in the Booster II
by K. Hock
Summary of corrector current needs for each imperfection resonance with total maximum currents needed to flip or correct the imperfection resonance ( and ). All resonances evaluated with h=4 and 5 corrected.
Froissart-Stora for imperfection resonance crossing for resonance at h=k with optimal currents ( and ) and given currents ( and ):

## Slide 18: Polarized Helium-3 in the AGS
by K. Hock

## Slide 19: Polarized Helium-3 HIC Development Schedule
by K. Hock
Polarized He-3 development in the Booster will follow the installation of the He-3 gas cell at EBIS and the Booster polarimeter installation.
Polarized He-3 development in the Booster will follow the AGS re-cabling and Readiness Reviews

## Slide 20: Polarized Beam HIC Development Schedule
by K. Hock
FY27
Complete survey of AGS.
Install Booster polarimeter.
Install He-3 gas cell in EBIS.
FY28
Commission Booster polarimeter with protons and polarized He-3
Begin commissioning of He-3 in Booster
FY29
He-3 in Booster commissioned
AGS cable tray replacement complete.
Begin commissioning polarized He-3 in AGS.
Continue skew quad studies in AGS.
FY30
He-3 commissioned in AGS.
Skew quads in AGS fully commissioned.
Make determination in FY30/31 of maximum achievable polarization transmission and determine if additional upgrades need to be implemented.

## Slide 21: Current endeavors to support polarization
Booster polarimeter design for measurements independent of the AGS.
  Measurement time for polarization error of dP/P~1%: protons ~50 ms, He-3 ~8 s.
AGS survey (paused since early June) expected to be done before the end of 2026 (~3 months of work remain).
AGS low energy modelling and skew quad analysis.
Simulation work to understand the vertical polarization profile in the AGS.
Design work on raising the maximum supported Booster to AGS transfer rigidity from 9.5 Tm to 12.7 Tm to support transfer of protons at and He-3 at
Simulations of space charge effects at AGS injection.
AGS snake upgrades.
TBT BPM upgrade for Booster and AGS.
Corrector upgrades for Booster and AGS.
by H. Huang

## Slide 22: Summary
Polarized proton development continues in the AGS, with the survey expected to be completed early FY27 and commissioning to resume in FY29.
Polarized He-3 development will begin after EBIS He-3 gas cell is installed and the Booster polarimeter is installed, both expected in late FY27 and commissioning expected to begin in FY28.
A campaign covering various studies is underway to better understand the current polarization loss and emittance growth.
To meet the EIC requirements, near lossless transmission of polarization must be achieved.