## Slide 1: sPHENIX Director’s Review
OUTER HCAL DETECTOR
ANATOLI GORDEEV
August 2-4, 2017
BNL

## Slide 2: sPHENIX OUTER HCAL Description
HCAL steel-
  HCAL ABSORBER STEEL
  MAGNET FLUX RETURN
  STRUCTURAL SUPPPORT FOR INNER DETECTORS AND MAGNET
Scintillating tiles with wavelength shifting fiber
SiPM Readout

## Slide 3: The Subsystem Technical Overview
32 MODULES
INNER RADIUS 1.9m
OUTER RADIUS 2.6m
10 GAPS of 7mm Scint Tiles
24 Tiles in each row.
~26.1mm - ~42.4mm
Tapered 1006 Steel Plates

## Slide 4: OUTER HCAL SECTOR- LOWER
SUPPORT ENDPLATE
LIFTING/ROTATING TRUNION
MAGNET STEAL
ABSORBER PLATE
MAGNET STEEL
HALF PLATE
SPLICE PLATE
SUPPORT RING
BRACKET LOCATION

## Slide 5: OUTER HCAL MODULE
SUPPORT COMB
6.3m LG
13.5 TONS
LIGHT TIGHT
COVERS/PROTECTOR
INSTALLED BEFORE INSTALLATION
COMPLETED MODULE
READY FOR INSTALLATION IN IR

## Slide 6: OUTER HCAL HANDLING FIXTURES
OUTER HCAL SECTOR
LIFTING FIXTURE
SECTOR ROTATION ATTACHMENT (WORM GEAR)
HOLDING FIXTURE (BASE STAND)
CLOSER VIEW OF LIFTING FIXTURE WITH ROTATION GEARS

## Slide 7: 1ST HCAL MODULE INSTALLATION
1ST MODULE SHIMMED/SURVEYED
AND KEYED IN PLACE
SHIM HERE
LIFTING/ROTATING TRUNION
PINNED TO
NEXT
MODULE
BOLTED TO
CRADLE
ONE SIDE
BOLTED TO
ENDPLATES
CRADLE CARRIAGE WELDMENT
OUTER HCAL SERVES AS THE
SUPPORT STRUCTURE FOR THE DETECTOR
AND MAGNET FLUX RETURN

## Slide 8: OUTER HCAL LOWER HALF INSTALLATION
ACCESS SCAFFOLDING

## Slide 9: SC MAGNET INSTALLATION
MAGNET IS SUPPORTED
BY THE OUTER HCAL

## Slide 10: OUTER HCAL SECTOR ANALASYS
TOTAL DEFORMATION
WITHOUT SUPPORT COMBS 4.6mm
TOTAL DEFORMATION
WITH 5 SUPPORT COMBS ON TOP
7 COMBS ON BOTTOM 2.5mm
SUPPORT COMB
WORST CASE SCENARIO – HORIZONTAL LIFT

## Slide 11: ~180 deg OUTER HCAL ASSEMBLED
120 DEGREE OR MORE
BOTTOM SUPPORT
WILL BE SUFFICIENT
TOTAL DEFORMATION IS 0.4mm MAX

## Slide 12: ASSEMBLE UPPER QUADRANT
MOMENT
BOLTED SECTOR CONNECTION –FRICTION CONNECTION.
TOP MODULE SECTION CAN ROTATE AND
MAKE ASSEMBLY IMPOSSIBLE
AFTER MAGNET IS INSTALLED
REMAINING SECTORS ARE INSTALLED

## Slide 13: ASSEMBLY DEFORMATION
FIXED SUPPORTS
8 MODULES
2.3mm DEFORMATION
DEFORMATION IS TOO GREAT
FOR INSTALLATION OF REMAINING
SECTORS WITHOUT ADDITIONAL TEMPORARY SUPPORT

## Slide 14: ASSEMBLY DEFORMATION
AN EXTERNAL SUPPORT IS REQUIRED
FOR REMAINING MODULES TO BE INSTALLED

## Slide 15: TEMPORARY SUPPORT FOR TOP SECTOR INSTALLATION
FRONT AND BACK SUPPORT COLUMNS
TOP AND BOTTOM
FRAME SUPPORTS
ONE POSSIBLE SOLUTION SHOWN. OTHER OPTIONS INCLUDE USING HYDRAULIC PISTONS BETWEEN SECTOR TRUNIONS TO ACHIEVE ADEQUATE SEPARATION FOR INSTALLATION

## Slide 16: COMPLETED ASSEMBLY ANALYSYS
X DEFORMATION +/- 0.6mm
Y DEFORMATION 1mm MAX
FINAL ASSEMBLY DEFORMATION IS WITHIN TOLERANCE AFTER
REMOVAL OF TEMPORARY SUPPORTS

## Slide 17: Status and Highlights
Analyses are continuing (near completion)
  Outer HCal to Cradle carriage
  Adding SC Magnet, Inner HCal and EMCAl support loads to model
  Splice Plate and Pin stresses
  Modified sectors (with cut out for SC Magnet Chimney extension)
Lifting fixture design (including rotation attachment) nearly complete
  Design to be submitted to BNL lifting safety committee this month
  Tile/electronics assembly stands detailed awaiting final approval for fabrication
Full scale prototype sector in production at vendor. Delivery this month.
  Validate and qualify lifting and handling fixtures/tools
  Evaluate tile holding features and alignment
  Evaluate cable management
  Partial instrumentation to validate operational characteristics with cosmic rays
  Evaluate light tightness design
  Test structural integrity in all installed orientations

## Slide 18: Summary
Design is maturing rapidly
Analyses indicate acceptable structural integrity
Full scale prototype sector (near final design) in production
Design drawing package nearly complete
Interfaces with Cradle Carriage and other detectors under development
Assembly area at BNL to be identified shortly (candidates identified, negotiating availability)
Cost and production schedules being validated with full scale prototype sector

## Slide 19: Back Up

## Slide 20
SPHENIX EXPLODED VIEW
SOUTH EMCAL
SOUTH ENDCAP
SOUTH SUPPORT RING
CRYOSTAT/SC COIL
OUTER HCAL
INNER HCAL
NORTH EMCAL
NORTH SUPPORT RING
COIL CHIMNEY
NORTH ENDCAP
(FLUX RETURN)
(FLUX RETURN)

## Slide 21
INNER HCAL ATTACHMENTS
L-BRACKET
LOAD TRANSFER
SUPPORT RING
(INNER HCAL TO
OUTER HCAL)
PLATE
INNER
HCAL END
RING
EMCAL
OUTER
HCAL
21

## Slide 22
COMPLETED HCAL INSTALLATION
22

## Slide 23
BNL, D. Lynch, R.Ruggiero, A. Gordeev
23
SUPPORT COLUMNS
HYDRAULIC JACKS
TOP MODULES
BOTTOM MODULES
TEMPORARY SUPPORT FOR
TOP MODULE INSTALLATION
FRAME SUPPORT
FRAME SUPPORT DEFORMATION IS ONLY 0.02mm
DEFORMATION DOES NOT EFFECT LOWER HCAL MODULES INTERNAL STRUCTURE

## Slide 24
BNL, D. Lynch, R.Ruggiero, A. Gordeev
24
xPHENIX OUTER H-cal MODULE VERSION. PRELIMINARY STUDY . ASSEMBLY POSSIBLE SCENARIO. TEMPORARY SUPPORT
INNER HCAL INSTALLATION
INNER HCAL MODULE
I-BEAM
SUPPORT
SHORT I-BEAM
C3PO
INNER HCAL
ASSEMBLY FIXTURE
I-BEAM
SUPPORT
SUPPORT RING
I-BEAM EXTENSION

## Slide 25
CUT AWAY VIEW
INNER HCAL
SUPPORT RING
OUTER HCAL
MAGNET
EMCAL

## Slide 26
InnerHCAL ENDPLATE
Inner HCAL SUPPORT END RING
L-BRACKET
SUPPORT RING
SPLICE PLATE
SUPPORT RING CROSS SECTION

## Slide 27
SiPM PC Board
SiPM Holder
TOWER BOARD
PC BOARD
PC Board Brace
SiPM PC Board
HCAL ELECTRONICS & CABLE ROUTING

## Slide 28
EMCAL MODULES ATTACHED TO INNER HCAL
LINEAR RAILS
CARRIAGE

## Slide 29
SUPPORT RING ATTACHMENTS
L-BRACKET
SPLICE PLATE