## Slide 1: sPHENIX Director’s Review Calorimeter Digitizer
C-Y Chi
August 2-4, 2017
BNL

## Slide 2: The Subsystem
The calorimeter digitizer system
  Off detector ADC system for both EM and Hadronic calorimeter.
  Received the amplified signal from on-detector amplify through cables
  Digitize the signal at 6x beam crossing rate, ~ 60 MHz, with 14 bits ADC
    Offset the baseline to use most of the ADC range.
  Provide at least 40 beam crossing of data buffers to cover L1 trigger latency
  Provide Level 1 trigger primitives.
  have at least 4 Level 1 events buffer.
    Maximum 31 ADC samples per channel per events, 16 samples planned.
  Up to 15 KHz Level 1 trigger rate.
  Send Level 1 trigger events to the DAQ system.

## Slide 3: The Subsystem Technical Overview
Controller
clockmaster
GTM
JSEB II
PC
ADC
ADC
XMIT
Trigger
out
Trigger
out
DCM II
crate
(rack based)
Slow control/readback
Beam clock,
L0, L1 trigger
SPHENIX DAQ System
detector
Slow control/readback
bus, L0, L1 trigger
Token passing
dataway
Token passing
dataway
Clock are fanout point to
point through the backplane
Crate based system.
Signals are cable from the on-detector electronics.
Digitized with 14 bit ADC.
Receive timing information the SPHENIX Granule Timing Module (GTM)
Generate L1 trigger primitives
(not in the reference design)
Receive L1 trigger and send out L1 triggered event data to Data Collection Module II (DCMII).
Provide buffer for both the 40 beam crossing L1 delay buffer and 4 L1 triggered events
3 ADC  XMIT
3Gbit/sec
optical link
1.6Gbit/sec
optical link

## Slide 4: Scope
The sub-system consists of
  432 ADC boards
    64 channel per board
      EMCAL 24576 Channels, HCAL 3072 channels.
  144 XMIT modules
  36 crates
  Power supplies
  Up to 36 clock master modules

## Slide 5: Subsystem Collaborators
Currently we have only Columbia University handle this project.
  BNL is helping integration and DAQ test.
  Other groups can help us when the time ready for production or further long term testing.
This is the 3rd ADC system we have done in the last 10 years.
  The PHENIX HBD 60 MHz 12 bits ADC (48 channel per board).
  The MicroBooNe PMT readout, 64 MHZ 12 bits system.
    The difference for this ADC system are ADC baseline shifting, serial backplane pathway, trigger primitive generators and more channel in the same space

## Slide 6: Schedule Drivers
The ADC system prototype works
  Low Noise
  ADC data unpack
  Data buffering & trigger data readout
  Trigger primitive path
The electronics is off detector
  Little detector mechanical constraint.
If the testing with detector continues to be successful, we have not much schedule constraint.

## Slide 7: Cost Drivers
The cost drivers are on the ADC board.
  The 8 channel Analog Device ADC AD9257
    64 channel board  8 ADCs per board
  The Altera Arria 5 FPGA
    receive the ADC data and data manipulation, L1 delay, 5 events buffer and generating trigger primitives.
  The differential receiver, AD8132
    Receiver the differential signals from the cable. One per channel.
  The PCB board
  The PCB assembly.

## Slide 8: Basis of Estimate and Resource-Loaded Schedule

## Slide 9: Status and Highlights
ADC board
Custom ADC system backplane
ADC crate controller
ADC XMIT board

## Slide 10: Status and Highlights
channel
channel
ADC counts
ADC counts
Average
Sigma
ADC baseline histogram (without signal cables)
14 bits ADC system (16384 ADC counts)
Without baseline shifting
Test stand in BNL
3 ADCs boards

## Slide 11: Summary
We have construct first round of the digitizer system.
  All first round prototype boards works so far.
    ADC board has low analog noise.
    Digital logics work so far
    Trigger daughter card seems to work.
  Some modification may be necessary when interface with sphenix timing system
    Just affect the crate controller.
  BNL test stands ongoing
    Going reasonable well.
    Fine tune tests will be done.

## Slide 12: Back Up

## Slide 13
7X ADC clock
F
R
A
M
E
Serialized ADC DATA
De-serializer
Serial
command
L1
Delay
Buffer
5 L1
Accepted
Event
buffer
Token
Passing
Data
ALTERA Arria V GX
BB1D4F35
1152 pins FPGA
Analog
Device
AD9257
8 channel
14bits
65 MHz
ADC
Clock
Fanout
Differential
receiver
6 X beam
clock
2 mm
Hard Metric
or mini-SAS
Connector
Analog
Device
AD9257
8 channel
14 bits
65 MHz
ADC
2 mm
Hard Metric
or min-SAS
Connector
Differential
receiver
Serialized ADC DATA
F
R
A
M
E
7X ADC clock
64 channel
ADC board
6x beam clock
Beam phase,
init, L1
Serialized
Token
Passing
command/
offline data read
De-serializer
Bused command
Serial data
+- 3.5V, -2.5V
Differential
receiver power
+1.8V analog
ADC power
+1.8V digital
ADC power
DC/DC
switch regulator
+4V, -3.5V, +2.5V
Power
+12V
Power
DC/DC
switch regulator
1.5V
LDO
1.1V
core
4V
2.5V FPGA I/O
3.3V
LDO
3.3V
LDO
D
P
U
two transceivers
two transceivers
sPHENIX ADC Module Block Diagram
L1 trigger primitives
transceiver out
RHIC beam clock 9.6MHz

## Slide 15
2mm HM
Input
connector
Differential
receivers
Analog
Device
AD9257
14 bits
ADC
Analog
Power
Trigger
Primitives
output
Serial
Command
output
Serial
Command
input
Clock in
L0/L1
Digital
Power
Token
Passing
Data
In/out
SPHENIX ADC board
64 channel inputs
2mm HM connectors
160mm by 190mm (6U board)
The 8 channel 14 bits ADC will be running at 6x beam crossing rate ~ 60 MHz
Altera Arria 5GX FPGA de-serialize data, provide 5 events buffer, 40 beam crossing L1 delay, token passing data, L1 trigger primitives output
ALTERA
Arria 5GX
FPGA

## Slide 17
Pulse shape channel 40
ADC
ADC
ADC
ADC
Sample number
rms