## Slide 1: sPHENIX Director’s Review Calorimeter Simulations
Jin Huang (BNL)
August 2-4, 2017
BNL

## Slide 2: sPHENIX Calorimeters in Simulation
EM calorimeter (EMCal) : 18 X0 W-SPACAL
Inner hadron calorimeter (Inner HCal) : 1 λ0 SS-Scint. sampling
sPHENIX coil and cryostat. (Magnet): 1.4 X0 Coil & Cryostat
Outer hadron calorimeter (Outer HCal) : 4 λ0 SS-Scint. sampling
EMCal
Inner HCal
Magnet
Outer HCal
IP
Open source @
https://github.com/sPHENIX-Collaboration/
Geant4 Land

## Slide 3
Simulation Setup: EMCal
10GeV, e+
2 cm
SPACAL Tower w/ fibers displayed
EMCal Half Sector
(fibers simulated but hidden from display)
8 GeV photons in full EMCal
Side view/beam view

## Slide 4: Simulation Setup: HCal
Baseline design
Calorimeter simulation & analysis chain: GEANT4 hit → Scintillation light model → Light collection model → Tower readout → Digitization → Calibrated tower energy → Clustering/Track matching/Jet finding
24-GeV pion shower
EMCal
Inner HCal
Magnet
Outer HCal
Beam view of full calorimeters

## Slide 5: Test Beam Verification [arXiv:1704.01461]
EMCal energy resolution for EM shower in tower center
EMCal rejection for pion-
HCal energy response for pion-
Geant4 World
sPHENIX beam test data
sPHENIX beam test data

## Slide 6: Occupancy in Central Au+Au Events
sPHENIX is designed to handle large background environment of central AuAu collisions
Such background is simulated with HIJING → full detector in Geant4 → full analysis chain
Taken into account for electron ID and jet performance via embedding
EMCal
Inner HCal
Outer HCal
EMCal
Inner HCal
Outer HCal

## Slide 7: Spatial responses
EMCal radius (cm)
EMCal X (cm)
EMCal Y (cm)
← Moliere radius, 2cm
← 3x3 tower
95% containment
EMCal radius (cm)
Inner HCal radius (cm)
EMCal X (cm)
Inner HCal X (cm)
Inner Hcal Y (cm)
EMCal Y (cm)
← 3x3 tower
50% containment
← ~3x3 tower
60% containment
― Energy deposition (A.U.)
― Percentage outside radius
4 GeV Electrons
4 GeV Pions, that passed E/p electron-ID cut
EMCal
EMCal
Inner HCal
A.U./Leakage Ratio
A.U./Leakage Ratio
A.U./Leakage Ratio
EMCal design has a tight Moliere radius of 2 cm → Reduce background in Au+Au

## Slide 8: Performance : Single EM Showers
Applied cluster-position-based non-uniformity correction as used in test beam analysis
dE/E ~ 15%/ √(E) + 4% (meets sPHENIX goal)
sPHENIX beam test data
Beam test [arXiv:1704.01461] Full sPHENIX detector simulation

## Slide 9: Performance : Photon in Full Event
Good linearity up to photon kinematic limit of sPHENIX
Good photon response shown in full gamma-jet event simulations
In progress: improving clustering algorithm to minimize background pickup in central Au+Au collisions.
Nevertheless, jet energy resolution dominates precision for gamma-jet momentum balance measurements

## Slide 10: Physics Performance : Electron-ID
Critical driving factor for EMCal design: Upsilon electron ID
Satisfied detector requirement (>90:1-pion rejection @ pT=4 GeV/c in central Au+Au collisions at 70% efficiency)
Updating Upsilon background and RAA projections
Updating ...
Upsilon RAA projections in sPHENIX proposal
Assuming 100:1 pion rejection @ 70% e-eff.
Pion rejection @ (improved) 90% efficiency
arXiv:1501.06197

## Slide 11: Performance : Jet Finding
Jets in p+p and central Au+Au collisions are also studied in full detector simulations
Jet finding followed by iterative background subtraction [10.1103/PhysRevC.86.024908]
Study are in progress updating the jet performance plots as in sPHENIX proposal
Preliminary results show good efficiency (>80% for pT>20 GeV/c jet in central Au+Au collisions)
Further improving underlying event subtraction and fake-jet rejection algorithm based on RHIC and LHC experiences

## Slide 12: Performance : Jet Energy Resolution
Detector simulations has been updated with detailed engineering design and beam test tunings
Study are in progress, results are still preliminary
Preliminary energy resolution was found consistent with simulation study as in sPHENIX proposal [arXiv:1501.06197]
sPHENIX proposal [arXiv:1501.06197]
Full detector simulation with the current design

## Slide 13: Physics Performance : Jet Observables
Jet-balance/imbalance observables simulated in full detector events: day-1 measurement, resolution under control
On-going effort in understanding the details of the jet simulations and unfolding studies.
Expanding jet observables studied with the updated design and simulations
Di-jet transverse momentum asymmetry
γ-jet transverse momentum balance

## Slide 14: Summary
A detailed model of the sPHENIX calorimeter has been implemented in GEANT4 and used for design and performance studies
Good agreement with test beam data
Calorimeter performance achieves the scientific goals
Work in progress to update reconstruction algorithms and the physics performance plots with refined detector design and simulation

## Slide 15: Extra information

## Slide 16: HCal simulation verification
HCal prototype @ eta = 0 energy response for pion-
T-1044 test beam and simulation
arXiv:1704.01461
Full sPHENIX energy response for pion-

## Slide 17: HCal prototype 3 @ η = 1
sPHENIX beam test data, Inner + Outer HCal
sPHENIX beam test simulation, Inner + Outer HCal
sPHENIX beam test data, Inner + Outer HCal

## Slide 18: HCal prototype 2 @ η = 0

## Slide 19: Performance : Single Hadron showers
Single pion shower studied with clusters of digitized towers (3x3 and 5x5 clusters), which is compared with ideal sum of Geant4 hit in scintillator (label G4Hits)
Energy resolution satisfied design goal. Tails <= 10%
Requirement: 100%/√E ⊕ 10%
10% stat. in each tail
2.5% stat. in tails as expected from Gauss shape
Energy resolution
Linearity
Single-side tail

## Slide 20: Performance : Single Hadron showers

## Slide 21: Jet energy response and scale
Fig 5

## Slide 22: Jet and di-jet response

## Slide 23: Tilt angle optimization
Reasonable Range
Performance not a strong function of tilt angle of Hcal iron plates
Baseline design (4-crossing tilt angle) is a reasonable choice
Baseline design
Baseline design
Hcal #-of-crossing
50GeV π- tail
2GeV π- tail
24GeV π- ΔE/E

## Slide 24: Fast simulation for Jets in central Au+Au
Algorithm developed based on ATLAS and CMS heavy ion experience
Good efficiency and purity
Resolution/tails fit for unfolding jet spectrum
Need to keep updated as detector design/performance evolves
pT (GeV)