## Slide 1: sPHENIX Director’s Review sPHENIX Triggering
Jamie Nagle
Dennis Perepelitsa
University of Colorado Boulder
August 2-4, 2017
BNL

## Slide 2: The Trigger Technical Overview
sPHENIX 5-Year Run Plan
Trigger needs to deliver the physics within the 15 kHz DAQ bandwidth constraint.
Au+Au plan – record minimum bias events (using MBD trigger) at ~ 15 kHz. This delivers 239 billion events.
p+p and p+Au plan – sample full luminosity for key physics with Electromagnetic and Hadronic Calorimeter Level-1 triggers

## Slide 3: Scope
* No multi-tiered triggering necessary (i.e. Level-2, 3, …).
EMCal
Hcal
MTD
Front End Electronics
Level-1 Trigger
MTD, EMCal, HCal
Timing System
Global Trigger Decision
Trigger inputs – 8 bit 2x2 calorimeter tower sums, MTD tube time/energy
Trigger outputs – summary information within 4 microseconds, trigger primitive archiving

## Slide 4: Subsystem Collaborators
Professor Jamie Nagle
Professor Dennis Perepelitsa
University of Colorado Boulder
Dr. Cheng-Yi Chi
Columbia University, Nevis Laboratories
PHENIX Trigger Coordinator (2002-2010)
sPHENIX Calorimeter, MTD electronics
PHENIX DAQ / Electronics
Previous successful electronics collaborations:
PHENIX Data Collection Modules
PHENIX Resistive Plate Chamber Electronics
PHENIX Data Collection Modules II
sPHENIX Jet Working Group Co-Convener

## Slide 5: Status and Highlights
Maximum rates (early in store) and highest projections from C-AD
Au+Au simulations indicate MTD trigger > 90% efficient and with good z-vertex resolution. Sampling with Level-1 triggers under study.
For p+p and p+Au, rejections of order 5,000 - 10,000 are needed to get down to 1-2 kHz of bandwidth allocation for different physics topics.
Full GEANT-4 Simulations for trigger performance in 4 key channels:
(1) High pT Jets, (2) High pT Hadrons, (3) High pT Photons, (4) Upsilons

## Slide 6: C-AD Rate Projections Au+Au

## Slide 7: Status and Highlights

## Slide 8: Status and Highlights
Upsilon  ee Trigger Example
Trigger Efficiency and Rejection look good.
8-bit bandwidth on 2x2 energy sum inputs under study.
Invariant mass cut and FPGA implementation in early stages.

## Slide 9: Summary
Trigger requirements for sPHENIX are modest.
Au+Au physics delivered by minimum bias (MTD) triggering only.
p+p and p+Au simulation studies look good in terms of the 4 key channels
Early stages of architecture and board considerations. No major schedule concerns.

## Slide 10: Back Up

## Slide 11
Direct photons

## Slide 12
2. Reconstructed Jets

## Slide 13
3. Hadrons…

## Slide 14
4. Upsilons…
All look in reasonable shape for p+p case for “core sPHENIX physics deliverables”…. Probably the bigger question is
what more can we deliver…