## Slide 1: EPIC Power and Grounding Thoughts
E.J. Mannel
July 14, 2026

## Slide 2: AC Power
”Dirty AC”: supplies power to things that can generate noise on the AC lines
  Pumps
  Fans
  Compressors
  Fluorescent lights
”Clean AC”: Electronics
  AC-DC power supplies
  Crates, AC-DC power suppies
  Scopes or other monitoring hardware
  Computers (could be on dirty AC depending on application)
Ideally on separate AC transformers to isolate noise.
All racks, cabinets, crates are bonded to AC ground.
Balance loads between all phases

## Slide 3: DC Power (Electronics)
Need to think of DC power as:
  Source: positive connection on a DC supply
  Return: negative connection on a DC supply
  Reference ground: This is the “zero” potential with respect to earth ground
  For most AC-DC supplies, they are floating, so until you reference either the source or the return to the reference ground, there is no “ground”.
  Most supplies have a “safety” ground which is a diode to ground
Ideally, the reference ground is a “stake” in the earth
  Heavy conductors radiating outwards, “star configuration”
  DC power supplies are referenced at the power supply side
  Reference ground is not the “AC” ground connection on the power cord
  Avoid ground loops

## Slide 4: Ground Referencing
Positive Power Supply
RL
+
-
Negative Power Supply
RL
+
-
Reference Ground
Reference Ground
The green is best
The red, while it is OK, has potential
Issues if there is a break in the
connections to the supplies
Having both leads to potential ground loops

## Slide 5: Things to Consider
Power and grounding should be a part of every design review.
  Ground loops
  Conductor size, connectors
  Power distribution on electronics
Power drops across both the supply and return conductors need to be taken into account when determining the supply voltage.
Fusing and selecting power supplies appropriately.
Cooling of components and electrically isolating the electronics from the chillers. Detector component specific.

## Slide 6: Things to Consider II
Proper selection of cable
  Voltage rating
  Current rating
  Fire rating
Cable tray loading
  Volume
  Heat/power dissipation
  Cables don’t follow the AI’s routing all the time
No matter how well you design and document it, Physicist will find a way to violate the power/ground plan and provide justification.