## Slide 1: Overview of ZDC Requirements for the EIC
Alex Jentsch, Brookhaven National Lab
ajentsch@bnl.gov
ePIC TIC Meeting
Sept. 23rd, 2024

## Slide 2: Basic “Requirements”
ZDC requirements were put together prior to the Yellow Report, and before any comprehensive study of the physics was really put together.
  Hadronic energy resolution:
  EM energy resolution:
  Soft photon sensitivity for MeV
  Sufficient dynamic range for energy deposits from breakup of heavy nuclei (several neutrons with eV)
  Sufficient granularity to provide angular resolution for pT reconstruction:
ZDC acceptance: 𝜃 < 5mrad (not 𝜙-symmetric) – driven by aperture, not detector.
General NB: Previous and current studies and extracted resolutions all assume “perfect” ZDC performance, except for transverse and longitudinal leakage. They do not include effects of backgrounds, electronics, light collection, etc.

## Slide 3: (some) Physics channels relying on ZDC
J/Ψ
e+d exclusive J/Psi with p/n
tagging
spectator tagging in light nuclei
Quasi-elastic electron scattering
u-channel backward exclusive electroproduction
Sullivan process

## Slide 4: (some) Physics channels relying on ZDC
J/Ψ
e+d exclusive J/Psi with p/n
tagging
spectator tagging in light nuclei
Quasi-elastic electron scattering
u-channel backward exclusive electroproduction
Sullivan process
High-energy single neutrons and
High energy photons from and
High-energy single neutrons
High-energy single neutrons
Multiple high-energy neutrons; soft photons
High-energy single neutrons
In every case, we will only have *one* of the possible final state options (e.g. either neutrons or photons, not both).

## Slide 5: Top-level Summary of Requirements
Physics process | Final State particles (for ZDC) | Required HCAL E resolution | Required HCAL angular resolution | Required EMCAL E resolution | Required EMCAL spatial resolution | Notes
Spectator tagged e+d breakup | Neutrons |  |  | N/A | N/A | https://arxiv.org/pdf/2005.14706.pdf https://arxiv.org/abs/2108.08314
Exclusive production | Neutrons |  |  | N/A | N/A | 
Incoherent vetoing of e+A events | Neutrons/photons |  | N/A | 100 MeV photon sensitivity | N/A | https://arxiv.org/abs/2108.01694
u-channel backward VCS | Photons | N/A | N/A |  | < 1-2cm | https://arxiv.org/pdf/2308.10478.pdf https://indico.bnl.gov/event/21074/contributions/82988/attachments/50847/86922/23_11_07%20ZDC%20Update.pdf
Kaon structure functions |  |  |  |  | < 1-2cm | https://arxiv.org/pdf/2102.11788.pdf
Physics process | Final State particles (for ZDC) | Required HCAL E resolution | Required HCAL angular resolution | Required EMCAL E resolution | Required EMCAL spatial resolution | Notes
Spectator tagged e+d breakup | Neutrons |  |  | N/A | N/A | https://arxiv.org/pdf/2005.14706.pdf https://arxiv.org/abs/2108.08314
 | Neutrons |  |  | N/A | N/A | 
Incoherent vetoing of e+A events | Neutrons/photons |  | N/A | 100 MeV photon sensitivity | N/A | https://arxiv.org/abs/2108.01694
u-channel backward VCS | Photons | N/A | N/A |  | < 1-2cm | https://arxiv.org/pdf/2308.10478.pdf https://indico.bnl.gov/event/21074/contributions/82988/attachments/50847/86922/23_11_07%20ZDC%20Update.pdf
Kaon structure functions |  |  |  |  | < 1-2cm | https://arxiv.org/pdf/2102.11788.pdf

## Slide 6: Photons
Soft photon tagging important for vetoing of incoherent e+A events (about 3.25% of events produce *only* soft photon).
Figure from: W. Chang, E.C. Aschenauer, M. D. Baker, A. Jentsch, J.H. Lee, Z. Tu, Z. Yin, and L.Zheng, Phys. Rev. D 104, 114030 (2021)
Backward u-channel 𝜔 production.
Study performed with STARLIGHT events using EICROOT.
Final state: (ZDC acceptance ~ 16%)
Study assumed and

## Slide 7: Photons
Calculation of missing energy requires precise knowledge of the photon energy from the decay.
Reference for the study implies need for 1-2cm spatial resolution to resolve decay photons and separate from desired Compton photon, and implies need for .
  https://arxiv.org/pdf/2308.10478.pdf

## Slide 8: Photons
Requires precise knowledge of the photon energy from the decay.
1-2cm spatial resolution required for separation of neutron and gamma from .
  Depends on the decay vertex for the along the beamline!
Reference for the study implies need for .
  https://arxiv.org/pdf/2102.11788.pdf

## Slide 9: Single Neutrons
e+d spectator tagging to study short-range correlations.
Proton spectator from OMD.
Neutron spectator from ZDC.
Assuming and
From: Z. Tu, A. Jentsch et al., Phys. Lett. B, 811 (2020)

## Slide 10: Single Neutrons
From: A. Jentsch, Z. Tu, and C. Weiss, Phys. Rev. C 104, 065205, (2021)
e+d spectator tagging to study neutron structure functions  focus on very small angle neutrons near
Proton spectator from OMD.
Neutron spectator from ZDC.
Assuming and
Baseline ZDC assumption is problematic here – would benefit from improved neutron energy and angular resolution.

## Slide 11: Single Neutrons
If energy resolution is too poor, better spatial/angular resolution does very little to improve pT-resolution.
  Need minimum
To get pT resolution competitive with the tagged-proton case would require
Very little difference between and  Improved constant term has small effect.

## Slide 12: Single Neutrons (better constant term)
If energy resolution is too poor, better spatial/angular resolution does very little to improve pT-resolution.
  Need minimum
To get pT resolution competitive with the tagged-proton case would require
Very little difference between and  Improved constant term has small effect.