## Slide 1: Status report
Ayuki Watanabe
Tohoku Univ.

## Slide 2: Purpose
Evaluate the material effect of BTOF on BIC.
  Calculate energy resolution

## Slide 3: Simulation condition
EICrecon version：v1.39.0
ePIC：26.07.0
Single particle simulation
Particle：e-
Momentum：1, 2, 3, 5, 7, 10 GeV/c
10000 events
Theta=90*deg
Distribution：uniform (flat in )
Generation point：(0, 0, 0)
Multiplicity：1
Chang the material of BTOF support structure “cfoam” to Aluminum, carbon fiber, and vacuum.
Supprot structure
BTOF

## Slide 4: How to analysis
I use branch “EcalBarrelClusters.energy”. This shows reconstructed energy from ScFi energy.
A tail is observed in low energy side.
Use Crystal ball fit for fitting data.
A and B are function of and n

## Slide 5: Results
This shows energy distribution of e- with 5 GeV/c through vacuum support structure.
Use Crystal Ball fit with fit range from -4 * sigma of gaussian prefit to 3 * sigma of gaussian prefit.
：energy at generated point
Energy distribution ( GeV, Vacuum)

## Slide 6: Results
Energy resolution as a function of
Fit energy resolution with
.
：sigma of gaussian core of Crystal ball function
It seems resolution almost doesn’t change from material effect of BTOF.
Energy resolution

## Slide 7: Results
This shows yields of 1 cluster / 1event
：number of events of 1 cluster / 1 event
：number of events
This almost doesn’t change from materials.
yields
Aluminum (X/X0=17.6%)
CarbonFiber (X/X0=6.3%)
CarbonFoam (X/X0=1.3%)
Vacuum

## Slide 8: Results
This shows Ratio of tail area.
tail area ()
：Crystal ball fit area
Tail doesn’t have much events, so this has big error.
As energy increases, the ratio of tail area becomes large with Aluminum compared to other materials.
Ratio of tail area

## Slide 9
Clusters / 1 event