## Slide 1: Charge sharing and EICROC2 readout architecture implications
AC-LGAD electronics meeting
Friday, Sept. 4th, 2026
Alex Jentsch (BNL)

## Slide 2: Preliminaries
AC-LGADs use capacitive coupling to enable deposited charge to share signal across neighboring readout pads.
AC-LGAD
EICROC0
PCB
backplane
Incident particle
A 30um “active layer” in an AC-LGAD has around 0.35 fC of charge from an average MIP.
  Gain of the device is around 50  avg. MIP charge is ~ 17.5 fC (Landau fluctuations will obviously provide a range of values)
  EICROC0A + sensor has minimum threshold ~ 5-6 fC
Adjacent neighbor
Primary “pixel”
adjacent neighbor
Corner neighbor
primary pixel
Adjacent neighbor
Adjacent neighbor
Adjacent neighbor
Adjacent neighbor
Corner neighbor
Corner neighbor
Corner neighbor
Corner neighbor

## Slide 3: How does charge sharing affect resolution?
Improved timing resolution using combined timing information in same sensor from neighboring pixels.
Significant improvement in spatial resolution compared to a standard pixel device.
    500 um pixel pitch nominally gives ~ 144um spatial resolution, AC-LGADs have been shown to deliver ~ 20um spatial resolution using charge sharing.
Hit position resolution limited to ~ pitch/
Refined hit position resolution using barycenter/center of gravity

## Slide 4: Resolution vs. neighboring pixels used
Assume average MIP is ~ 20fC  leads to an amplitude (preamp) ~ 160mV from a 30um device biased to -170V.
Simple toy MC  use Lorentzian to mimic charge falloff in neighboring pads as a function of distance from hit.

## Slide 5: Resolution vs. neighboring pixels used
Assume average MIP is ~ 20fC  leads to an amplitude (preamp) ~ 160mV from a 30um device biased to -170V.
Simple toy MC  use Lorentzian to mimic charge falloff in neighboring pads as a function of distance from hit.
Produce random hits sampled from a Gaussian.

## Slide 6: Resolution vs. neighboring pixels used
Assume average MIP is ~ 20fC  leads to an amplitude (preamp) ~ 160mV from a 30um device biased to -170V.
Simple toy MC  use Lorentzian to mimic charge falloff in neighboring pads as a function of distance from hit.
Cross readout
3x3 readout
Using RMS values
Essentially no use of charge sharing

## Slide 7: Summary
Assuming average MIP (with gain of 30um AC-LGAD) is around 20 fC, 3x3 readout necessary to be able to meet requirements of the B0 tracking detector.