## Slide 1: Position resolution of BTOF
9/10/2026

## Slide 2: Charge sharing and digitization work-flow
Start
Geant hit
Charge sharing
Edep in cells
Pulse Generation
Pulse Combiner
ADC and TDC values
Pulse Discretization
Pulse Digitization
Calibration
Clustering
Cluster
Association
Tracking
Measurement2D

## Slide 3: Charge sharing and digitization work-flow
Start
Geant hit
Charge sharing
Edep in cells
Pulse Generation
Pulse Combiner
ADC and TDC values
Pulse Discretization
Pulse Digitization
Calibration
Clustering
Cluster
Association
Tracking
Measurement2D
Challenges:
Efficiency lost due to digitization not yet understood.
  Thresholds, dynamic range, etc not realistic yet.
Truth-hit association not implemented

## Slide 4: Proposed update: Bypass all digitization routine
Start
Geant hit
Charge sharing
Edep in cells
Pulse Generation
Pulse Combiner
ADC and TDC values
Pulse Discretization
Pulse Digitization
Calibration
Clustering
Cluster
Association
Tracking
Measurement2D
Without digitization steps,
Hit lost due to thresholds minimized.
Truth association is easy to implement.

## Slide 5: Clustering algorithm
Clustering: weighted average of neighbors.
  Group contiguous neighbors.
    Hits are contiguous in time if Δt < 1ns.
  Weighted by Edep.
  Time of a cluster = time of the earliest hit.
  No Edge correction.
Cluster 1
Cluster 2
Cluster 3
Time axis not shown

## Slide 6: Settings for performance study
MC particle gun:
  0.8 < theta < 2.3 rad
  2pi azimuth uniform
  |p| = 1 GeV/c
  e- only
Thresholds:
  Edep > 6 keV hits only.
Charge sharing profile:
  2D gaussian, with principal axis aligned with local sensor coordinates.
Z (beam axis)
x
sigmax
BTOF sensor
Pictorial illustration
Pixel pitch

## Slide 7: Position resolution (Delta Phi)
Delta between cluster position and TOFBarrelHits position (i.e. Geant4 exact hit position on BTOF)
Red (old): No clustering algorithm (Use pixel center)
Blue (new): With clustering algorithm
Sigmax=0.5*pixel width

## Slide 8: Position resolution vs charge sharing magnitude