## Slide 1
LFHCal calibration fits
Paul Nord
6 October 2026
Notes: Integrated presentation: original F1 Yallfile workflow, discussion and interpretation, and all 53 plots from the supplied deck. New technical and discussion slides are editable. Plot images and their source notes are preserved. Observations and proposed validation steps are distinguished.

## Slide 2
Main findings
Reanalysis of F2 agrees with Fredi’s calibration to better than 0.01% in all 380 calibrated channels. - Same code. Likely machine precision differences.
Adaptive integration removes artificial wiggles from the fit function.
The new lower boundary improves many examples and can shift calibration values by a few percent.
A stable refinement history can still end at a poor fit.
F2 reproduction check: 17 September 2026
Notes: F2 reproduction evidence: README(2).md, “LFHCAL FullSetF_2 calibration reproduction comparison,” 17 September 2026. Library source libfile_4a0bd56cf7a081919d18cb7bfc24cafe, file_00000000025881f9ab6dd034cf4a4e51. The final file is byte-identical to the user’s Imp5R output. All 380 positive HG MIP scales differ from Fredi’s reference by less than 0.01%, with median absolute relative difference 0.000003374% and maximum 0.005241889%. Both tables have the same four unavailable scales. This verifies the F2 constants comparison and is not an all-dataset reproduction claim.
Numerical wiggles: prior comparison of the fixed 100-point Legacy Langau evaluation with adaptive integration, and the E3 cell 1346 overlay in this deck. The physical Landau–Gaussian model is unchanged.
Range sensitivity: lfhcal-fit-range-report.pdf, 1 October 2026, Library source libfile_a0d224264fd481919be7135b0463c199. Fixed-histogram B1 controls shift 0 to -4.00% with the Adaptive evaluator when the window changes. The cleaner controls change less. The improvement statement is qualitative for selected examples, not an aggregate success rate. Both Legacy and Adaptive with the valley boundary remain candidates.
Convergence does not certify fit quality. The B2 cell 704 valley Adaptive example changes markedly between R7 and R8, and an unsuitable fit can also remain stable.

## Slide 3
Study of 2 numerical fitting methods and 2 range selection methods
Fit method | Original lower boundary | Valley lower boundary
Legacy | Original numerical fit Original range choice | Same numerical fit New range choice
Adaptive | Adaptive evaluation Original range choice | Adaptive evaluation New range choice
Notes: Study context and observations are from this conversation and the supplied BNL plots. Plot slides retain their original source notes. Original-boundary and valley-boundary results are distinct campaigns. Selected events were inherited separately for Legacy and Adaptive in the valley campaign. This is a refinement study, not a rerun of all upstream stages with the new boundary.

## Slide 4
Plotting ALL fit parameters in one calibration flow plot
Each thin line follows one channel through the calibration stages.
The dark line shows the median.
Step plots: compare each channel with its own previous value. (e.g. R1-R2)
R5-reference plots: compare each channel with its Fredi’s calibration values.
A signed-log scale lets us see small differences and large jumps together.
Most channels settle down. B2 and a few channels in the E sets keep jumping.
Note: A stable calibration can still come from a poor fit.
Notes: Study context and observations are from this conversation and the supplied BNL plots. Plot slides retain their original source notes. Original-boundary and valley-boundary results are distinct campaigns. Selected events were inherited separately for Legacy and Adaptive in the valley campaign. This is a refinement study, not a rerun of all upstream stages with the new boundary.
H denotes the stored high-gain MIP calibration scale, distinct from the Landau MPV parameter. The supplied plots include H, Landau MPV, Landau width, and Gaussian sigma. Inspect each plot’s title and axis labels before comparing panels. Median convergence cannot certify every channel. A carried-forward value is not a fresh successful fit.

## Slide 5
Calibration step size: Legacy (B and E sets)
Notes: Source: lfhcal-step-convergence-focus-legacy.pdf, page 1
Section: Convergence
Original source path: /workspace/scratch/973a74c46106/upload/lfhcal-step-convergence-focus-legacy.pdf

## Slide 6
Calibration step size: Adaptive (B and E sets)
Notes: Source: lfhcal-step-convergence-focus-adaptive.pdf, page 1
Section: Convergence
Original source path: /workspace/scratch/973a74c46106/upload/lfhcal-step-convergence-focus-adaptive.pdf

## Slide 7
Calibration step size: Legacy
Notes: Source: lfhcal-step-convergence-legacy.pdf, page 1
Section: Convergence
Original source path: /workspace/scratch/973a74c46106/upload/lfhcal-step-convergence-legacy.pdf

## Slide 8
Calibration step size: Adaptive
Notes: Source: lfhcal-step-convergence-adaptive.pdf, page 1
Section: Convergence
Original source path: /workspace/scratch/973a74c46106/upload/lfhcal-step-convergence-adaptive.pdf

## Slide 9
B2 needs a data-quality check as well
Data quality is a hypothesis to investigate, not an explanation already proved
B1 is comparatively stable, while B2 remains troublesome despite nominally similar configuration.
The run database labels two contributing B2 runs “dirty muon.”
That note motivates a run-level comparison, but does not establish the cause of the difficult spectra.
Inspect fit shape, parameter jumps, and fresh-fit coverage together before choosing a method.
Notes: Study context and observations are from this conversation and the supplied BNL plots. Plot slides retain their original source notes. Original-boundary and valley-boundary results are distinct campaigns. Selected events were inherited separately for Legacy and Adaptive in the valley campaign. This is a refinement study, not a rerun of all upstream stages with the new boundary.
Dirty-muon labels: https://github.com/paulnord/epic-lfhcal-tbana/blob/924ad82de6d150534b4d7684b5638df92c0a2016/configs/TB2026/DataTakingDB_TBSPSH2_202605_HGCROC.csv
The B2 merge list includes the two labelled runs. Acquisition run identifiers intentionally omitted. The database annotation alone does not establish the contamination mechanism or its fraction after selection. B1/B2 configuration similarity is the working context supplied by the user.

## Slide 10
B2: Legacy relative to Legacy R5
Notes: Source: b2-legacy-r5-legacy.png
Section: Selected examples
Original source path: /workspace/scratch/973a74c46106/upload/b2-legacy-r5-legacy.png

## Slide 11
B2: Adaptive step changes
Notes: Source: b2-step-adaptive(1).png
Section: Selected examples
Original source path: /workspace/scratch/973a74c46106/upload/b2-step-adaptive(1).png

## Slide 12
Why change the lower fit boundary?
Boundary-selection study
Some fits extend too far into the low-ADC region and miss the visible MIP peak.
A boundary controlled by one low bin can be sensitive to statistical fluctuations.
A fitted valley uses the surrounding shape to choose a more stable lower edge.
A rejected valley candidate can fall back to the original boundary, so the reported status matters.
Notes: Study context and observations are from this conversation and the supplied BNL plots. Plot slides retain their original source notes. Original-boundary and valley-boundary results are distinct campaigns. Selected events were inherited separately for Legacy and Adaptive in the valley campaign. This is a refinement study, not a rerun of all upstream stages with the new boundary.
The lower-edge study was motivated by the supplied histogram overlays and range-scan discussion. The valley procedure is a candidate boundary finder, not a guarantee that each fit uses a newly accepted valley. B2 cell 704 illustrates the minimum_at_boundary fallback. Do not infer that the procedure always excludes individual noisy bins.

## Slide 13
Old boundary: Legacy step changes
Notes: Source: lfhcal-old-boundary-step-legacy(1).png
Section: Boundary comparison
Original source path: /workspace/scratch/973a74c46106/upload/lfhcal-old-boundary-step-legacy(1).png

## Slide 14
Old boundary: Adaptive step changes
Notes: Source: lfhcal-old-boundary-step-adaptive(1).png
Section: Boundary comparison
Original source path: /workspace/scratch/973a74c46106/upload/lfhcal-old-boundary-step-adaptive(1).png

## Slide 15
New boundary: Legacy step changes
Notes: Source: lfhcal-new-boundary-step-legacy(1).png
Section: Boundary comparison
Original source path: /workspace/scratch/973a74c46106/upload/lfhcal-new-boundary-step-legacy(1).png

## Slide 16
New boundary: Adaptive step changes
Notes: Source: lfhcal-new-boundary-step-adaptive(1).png
Section: Boundary comparison
Original source path: /workspace/scratch/973a74c46106/upload/lfhcal-new-boundary-step-adaptive(1).png

## Slide 17
Better-looking fits can shift the calibration
Interpretation
The new lower boundary improves several examples with both Legacy and Adaptive.
Legacy with the valley finder remains a candidate in the comparison.
Percent-level changes also occur in well-behaved channels. These are calibration changes that need validation.
Convergence and visual agreement are useful evidence, but neither establishes an unbiased scale.
Notes: Study context and observations are from this conversation and the supplied BNL plots. Plot slides retain their original source notes. Original-boundary and valley-boundary results are distinct campaigns. Selected events were inherited separately for Legacy and Adaptive in the valley campaign. This is a refinement study, not a rerun of all upstream stages with the new boundary.
This is a qualitative interpretation of the reviewed examples and the range tests, not an aggregate success rate. The user specifically raised concern about shifts of two or three percent in controls. Avoid claiming that the new range is universally superior or that Legacy is ruled out.

## Slide 18
E3 and B1: inspect the fitted shape
Selected R5 overlays
E3 cell 1346 makes the Legacy curve’s numerical structure visible in the overlay.
E3 cell 640 has an Adaptive fit at R5 where the original Legacy overlay has no saved fit.
B1 cell 1479 shows why a visible low bin and the lower edge deserve attention even in a stable set.
Use these overlays to identify questions for testing, rather than accepting a fit because it was saved.
Notes: Study context and observations are from this conversation and the supplied BNL plots. Plot slides retain their original source notes. Original-boundary and valley-boundary results are distinct campaigns. Selected events were inherited separately for Legacy and Adaptive in the valley campaign. This is a refinement study, not a rerun of all upstream stages with the new boundary.
E3 cell 640: the Adaptive fit already exists in earlier passes and stabilizes before R5; do not say it is first recovered at R5. B1 cell 1479: the supplied slide is the original-boundary overlay. A valley overlay for this exact cell is not included in the supplied deck, so this slide does not claim a visual demonstration that the valley solved it.

## Slide 19
E3 cell 1346: R5 fits
Notes: Source: e3-refine5-cell1346.png
Section: Selected examples
Original source path: /workspace/scratch/973a74c46106/upload/e3-refine5-cell1346.png

## Slide 20
E3 cell 640: R5 fits
Notes: Source: e3-refine5-cell640.png
Section: Selected examples
Original source path: /workspace/scratch/973a74c46106/upload/e3-refine5-cell640.png

## Slide 21
B1 cell 1479: R5 fits
Notes: Source: b1-refine5-cell1479.png
Section: Selected examples
Original source path: /workspace/scratch/973a74c46106/upload/b1-refine5-cell1479.png

## Slide 22
B2 cell 704: a late pass can get worse
Inspect R6, R7, and R8 together
The valley-campaign Adaptive fit changes substantially between R7 and R8.
H falls while the Gaussian width collapses toward zero and the Landau width increases.
The reported boundary status is minimum_at_boundary. The lower edge remains at the fallback value.
A high bin may influence the result, but the overlay alone cannot establish the cause.
Notes: Study context and observations are from this conversation and the supplied BNL plots. Plot slides retain their original source notes. Original-boundary and valley-boundary results are distinct campaigns. Selected events were inherited separately for Legacy and Adaptive in the valley campaign. This is a refinement study, not a rerun of all upstream stages with the new boundary.
From the supplied valley Adaptive panel: R7 H=27.962, MPV=23.643, wL=2.6192, sigma=14.357, range [7.5,176.23], chi2/ndf=2.1916. R8 H=21.134, MPV=21.134, wL=6.991, sigma=0.020334, range [7.5,176.41], chi2/ndf=3.3849. The lower edge remains 7.5 for R6–R8. These observations support an instability flag, not a unique causal explanation.
Plots omit nonfinite displayed errors while leaving bin counts unchanged. That presentation choice is not a repair of the underlying histogram error arrays.

## Slide 23
B2 cell 704: Original boundary, Legacy
Notes: Source: b2-cases.pdf, page 1
Section: B2 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b2-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b2-cell704-original-legacy.png

## Slide 24
B2 cell 704: Original boundary, Adaptive
Notes: Source: b2-cases.pdf, page 2
Section: B2 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b2-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b2-cell704-original-adaptive.png

## Slide 25
B2 cell 704: Valley boundary, Legacy
Notes: Source: b2-cases.pdf, page 3
Section: B2 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b2-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b2-cell704-valley-legacy.png

## Slide 26
B2 cell 704: Valley boundary, Adaptive
Notes: Source: b2-cases.pdf, page 4
Section: B2 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b2-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b2-cell704-valley-adaptive.png

## Slide 27
B2: remaining difficult channels
B2 cells 579, 2562, 709, 2118, and 1287
The next examples keep the same cell visible across both methods and both boundaries.
Check whether the peak position stabilizes, and whether the fit range follows the intended MIP feature.
Watch for a sudden exchange between Landau and Gaussian width as H changes.
A smoother function helps expose data structure, but cannot make an unsuitable spectrum well behaved.
Notes: Study context and observations are from this conversation and the supplied BNL plots. Plot slides retain their original source notes. Original-boundary and valley-boundary results are distinct campaigns. Selected events were inherited separately for Legacy and Adaptive in the valley campaign. This is a refinement study, not a rerun of all upstream stages with the new boundary.

## Slide 28
B2 cell 579: Original boundary, Legacy
Notes: Source: b2-cases.pdf, page 5
Section: B2 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b2-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b2-cell579-original-legacy.png

## Slide 29
B2 cell 579: Original boundary, Adaptive
Notes: Source: b2-cases.pdf, page 6
Section: B2 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b2-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b2-cell579-original-adaptive.png

## Slide 30
B2 cell 579: Valley boundary, Legacy
Notes: Source: b2-cases.pdf, page 7
Section: B2 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b2-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b2-cell579-valley-legacy.png

## Slide 31
B2 cell 579: Valley boundary, Adaptive
Notes: Source: b2-cases.pdf, page 8
Section: B2 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b2-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b2-cell579-valley-adaptive.png

## Slide 32
B2 cell 2562: Original boundary, Legacy
Notes: Source: b2-cases.pdf, page 9
Section: B2 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b2-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b2-cell2562-original-legacy.png

## Slide 33
B2 cell 2562: Original boundary, Adaptive
Notes: Source: b2-cases.pdf, page 10
Section: B2 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b2-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b2-cell2562-original-adaptive.png

## Slide 34
B2 cell 2562: Valley boundary, Legacy
Notes: Source: b2-cases.pdf, page 11
Section: B2 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b2-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b2-cell2562-valley-legacy.png

## Slide 35
B2 cell 2562: Valley boundary, Adaptive
Notes: Source: b2-cases.pdf, page 12
Section: B2 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b2-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b2-cell2562-valley-adaptive.png

## Slide 36
B2 cell 709: Original boundary, Legacy
Notes: Source: b2-cases.pdf, page 13
Section: B2 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b2-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b2-cell709-original-legacy.png

## Slide 37
B2 cell 709: Original boundary, Adaptive
Notes: Source: b2-cases.pdf, page 14
Section: B2 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b2-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b2-cell709-original-adaptive.png

## Slide 38
B2 cell 709: Valley boundary, Legacy
Notes: Source: b2-cases.pdf, page 15
Section: B2 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b2-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b2-cell709-valley-legacy.png

## Slide 39
B2 cell 709: Valley boundary, Adaptive
Notes: Source: b2-cases.pdf, page 16
Section: B2 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b2-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b2-cell709-valley-adaptive.png

## Slide 40
B2 cell 2118: Original boundary, Legacy
Notes: Source: b2-cases.pdf, page 17
Section: B2 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b2-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b2-cell2118-original-legacy.png

## Slide 41
B2 cell 2118: Original boundary, Adaptive
Notes: Source: b2-cases.pdf, page 18
Section: B2 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b2-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b2-cell2118-original-adaptive.png

## Slide 42
B2 cell 2118: Valley boundary, Legacy
Notes: Source: b2-cases.pdf, page 19
Section: B2 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b2-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b2-cell2118-valley-legacy.png

## Slide 43
B2 cell 2118: Valley boundary, Adaptive
Notes: Source: b2-cases.pdf, page 20
Section: B2 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b2-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b2-cell2118-valley-adaptive.png

## Slide 44
B2 cell 1287: Original boundary, Legacy
Notes: Source: b2-cases.pdf, page 21
Section: B2 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b2-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b2-cell1287-original-legacy.png

## Slide 45
B2 cell 1287: Original boundary, Adaptive
Notes: Source: b2-cases.pdf, page 22
Section: B2 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b2-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b2-cell1287-original-adaptive.png

## Slide 46
B2 cell 1287: Valley boundary, Legacy
Notes: Source: b2-cases.pdf, page 23
Section: B2 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b2-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b2-cell1287-valley-legacy.png

## Slide 47
B2 cell 1287: Valley boundary, Adaptive
Notes: Source: b2-cases.pdf, page 24
Section: B2 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b2-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b2-cell1287-valley-adaptive.png

## Slide 48
E1: check how general the improvement is
E1 cells 196 and 1348
Compare the same E1 channels with both numerical methods and both lower boundaries.
Look for agreement in peak location as well as differences in width and fit range.
These examples help test whether an improvement extends beyond the B2 spectra that motivated it.
Notes: Study context and observations are from this conversation and the supplied BNL plots. Plot slides retain their original source notes. Original-boundary and valley-boundary results are distinct campaigns. Selected events were inherited separately for Legacy and Adaptive in the valley campaign. This is a refinement study, not a rerun of all upstream stages with the new boundary.

## Slide 49
E1 cell 196: Original boundary, Legacy
Notes: Source: e1-cases.pdf, page 1
Section: E1 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/e1-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/e1-cell196-original-legacy.png

## Slide 50
E1 cell 196: Original boundary, Adaptive
Notes: Source: e1-cases.pdf, page 2
Section: E1 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/e1-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/e1-cell196-original-adaptive.png

## Slide 51
E1 cell 196: Valley boundary, Legacy
Notes: Source: e1-cases.pdf, page 3
Section: E1 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/e1-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/e1-cell196-valley-legacy.png

## Slide 52
E1 cell 196: Valley boundary, Adaptive
Notes: Source: e1-cases.pdf, page 4
Section: E1 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/e1-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/e1-cell196-valley-adaptive.png

## Slide 53
E1 cell 1348: Original boundary, Legacy
Notes: Source: e1-cases.pdf, page 5
Section: E1 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/e1-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/e1-cell1348-original-legacy.png

## Slide 54
E1 cell 1348: Original boundary, Adaptive
Notes: Source: e1-cases.pdf, page 6
Section: E1 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/e1-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/e1-cell1348-original-adaptive.png

## Slide 55
E1 cell 1348: Valley boundary, Legacy
Notes: Source: e1-cases.pdf, page 7
Section: E1 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/e1-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/e1-cell1348-valley-legacy.png

## Slide 56
E1 cell 1348: Valley boundary, Adaptive
Notes: Source: e1-cases.pdf, page 8
Section: E1 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/e1-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/e1-cell1348-valley-adaptive.png

## Slide 57
B1 controls: measure the cost of a change
B1 cells 704 and 1287
Compare B1 and B2 at the same channel identifiers to separate channel-specific and sample-specific behavior.
A well-behaved control should retain a plausible peak and stable refinement history.
Any systematic movement of H in these controls belongs in the calibration uncertainty study.
Notes: Study context and observations are from this conversation and the supplied BNL plots. Plot slides retain their original source notes. Original-boundary and valley-boundary results are distinct campaigns. Selected events were inherited separately for Legacy and Adaptive in the valley campaign. This is a refinement study, not a rerun of all upstream stages with the new boundary.

## Slide 58
B1 cell 704: Original boundary, Legacy
Notes: Source: b1-cases.pdf, page 1
Section: B1 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b1-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b1-cell704-original-legacy.png

## Slide 59
B1 cell 704: Original boundary, Adaptive
Notes: Source: b1-cases.pdf, page 2
Section: B1 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b1-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b1-cell704-original-adaptive.png

## Slide 60
B1 cell 704: Valley boundary, Legacy
Notes: Source: b1-cases.pdf, page 3
Section: B1 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b1-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b1-cell704-valley-legacy.png

## Slide 61
B1 cell 704: Valley boundary, Adaptive
Notes: Source: b1-cases.pdf, page 4
Section: B1 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b1-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b1-cell704-valley-adaptive.png

## Slide 62
B1 cell 1287: Original boundary, Legacy
Notes: Source: b1-cases.pdf, page 5
Section: B1 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b1-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b1-cell1287-original-legacy.png

## Slide 63
B1 cell 1287: Original boundary, Adaptive
Notes: Source: b1-cases.pdf, page 6
Section: B1 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b1-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b1-cell1287-original-adaptive.png

## Slide 64
B1 cell 1287: Valley boundary, Legacy
Notes: Source: b1-cases.pdf, page 7
Section: B1 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b1-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b1-cell1287-valley-legacy.png

## Slide 65
B1 cell 1287: Valley boundary, Adaptive
Notes: Source: b1-cases.pdf, page 8
Section: B1 interesting cases
Original source path: /workspace/scratch/973a74c46106/boundary-case-results-real/interesting-cases-pdfs/b1-cases.pdf
BNL source image: /gpfs/mnt/gpfs01/star/scratch/pnord/lfhcal/boundary-fullchains-20261002/interesting-cases/b1-cell1287-valley-adaptive.png

## Slide 66
What we’ve learned
Conclusions from the examples
The new boundary gives better fits in many of these examples.
Both Legacy and Adaptive still have troublesome cases.
More refinement steps do not always give a better answer.
A stable calibration can still come from a poor fit.
Notes: These are qualitative conclusions from the reviewed histogram overlays and convergence plots, not a measured success rate over every channel. Legacy with the new boundary remains a candidate. The B2 late-pass examples show why convergence and fit quality need separate checks. No claim of a universally best method is made.

## Slide 67
Flagging channels for review
A procedure for the full detector
With tens of thousands of channels, we need an automatic way to find the bad and funky ones.
Flag failed fits, large calibration jumps, and unusual spectra.
Show the histogram and fit overlay for human review.
Notes: Proposed next step: build an automated flagging procedure and review the flagged channels with their fit overlays. The thresholds and criteria still need study. Reports should distinguish fresh fits, carried-forward calibrations, and missing calibrations. This is a proposal, not a statement that the procedure is already implemented.
Detector scale: hundreds of thousands of physical scintillator tiles/SiPMs feed tens of thousands of summed readout channels. Do not equate tiles with calibration channels. The June 2026 LFHCal design uses eight longitudinal readout segments per tower; older seven-segment inventories should not be presented as a current exact total. Source: Emily Pottebaum, CALOR 2026, 1 June 2026, slides 12–23, https://zenodo.org/records/21478358 .

## Slide 68
What to try next
Proposed tests
Check how much the calibration changes when we move the fit range.
Understand how to handle undercounted and overcounted bins.
Remove the runs marked “dirty muon” and refit.
Compare with a few well-behaved channels as controls.
Notes: These are proposed tests, not results or jobs already submitted. Quantify calibration sensitivity to lower-edge selection, including shifts in well-behaved controls. Investigate the source and treatment of undercounted/overcounted bins before choosing a correction or masking procedure. For the dirty-muon test, compare the full sample with a refit excluding the labelled runs, keeping the fit procedure fixed. The label alone does not establish the cause of the difficult spectra. The test needs suitable inputs and run-level identification; availability must be checked because some pre-MIP files were missing.

## Slide 69
Appendix: the original F1 recipe
Recipe provenance • source links in notes
The dataset recipes came from Fredi’s calibration post and the 2026 test-beam helper scripts.
The original F1 Yallfile makes the processing order and DataPrep switches explicit.
The later Python runner organized the larger comparison campaigns.
ROOT fit functions and minimizer options are implemented inside DataPrep’s C++ routines.
Notes: Original F1 Yallfile: https://github.com/paulnord/epic-lfhcal-tbana/blob/yall-integration/examples/yall/fullset-f1-repro/Yallfile
Retrieved Yallfile blob SHA: f5d614d41f6d8de0f3dc311dbcfe42349e377859. The source is the original yall-integration F1 recipe, not the later Python campaign wrapper.
Implementation cross-check: https://github.com/paulnord/epic-lfhcal-tbana/blob/924ad82de6d150534b4d7684b5638df92c0a2016/NewStructure/DataPrep.cc
https://github.com/paulnord/epic-lfhcal-tbana/blob/924ad82de6d150534b4d7684b5638df92c0a2016/NewStructure/Analyses.cc
https://github.com/paulnord/epic-lfhcal-tbana/blob/924ad82de6d150534b4d7684b5638df92c0a2016/NewStructure/TileSpectra.cc
Specific acquisition run numbers intentionally omitted.
Fredi’s calibration post: https://indico.bnl.gov/event/34397/
F1 calibration presentation: https://indico.bnl.gov/event/34397/contributions/129732/subcontributions/4734/attachments/72620/124340/2026_SPS_Analysis_Status_FullSetF.pdf
Helper script: https://github.com/paulnord/epic-lfhcal-tbana/blob/924ad82de6d150534b4d7684b5638df92c0a2016/NewStructure/helperCalibHGCROC.sh
The post establishes the dataset recipe provenance. The exact commands here are grounded in the Yallfile and code, not claimed to be a command log of the published calibration PDFs.

## Slide 70
Original F1 Yallfile: the complete workflow
F1 sequence • run numbers omitted
Stage | Program / switches | Purpose
Convert | Convert -c -w | Decode raw data with mapping and run metadata
Merge | hadd -f | Combine the converted muon runs
Pedestal fits | DataPrep -p | Fit the pedestal spectrum and waveform baseline
Transfer | DataPrep -P -B -G | Attach pedestal, bad-channel map, and TOA offsets
Initial MIP | DataPrep -s | Estimate MIP scales and refit locally selected hits
Event selection | DataPrep -X | Skim events that contain a TOA signal
Refine 1–5 | DataPrep -S -x -k from refine 2 | Refit the selected sample with updated calibration
Final products | Copy refine 5 outputs | Copy final ROOT and text calibration files
Notes: Original F1 Yallfile: https://github.com/paulnord/epic-lfhcal-tbana/blob/yall-integration/examples/yall/fullset-f1-repro/Yallfile
Retrieved Yallfile blob SHA: f5d614d41f6d8de0f3dc311dbcfe42349e377859. The source is the original yall-integration F1 recipe, not the later Python campaign wrapper.
Implementation cross-check: https://github.com/paulnord/epic-lfhcal-tbana/blob/924ad82de6d150534b4d7684b5638df92c0a2016/NewStructure/DataPrep.cc
https://github.com/paulnord/epic-lfhcal-tbana/blob/924ad82de6d150534b4d7684b5638df92c0a2016/NewStructure/Analyses.cc
https://github.com/paulnord/epic-lfhcal-tbana/blob/924ad82de6d150534b4d7684b5638df92c0a2016/NewStructure/TileSpectra.cc
Specific acquisition run numbers intentionally omitted.

## Slide 71
F1 setup and event preparation
Original F1 recipe
Declare data, work, and eic-shell locations, plus mapping and run-database inputs.
Run through the eic-shell wrapper with ROOT and OpenMP restricted to one thread.
Create the output directories, then convert pedestal and muon data separately.
Merge only the muon files. Keep the dedicated pedestal sample for the pedestal task.
Yall dependencies connect each task to the files produced by the preceding tasks.
Notes: Original F1 Yallfile: https://github.com/paulnord/epic-lfhcal-tbana/blob/yall-integration/examples/yall/fullset-f1-repro/Yallfile
Retrieved Yallfile blob SHA: f5d614d41f6d8de0f3dc311dbcfe42349e377859. The source is the original yall-integration F1 recipe, not the later Python campaign wrapper.
Implementation cross-check: https://github.com/paulnord/epic-lfhcal-tbana/blob/924ad82de6d150534b4d7684b5638df92c0a2016/NewStructure/DataPrep.cc
https://github.com/paulnord/epic-lfhcal-tbana/blob/924ad82de6d150534b4d7684b5638df92c0a2016/NewStructure/Analyses.cc
https://github.com/paulnord/epic-lfhcal-tbana/blob/924ad82de6d150534b4d7684b5638df92c0a2016/NewStructure/TileSpectra.cc
Specific acquisition run numbers intentionally omitted.
Default task resources: 1 CPU, 4 GB memory, 8 GB disk, 2 h. Wrapper sets ROOT_MAX_THREADS=1 and OMP_NUM_THREADS=1. Convert command: Convert -d 0 -f -w -c INPUT -o OUTPUT -m MAPPING -r RUNDB. Merge command: hadd -f OUTPUT MUON_PARTS. Inputs are table-driven and include muon and pedestal rows.

## Slide 72
F1 pedestal step: two fits per channel
DataPrep -p • ROOT options live in C++, not in the Yallfile
Fit | Procedure | Saved information
Pedestal spectrum | Gaussian seed fit Repeat within mean ± 2σ ROOT option: QNSWW | Gaussian mean Gaussian width
Waveform baseline | Constant (pol0) over samples Rebin waveform Y axis by 4 ROOT option: QRMNE0 | Constant level Uncertainty on that level
The pedestal task writes calibration constants, histograms,
and diagnostic plots for the next stage.
Notes: Original F1 Yallfile: https://github.com/paulnord/epic-lfhcal-tbana/blob/yall-integration/examples/yall/fullset-f1-repro/Yallfile
Retrieved Yallfile blob SHA: f5d614d41f6d8de0f3dc311dbcfe42349e377859. The source is the original yall-integration F1 recipe, not the later Python campaign wrapper.
Implementation cross-check: https://github.com/paulnord/epic-lfhcal-tbana/blob/924ad82de6d150534b4d7684b5638df92c0a2016/NewStructure/DataPrep.cc
https://github.com/paulnord/epic-lfhcal-tbana/blob/924ad82de6d150534b4d7684b5638df92c0a2016/NewStructure/Analyses.cc
https://github.com/paulnord/epic-lfhcal-tbana/blob/924ad82de6d150534b4d7684b5638df92c0a2016/NewStructure/TileSpectra.cc
Specific acquisition run numbers intentionally omitted.
GetPedestal configures Minuit2/Migrad and calls FitNoise, followed by FitPedConstWave for HGCROC.
Gaussian: https://github.com/paulnord/epic-lfhcal-tbana/blob/924ad82de6d150534b4d7684b5638df92c0a2016/NewStructure/TileSpectra.cc#L276-L328
Waveform constant: https://github.com/paulnord/epic-lfhcal-tbana/blob/924ad82de6d150534b4d7684b5638df92c0a2016/NewStructure/TileSpectra.cc#L933-L972
FitNoise requires valid successful fits. The first QNSWW fit does not contain the R option, so the TF1 constructor interval must not be presented as an enforced first-fit range. FitPedConstWave accepts a valid result with status 0 or 4000, excluding values at the parameter limits. The pedestal routine can retain a channel when one of the two fits succeeds.
HGCROC stores the Gaussian mean/sigma in PedestalMeanH/PedestalSigH and the constant/error in PedestalMeanL/PedestalSigL. These slot names should not be interpreted as a second independent low-gain noise distribution.

## Slide 73
F1 transfer and initial MIP extraction
Original F1 recipe • helper-script modes and Yallfile agree
Operation | Switches | Effect
Calibration transfer | -P -B -G | Load pedestal constants, bad-channel map, and TOA offsets
Initial MIP extraction | -s | Fit the spectra and establish MIP calibration scales
Local muon refinement | Part of -s | Use local trigger information for a subsequent MIP fit
Calibration and plots | -a -e | Write text calibration and extended diagnostics
These are DataPrep switches. The ROOT fit options are set inside the fitting code.
Notes: Original F1 Yallfile: https://github.com/paulnord/epic-lfhcal-tbana/blob/yall-integration/examples/yall/fullset-f1-repro/Yallfile
Retrieved Yallfile blob SHA: f5d614d41f6d8de0f3dc311dbcfe42349e377859. The source is the original yall-integration F1 recipe, not the later Python campaign wrapper.
Implementation cross-check: https://github.com/paulnord/epic-lfhcal-tbana/blob/924ad82de6d150534b4d7684b5638df92c0a2016/NewStructure/DataPrep.cc
https://github.com/paulnord/epic-lfhcal-tbana/blob/924ad82de6d150534b4d7684b5638df92c0a2016/NewStructure/Analyses.cc
https://github.com/paulnord/epic-lfhcal-tbana/blob/924ad82de6d150534b4d7684b5638df92c0a2016/NewStructure/TileSpectra.cc
Specific acquisition run numbers intentionally omitted.
Pedestal invocation: DataPrep -a -d 1 -p -i INPUT -f -o OUTPUT -O PLOTS -r RUNDB -F pdf. Transfer invocation: DataPrep -d 1 -e -f -P PEDESTAL -i INPUT -o OUTPUT -O PLOTS -r RUNDB -B BADMAP -G TOAOFFSETS. Initial MIP invocation: DataPrep -a -f -d 1 -e -s -i INPUT -o OUTPUT -O PLOTS -r RUNDB.
-a writes text calibration, -e requests extended plotting, -f allows overwrite, -d controls diagnostic output, -O chooses the plot location. DataPrep -e is not the ROOT fit-option E.
The original F1 recipe does not enable the separate -D data-rejection option or -n pedestal re-evaluation option.

## Slide 74
F1 selection, refinement, and final outputs
Original F1 recipe
DataPrep -X writes a skim of HGCROC events with a TOA signal.
Refine 1 runs DataPrep -S -x using calibration already stored in that selected ROOT file.
Refine 2–5 read the same event file and load the preceding text calibration with -k.
-S updates the MIP calibration. -x suppresses writing another event tree. -a saves text constants.
The final task copies the refine 5 ROOT and text outputs. It does not perform another fit.
Notes: Original F1 Yallfile: https://github.com/paulnord/epic-lfhcal-tbana/blob/yall-integration/examples/yall/fullset-f1-repro/Yallfile
Retrieved Yallfile blob SHA: f5d614d41f6d8de0f3dc311dbcfe42349e377859. The source is the original yall-integration F1 recipe, not the later Python campaign wrapper.
Implementation cross-check: https://github.com/paulnord/epic-lfhcal-tbana/blob/924ad82de6d150534b4d7684b5638df92c0a2016/NewStructure/DataPrep.cc
https://github.com/paulnord/epic-lfhcal-tbana/blob/924ad82de6d150534b4d7684b5638df92c0a2016/NewStructure/Analyses.cc
https://github.com/paulnord/epic-lfhcal-tbana/blob/924ad82de6d150534b4d7684b5638df92c0a2016/NewStructure/TileSpectra.cc
Specific acquisition run numbers intentionally omitted.
Selection: DataPrep -f -d 1 -X -i INPUT -o OUTPUT. Refinement: DataPrep -x -a -f -d 1 -S -i SELECTED_ROOT -o OUTPUT -O PLOTS -r RUNDB, adding -k PREVIOUS_CALIB for passes 2–5.
The -X TOA skim is not a guarantee of a pure muon sample. Event-tree membership is fixed through refinement, while local trigger selection can change with the calibration. A new calibration is passed forward even though the event file is reused.