## Slide 1: AncASIC_XT011 MPW3 Submission for Fabrication and Overview 09/2026
G.W. Deptuch, gdeptuch@bnl.gov
ePIC SVT DSC meeting, 09/29/2026

## Slide 2: Where is AncASIC in the ePIC SVT Detector?

## Slide 3: AncASIC location w.r.t. MAPS sensors
FPC bridge direct connection to MOSAIX/EIC-LAS interface

## Slide 4: Physical connection to lpGBT
Summary of ePortTX.pptx / ePortRx.pptx functionality
where AC and DC coupling
    AC-coupled only to lpGBT (up-link and down-link), with coupling capacitors next to lpGBT
    DC-coupled down from first AncASIC in chain

## Slide 5: Fabrication Process and System Constraints
Parameter | Draft requirement / choice
Process | X-FAB XT011, 110 nm (BCD) Partially-Depleted Silicon-on-Insulator; Automotive quality with extended temperature range -40°C …. 175°C, tox for 1.5 V transistors 3.5nm/3.5nm; (Suitable for high currents in voltage regulation)
TID | Up to 10⁶ rad (1 Mrad)
NIEL | ≈10¹² neq/cm²
AncASIC maximum T | 80 °C
Maximum ΔT | 10 °C
Process: XT011A0770, 31+1 Mask Layers, 31+1 Process Layers
Modules: MOS5, METAL1, METAL2, MOSLP, LVT, DTI, PSUB, METAL3, METAL4, METAL5, COPTHK, ALUCAP + DEPL
400 nm
400 nm
400 nm
400 nm
400 nm
400 nm
3,740 nm
4.5 m Ω/□
62 m Ω/□

## Slide 6: Starting point fro September MPW
Single SLDO and single section NVBG prototypes fabricated on the MPW run in March 2025;
MPW2
MPW1
AncASIC = Interface chip
• Main functional blocks:
  • Shunt LDOs (SLDO) – MPW2
  • Negative Voltage Bias Generator (NVG) – MPW1
  • AncBrain: SC communication; operation heartbeat
Main addition in the MPW run in September 2026;
tactical objectives set at the Oxford ePIC SVT Working Meeting in Dec. 2025 achieved in MPW run September 2026

## Slide 7: Power Management

## Slide 8: Negative Bias Management
Negative bias for MAPS sensors referred to local ground,
The NVBG follows the sensor’s local ground; ground-level variation of order 6–8 V along the serial-powering chain.
NVBG block specifications / simulations
Parameter | Value reported in the draft
Supply | 1.2 V ±10% (provided by 1st SLDO)
Output range | <−1 up to −5 V relative to local ground; 0 V mode
Reference DAC | 8 bit for Vref
Output-current capability | ≈1 mA / section (6 sections: 1 Main + 5 Auxiliary) ; ≈200 µA nominal reference load/section
Output ripple | <0.15 mV; simulated
Power consumption | <15 mW; ≈11 mW at −1.5 V
Main charge pump | 16 selectable parallel branches / section
Status MPW2

## Slide 9: Anc Brain – Slow Control Management (1)
Bridge between lpGBT and sensor control and monitoring
The input e-link and the sensor-side slow-control link have different rates and formats.
Interfaces and protocol — system baseline
Interface / function | Specification
lpGBT grouping | One slow-control e-link per group of up to 4 EIC-LAS 16 groups possible, while planned 12
Group signals | Command input, status output and clock: 3 differential pairs
Sensor-side protocol | 5 Mbit/s, Manchester encoded
Transaction protection | 40-bit data frame; CRC-16 protected
Sensor-side functions | Global clock, reset and synchronization; service and core slow control
Local management
Sequence supplies
Enable the four sensor rails after AncBrain start-up.
Program power and bias
Set SLDO and NVBG operating parameters.
Monitor operating nodes
ADC monitoring and over-temperature protection.
Handle faults
Centralized error handler and watchdog supervision.
SINGLE-DEVICE INTERFACE
160 Mbit/s | 160 MHz
Rx/Tx e-links | common clock
One AncASIC connected to one lpGBT ePort
Orchestrate MAPS operation
Autonomous synchronization of Strobe sequences (delay, frequence, duration).
Program and monitor MAPS
Loads and reads configuration.

## Slide 10: Anc Brain – Slow Control Management
Scope: no watchdog, TMR or autonomous temperature shutdown is instantiated; the final daisy-chain wrapper is outside this core.
CONFIGURE
Set supply and substrate-bias levels;
write and read the sensor registers.
ACT
Generate delayed RESET / GCLK;
start periodic SYNC by broadcast.
OBSERVE & RECOVER
Capture ADC data; report faults;
issue commanded OCP-reset pulses.
Programmable settings plus hardware engines for sensor transactions, timing, ADC capture and fault reporting.

## Slide 11: AncASIC_XT011 sent for fabrication 09/2026
MPW run September 2026; expected delivery mid-February 2027; order 100 regular + 100 extra die
provides power, bias and slow control management for the two outer barrel layers and electron and hadron direction disks in the ePIC SVT detector, where serial powering has been adopted.
designed by the team of ASIC designers from BNL, RAL (UK) and LBL.
AncASIC_XT011
GSVDD
GSVDD
GSVDD
GSVDD
16,446.2 µm
2,626.2 µm

## Slide 12: Description of Pads
Pads on both short sides are mostly for debugging in the current version of the ASIC only

## Slide 13: AncBrain: In/Out Frame Definition (1)
68 – bit AncBrain frame; lpGBT transparent to transmitted data and its format

## Slide 14: AncBrain: In/Out Frame Definition (2)
40 – bit AncBrain internal payload format

## Slide 15: AncBrain: In/Out Frame Definition (3)
40 – bit MOSAIX interface payload format

## Slide 16: AncBrain: In/Out Frame Definition (4)
Outbound IDLE frame for improving DC balancing in natural transmission
65 60 59 56 55 54 53 14 13 6 5 0 +------------+--------------+----------+----------------------------------------------+-----------+------------+ | SOF (6b) | ModAddr (4b) | Type(2b) | 40-bit IDLE Payload | CRC (8b) | EOF (6b) | | 6'b011101 | module_id | 2'b11 | 36'hAAAAAAAAA + toggle_q (1b) + 3'b010 | CRC-8 | 6'b101110 | +------------+--------------+----------+----------------------------------------------+-----------+------------+ [0x1D] [chip_id] [RESERVED] [Alternates 0xAAAAAAAAAA / 0xAAAAAAAAA2] [CCITT-8] [0x2E]
Idle frames are generated when no other frame is ready for outbound transmission.
Transmission of IDLE frames is enabled by default on startup
  can be disabled by writing 0x00 to register 0x0B (TX_IDLE_CTRL)
IDLE frames take the lowest priority in the TX queue (Error > Core > IDLE)
  Error and Core packets preempt IDLE at the next available TX slot
IDLE frames are structured as follows:
  They can be filtered by Type field = 2'b11
  The Payload alternates between two 40b words to attempt a balanced 0,1 population (DC balancing)

## Slide 17: Summary of AncASIC submission Sept. 2026
BNL: Leonardo Cecconi, Grzegorz W. Deptuch, Dominik Gorni, Syed Hassan, Arif Iqbal, Soumyajit Mandal, Joao de Melo, Prafull Purohit, Nicholas St. John,
RAL: Iain Sedgwick, University of Oxford: Jaya John John, Roy Wastie,
LBL: Amanda Krieger
Area | Submitted / reported status | Remaining work / next implementation
Analog integration | Five SLDOs + NVBG; monitoring ADC, temperature sensor and BGR-based pre-regulators for ADC and integrated with SLDOs | Coexistence, ground bounce at variable load conditions of MAPS sensors, load changes and protection behavior to be tested
Communication / digital integration | One AncASIC ↔ lpGBT ePort; 160 Mbit/s e-links and 160 MHz clock | Daisy-chain wrapper: buffering, retiming and response arbitration
Radiation / faults | Pad-clamp issues in MPW2 corrected – new simplified and reliability pads conceived | Holistic confirmation of radiation hardness, SEE cross-section testing; logic triplication and non-maskable interrupt handling
Verification | Mixed-level verification advanced, | Complete models, FPC mock-up populated with AncASIC, operating procedures for SC for DAQ group and chip documentation

## Slide 18: AncBrain: Wrapper to enable daisy chaining
A system-integration layer for daisy chaining and DC-balanced transmission
FOUNDATION
Core control + single-device ePort interface
WRAPPER EXTENSION
Daisy-chain transport around the same core

## Slide 19: Shared design infrastructure
AncASICXT011_P1
AncASICXT011_P2
AncASICXT011_P3
AncASICXT011_E1
EIC_LASTPSCo_P1
EIC_LASTPSCo_P2
EIC_LASTPSCo_E1
GitHub Enterprise Cloud is FedRAMP-certified at the Low-impact level; use remains subject to institutional authorization and information-handling requirements.
Two collaboration platforms connected ASIC, providing shared design resources and traceable contributions across institutions.
  Keysight SOS (formerly Cliosoft) — design-data management integrated with CAD/EDA tools,
  GitHub Enterprise — controlled repositories for AncBrain RTL, verification, implementation scripts and documentation,
Established and maintained through BNL ITD,

## Slide 20: Backup

## Slide 21: Anc Brain – Registers: settings, actions and readback
67 defined byte addresses • 8-bit address + 8-bit data • Field widths below are in bits.
*ADC trims use 6 of 7 bits; CTR_VAL uses 7 of 8. SLDO EXT/SEL masks exist in the core but are unconnected.
ADC readback: read 0x53 before 0x54; reading 0x54 clears held data, valid and conversion enable. Error/overflow counters clear on write.

## Slide 22: AncBrain - wrapper