## Slide 1: Transmission Dynode LDRD
Sept. 30, 2026
B. Azmoun, A. Kiselev (BNL)

## Slide 2: Apparatus
Model
As Built (so far)
Laser
(free-space)
Dark box for beam steering optics
Vacuum vessel
Bellows beam conduit
Window replaced by gauge for testing

## Slide 3: Vacuum Vessel
Vessel
Dual gauge (for test only)
Ports for RTD & gas in/out valves
Vacuum manifold
Signal pins (DB25 x 2)
HV feed-thru (SHV x 8)
Dual gauge (permanent)

## Slide 4: Vacuum
RGA
Pressure gauges
No baking
Pump duration: 5days
Pressure: ~5E-8 Torr
Turbo pump

## Slide 5: RGA
Water is the dominant component of trace residuals

## Slide 6: Vessel layout
MgF2 window
Lid
HV pigtails bridge HV tabs to SHV feed-thru pins
Signal cables pass through bottom plate to feed-thru connector on rear
Ceramic detector fixture
Distance to window is adjustable

## Slide 7: Detector stack-up
Signal pins
Mesh PC (Al plated, 55% trans., 750lpi Ni /9µm LW, 2 x 5mm aperture )
Trans. Dynode / hole
MCP-1
MCP-2
Mesh Anode (~90% trans., 70lpi Ni mesh /19µm LW)
Readout PCB
Blue: HV contacts
Gray: Ceramic mounting fixture and spacers
Readout PCB
Dual 3 x 3 pixel array (dynode/hole)
Rogers 3000 (UHV)
UHV coax cable x 10 bundle w/pin connectors

## Slide 8: Procurement list
In hand:
MCP disks x2
Anode
PC (Al, Ni)
Dynode holder
HV contacts
Ceramic hardware
Standoffs
Vented screws
Purchase
Custom spring loaded HV contacts
Custom ceramic spacers and cradles
(machined in house)
Bottom plate
Fixture top

## Slide 9: High Energy Laser
266nm (4.7eV) YAG (4th harmonic)
4mJ/pulse, 10Hz max rep rate
4ns pulse width
Jitter: O(1ns)
Free-space beam (diam. ~3mm)
Use lens to focus/defocus beam onto target focal plane
Initial studies

## Slide 10: Femto-second Laser
Timing studies
780nm (1.6eV) Erbium doped fiber
(2nd harmonic)
0.63nJ/pulse, 50MHz max rep rate
<140fs pulse width
Jitter: O(100fs)
Fiber coupled beam
Use lens + collimator to focus beam onto focal plane
Exploit 3-photon absorption: 3 x 1.6eV = 4.8eV
(Al Work Fcn ~ 4.0 - 4.3eV)