## Slide 1
Operation Status and Upgrade Plan of the KOMAC Proton Irradiation Facility
Sang-Pil Yun, Young-Gi Song, Yu-Mi Kim, Jeong-Jeung Dang, Pil-Soo Lee, Hyeok-Jung Kwon
Korea Multi-purpose Accelerator Complex, Korea Atomic Energy Research Institute, Gyeongju, South Korea
Operation status of Proton irradiation Facility
Acknowledgement:
This work has been supported through KOMAC (Korea Multi-purpose Accelerator Complex) operation fund and the NRF grant (No. NRF-2017M2A2A6A02071070) by MSIT
Upgrade Plan
WAO18, 2018. 9.30 - 10.5
100MeV Linac of KOMAC and Beam Line
Features of KOMAC 100MeV linac
50-keV Injector (Ion source + LEBT) 3-MeV RFQ (4-vane type) 20 & 100-MeV DTL RF Frequency : 350 MHz Beam Extractions at 20 or 100 MeV 5 Beamlines for 20 MeV & 100 MeV
TR23: General purpose
TR101: RI production
TR103: General purpose
TR102: Low flux
In – air Irradiation
Mostly High Fluence & thin target (thin film, semi-conductor…)
Incident Proton Energy : 20 MeV
Available Proton Energy : 3 ~ 17.8 MeV
- adjusted by the distance beam window – target
- < 10 MeV not recommended due to energy spread
Typical Fluence : 1E10 ~ 1E14 [#/cm2]
- Limited by Air radio-activation
TR23 facility : general purpose
Beam window
Sample holder
Sample
Proton beam
In – air Irradiation (fixed position)
High Fluence & thick target
Incident Proton Energy : 102, 92, 81, 69, 57, 45, 33
Available Proton Energy : 100 ~ 20 MeV
- adjusted by the degrader
Typical Fluence : 1E11 ~ 1E15 [#/cm2]
- Limited by residual radio-activation
TR103 facility : general purpose
Beam window
TR102 facility : for low flux density
Collimator
& Degrader
Octupole
In – air Irradiation
Low Fluence & thick target
Incident Proton Energy : 102, 92, 81, 69, 57, 45, 33
Available Proton Energy : 100 ~ 20 MeV
- adjusted by the Al degrader
Typical Fluence : 1E5 ~ 1E8 [#/cm2]
Typical beam shape: square like
Typical Uniformity: < 10%, 100 mm X 100 mm
Low radio-activation : easy access
New experimental set-up
Beam window
Monitoring Instruments
: In-air ACCT
: MWPM, SWIC
Defining
Collimator
Ref. Dosimetry
: IC & FC
Test location
Test
Collimator
FC
Proton
Beam
Beam Quality Assurance
Instrument & Method
- Beam profile : Radiochromic film, 2D array IC, Flat Panel Detector
- Reference Dosimetry (fluence or dose): FC, IC, Radiochromic film
- Beam Energy: Range in Polycarbonate, MLFC
2D Array Ion Chamber
Radiochromic
film
: KOMAC provide 20 & 100 MeV proton beam through the 3 kind of irradiation facility
New control interface for proton irradiation
Analysis Software(by Matlab)
Typical
Beam Profile
Sample holder
Proton beam
Typical
Beam Profile
Proton beam
Typical
Beam Profile
MLFC
Ion chamber
Faraday cup
Peak Ch. : 80
 101.5 MeV
In-situ / real-time Beam monitoring
: Efficient beam tuning & QA
Dual Beam on / off system
: User can control the beam delivery
New united interface for beam instruments
: signal processing & storage by EPICS IOC
: Easy management of experimental data
Automation
: Auto beam cut off by the mechanical shutter
: remote control of the instruments in target room
Main Feature