## Slide 1
Operational Software Tools for the Injection Efficiency Improvement in the PLS-II
Mun Gyung Kim PAL
BNL/ Oct. 1, 2018
Workshop on Accelerator Operation in 2018

## Slide 2: Abstract
One of the main issues of the linac operation problems in the PLS-II is injection efficiency for top-up mode to keep radiation safety levels. The energy spread of the injection beam is the main beam parameter to effect injection efficiency. So we try to develop several operational software tools to reduce the amount of energy spread. And also beam energy jitter is another parameter for injection efficiency. We tried to develop related operational software tools about these parameters. So this report introduces these operational software tools

## Slide 3: PAL Overview: Chronology
I. PLS
  Project for 2.0 GeV 200 mA PLS started Apr. 1988
  Construction Start Apr. 1991
  User Service 2.0 GeV 180 mA Decay Op. Sep. 1995
II. 2nd Major Upgrade of the PLS (PLS-II)
  3.0 GeV PLS-II Upgrade Dec. 2011
  3.0 GeV 150 mA User Service Mar. 2012
  3.0 GeV 400 mA Top-up Operation July 2015
  * S.R. is a new machine, but linac is almost the same.
III. PAL-XFEL: Another Fancy Machine
  Government approval of PAL-XFEL project Jan. 2010
  Beam commissioning started April 2016
  User service started June 2017

## Slide 4
In normal operation
Top-up Current: 400 mA
Current Difference : 0.5 ~ 0.7 %
Duration Time: 190 sec
Injection Time: ~5 sec, 30 sec limit
Injection Charge: 50 ~ 60 pC
Injection Efficiency: 80 ~ 90 %
 | 10th, 2018 | 
 | Start | Average
Beam Energy (GeV) | 3.00 | 3.00
Beam Current (mA) | 400.2 | 399.8
Beam Size X (um) | 74.9 | 74.7
Beam Size Y (um) | 14.0 | 12.7
Tune X | 0.365 | 0.365
Tune Y | 0.145 | 0.145
rms X (um) | 0.163 | 0.134
rms Y (um) | 0.106 | 0.105
Injection Efficiency (%) | 90.2 | 86.4
Injection Charge (pC) | 54.5 | 55.4
Operation Parameters for users
Chart: Time
Operation Parameters

## Slide 5
Limit by PSI interlock system on the top-up mode for radiation safety
: Transfer to the decay mode operation in the case of three times under 50 %
- Keep below 3 uS / hour
- Distortion storage ring orbit status during injection by the injection transient of the kicker system
: Reduce the injection time as short as possible
Important of the Injection Efficiency

## Slide 6
The Effect of Injection Efficiency on Radiation
0
1
2
3
4
5
6
7
8
0
20
40
60
80
100
Injection Efficiency
(%)
Time(day)
0
1
2
3
4
5
6
7
8
0
5
10
15
20
Sum of the highest 3 radiation monitoring systems around injection area
(uS)
Time(day)
QD18 Failed
Full injection
MK trip in injection

## Slide 7
Injection Transient

## Slide 8
Injection Beam Energy Stability
: RF Power & Phase, Timing Jitter, LCW & Air temperature
Energy Spread
: Linac LCW & Air Temperature, RF power & phase, Preinjector Stability(MK01, Prebuncher, Buncher)
- Injection Trajectory & Lattice(Position, Angle, Size)
: Status of MPS, Gun, Preinjector
SR Beam Dynamic Parameters(especially related in SR RF, ID Gap)
Parameters Related to the Injection Efficiency

## Slide 9
LLRF
Layout of the PLS-II RF System
RF Phase State
1.1 ms
4.2 ms
0o
180o
120 kW
K1
800 W Peak
SSA
26.5 dB
W/G – Coaxial
Cross Coupler
BUN.
P.BUN
10 dB
Attenuator
Phase
Shifter
K2A
1&5/8”
Main Drive Line
3 dBm CW
(with PSK)
C2
16 dB
C12B
6 dB
K12B
2,856 MHz
Master Osc.
2 W CW
(w/o PSK)
GUN
7/8" Coaxial Phase Reference Line
Load
C9A
6 dB
C2
20 dB
C12B
6dB
C9A
10 dB
K9A
K2B
C3
12 dB
K3
K8
C3
15 dB
3 dBm CW
(w/o PSK)
Load
IPA
IPA
IPA
IPA
LLRF
SSA
20 dB
Attenuator
Phase
Shifter
A31
A32
A45
A46
A9
A10
A7
A8
A5
A6
A3
A4
A1
A2
SLED
SLED
SLED
SLED
SLED
2 W Pre-amp.
with PSK
Modulator-Klystron: 17 set
6 M-K sets with 4 acc., 11 M-K sets with 2 acc.
Accelerating Columns: 46 ea
Energy Doubler: 16 set

## Slide 10
RF & SLED Pulse Form
Energy & Energy Spread Instability Source
: RF Power & Phase Jitter, Timing Jitter

## Slide 11
QD01
QD02
BCM
LI#07
BPM
T01
ICT1
BT
GV1
BPM
T01
BPRM
No#04
(OTR)
ACC45
ACC46
MK12B
Phase Control
Beam Diagnostic Area
End of the Linac
Start of the Beam Transport Line
QD03
HB1
BTOTR2
HSLIT
BCM
BTL#1
BPM
T02
BPRM
No#5
Fast Closing
Shutter 2 ea
10o
180o
BAS3
BPRM
BAS3
BCM
BAS31
BPM
BAS3
7.5o
Designed for 2 GeV, 10o Beam
Non linear field for 3GeV, 10o Beam
Using on user serveice
Using on reference

## Slide 12
Energy Maximization Program at BAS3
Measure Reference Performances at BAS3 for Turn on
Find peak phase of energy maximum
Find equations related to energy and phase of all of M-K Modules.
Check additional amount of beam energy for energy feedback system
- Minimize Energy Spread (usually 0ff crest about -3o)
Use the equation of M-K12B:
to measure dispersion in the BTL,
to calibrate BPM02 and BTOTR2,
to measure linac energy stability
Purpose
Algorithm
Get beam energy by changing RF phase angle
Fit sine function with the data
Set phase angle on the crest
* It has some time to measure for whole phase
0
50
100
150
200
250
300
350
-200
-150
-100
-50
0
50
100
150
200
MK12B Phase-Energy Relaton
Klystron Phase Angle(degree)
Measured Energy (MeV)
155.0426sin(0.017821X + -0.75292)

## Slide 13
E (MeV) = 3280.5 – 7.540X for OTR peak energy
Energy Spread = 0.257 %/mm for OTR beam size
E (MeV) = 6.508X + 2956.5
Calibration Factor for BTL Diagnostics

## Slide 14
M-K Performance Analysis
MK01: measure at BAS1 not using energy maximizing program 1.
MK02A: Not possible cause of too low energy to transmit to the end of linac
Focusing on SLED Factor for performance check.
MKname | HV(kV) | Rfpower(MW) | Calc. Energy | Measure Energy | SLED Factor | Peak Phase | Res. Energy | Total Energy | Deviation to Avg.(%)
MK02B | 36.0 | 35.1 | 83.79 | 107.726 | 1.29 | 140.4 | 2911.23 | 3018.96 | -0.21
MK03 | 40.0 | 55.3 | 148.73 | 231.598 | 1.56 | 349.9 | 2792.83 | 3024.42 | -0.03
MK04 | 39.5 | 60.4 | 155.43 | 240.540 | 1.55 | 209.3 | 2781.73 | 3022.27 | -0.10
MK05 | 39.5 | 58.6 | 153.10 | 268.426 | 1.75 | 240.0 | 2755.75 | 3024.17 | -0.03
MK06 | 39.5 | 57.5 | 151.66 | 206.569 | 1.36 | 319.8 | 2824.23 | 3030.80 | 0.18
MK07 | 39.0 | 51.8 | 143.94 | 268.761 | 1.87 | 234.3 | 2768.99 | 3037.75 | 0.41
MK08 | 39.5 | 64.9 | 161.12 | 261.991 | 1.63 | 347.1 | 2756.88 | 3018.88 | -0.21
MK09A | 39.1 | 49.7 | 99.70 | 162.620 | 1.63 | 165.8 | 2857.78 | 3020.40 | -0.16
MK09B | 39.5 | 52.8 | 102.76 | 165.101 | 1.61 | 143.1 | 2860.10 | 3025.20 | 0.00
MK10A | 39.5 | 53.3 | 103.25 | 181.447 | 1.76 | 312.3 | 2846.61 | 3028.05 | 0.09
MK10B | 39.5 | 45.2 | 95.08 | 151.642 | 1.59 | 276.7 | 2874.08 | 3025.72 | 0.02
MK11A | 38.5 | 43.3 | 93.06 | 171.090 | 1.84 | 189.4 | 2846.40 | 3017.49 | -0.26
MK11B | 39.5 | 63.8 | 112.96 | 200.119 | 1.77 | 317.0 | 2833.65 | 3033.77 | 0.28
MK12A | 40.0 | 61.6 | 111.00 | 199.733 | 1.80 | 109.2 | 2822.80 | 3022.54 | -0.09
MK12B | 38.5 | 47.8 | 97.78 | 168.434 | 1.72 | 66.8 | 2859.25 | 3027.69 | 0.08

## Slide 15
Minimize Energy Spread
All of Phase On Crest
Off Crest about -3o

## Slide 16
Energy Maximization Program at BTL
It is possible to find peak phase at BPMT02 in user service
: Sometimes we have trouble in an MK module in user service
Reduce time to measure at BTL
Use 2nd order linear fitting instead of sine curve fitting at BTL
It is possible using linear magnetic field at BTL in change of small energy
Purpose
Old vr. of Energy maximize program (only at BAS3)
: It is possible for one stop process, but operators prefer to new one.
New vr. of Energy maximize program (possible at BPMT02)

## Slide 17
Energy Feedback Program
0
50
100
150
200
250
300
350
-200
-150
-100
-50
0
50
100
150
200
MK12B Phase-Energy Relation
Klystron Phase Angle(degree)
Measured Energy (MeV)
162.62sin(0.017302X + 0.91418) + 2833.91
Peak Phase = 37.6212
fitted curve

## Slide 18
 | mean | rms | rms Stability (%)
Linac Energy (MeV) | -9.35 | 10.00 | 0.333
BPMT02 (mm) | -0.03 | 0.33 | 
Injec Energy (MeV) | -0.20 | 2.15 | 0.072
Linac Energy Stability for 1 User Run

## Slide 19
Energy Spread Adjustment Program
If it happens something problem in machine status,
power, phase, temperature, ect., in most case electron beam confronts phase offset of RF wave in the accelerating columns. It makes some energy change and energy spread increasing. In that case, instead of solving machine problem, move all of RF phase all (except MK12B) with same amount to fit that effect. And adjust the change of linac energy with energy feedback program with MK12B phase
Assumption
0
50
100
150
200
250
300
350
-200
-150
-100
-50
0
50
100
150
200
Klystron Phase Angle(degree)
Measured Energy (MeV)
0
50
100
150
200
250
300
350
-200
-150
-100
-50
0
50
100
150
200
Klystron Phase Angle(degree)
Measured Energy (MeV)

## Slide 20
Energy Spread Control Program

## Slide 21
Energy Spread Adjustment
Chart: 
Phase
E Spread(%)

## Slide 22
Energy Spread Control for 1 User Run

## Slide 23
Efficiency vs Espread for 1 User Run
 | mean | std
Injection Efficiency(%) | 87.030 | 7.920
Energy Spread (%) | 0.057 | 0.019

## Slide 24
Beamline map: 34 Beamlines , 20 ID Beamlines
PLS-II Beamlines

## Slide 25
ID Gpas vs. Injection Efficiency

## Slide 26
SR RF Frequency vs. ID Gaps

## Slide 27
SR RF Frequency vs. Injection Efficiency

## Slide 28
Use several programs to optimize injection parameters.
It is possible to keep energy spread under 0.1 %
Improve injection efficiency up to 90%
As possible as try to add operator – friendly concepts
Summary

## Slide 29
Future Plan
- To improve control speed :
limited phase control speed in present
To be upgrade automation process in energy spread control program with plotting process
Try to search S.R. parameters to change optimized injection energy and to develop program to adjust that effect.

## Slide 30
Thank you