## Slide 1: Machine Learning @ SLAC
William Colocho, Matt Gibbs, Chris Zimmer

## Slide 2: Outline
A word on Automation and the need for Tuning at LCLS
Machine Learning for Particle Accelerators Workshop 2018
SPEAR3 and LCLS Applications
SLAC NAL science
Questions

## Slide 3: SLAC

## Slide 4: ML in Particle Accelerators: The Need to Tune
Complex beam parameter space with complex coupling between parameters, sometimes nonlinear responses.
Limited diagnostics
Time varying performance (Jitter, Drift, Reproducibility)
LCLS FEL require configuration changes for dedicated users: different charge, energy, pulse duration, undulator settings…
Different operating modes: twin bunches, two bunches , sliced bunch for two pulses
Restoring configurations does not restore performance  Tune.
For LCLS Tuning = Downtime

## Slide 5: The Need to Automate
https://xkcd.com/1319/
Free up person time for other tasks
Improve reproducibility of result
Reduce time to get task done
Let human concentrate on the hard problems
Measure effort of task
  Person hours per week
  Machine time
  Personnel training
  How to train with no access to machine
Predict effort of automation
  Development, Test, Deployment, Maintenance
  Risk of acceptance by humans
  Options when automatic system fails
  What is gained/lost by automation
General Approach
Notes: “Star” operator finding best performance (Lanny on damping rings tuning)

## Slide 6: Weekly ML Seminar @SLAC
https://confluence.slac.stanford.edu/display/AI/AI+Seminar

## Slide 7: Workshop
Agenda included:
ML Tutorial
Facility Needs (XFEL, LHC, Synchrotrons)
Tuning
Simulations and Modeling
Prognosis
Data Analysis
64 Participants
https://conf.slac.stanford.edu/icfa-ml-2018/

## Slide 8: Machine Learning
“An artificial neural network is an interconnected group of nodes, akin to the vast network of neurons in a brain.” Wikipedia
Prognostics
Optimization
Notes: Input: Pixel representation of a character; Output: Probability of being a letter “a”

## Slide 9: Example: Collimator alignment – Spike detection
A predefined threshold is selected such that when the losses exceed the threshold the collimator stops moving and the data must be analyzed for spikes
Courtesy: G. Azzopardi

## Slide 10: Collimation Alignment – Spike extraction
5 features extracted:
Collimator Position
Spike Height
3 parameters from exponential decay
Dataset used has about ~1500 samples (e.g. 80% training, 20% test)
Courtesy: G. Azzopardi

## Slide 11: Areas for potential ML applications – Anomaly detection for the cavity signals
Cavity fault detection requires: Ufor, Uref, Uprobe
Data rates to DAQ per cavity per pulse:
  2048 x 2 x 3 x 16bit = 24.6kB
  Pulses per Day = 864000
  700 cavities  604 Mio events/day
  Total data/day = 14.8 TB
Good statistics (ensemble & events)
Questions we like to address:
  How many cav./pulses behave normally
  Cav/Pulses out of nominal operation range
  Reliably quench detection and reaction
  Anomalies: due to parameter changes
  Anomalies: due to digital / communication/ readout

## Slide 14
5.5 KeV Self-seeding FEL
  More than doubled peak energy
  Zig-zag taper profile: ~ 1 mJ in 10 fs
Paper in preparation, 2017

## Slide 15: Model Independent Analysis of Beam Centroid Data
Based on principal component analysis and interpretation of SVD
Uses BPM data, mostly non-invasive
Tool to deduce lattice functions from jitter
Possibility to identify other physical functions
New tool to track reproducibility questions
Used to identify questionable BPMs and improve BPM resolution limit
Kick Analysis helpful to find kick sources.
W. Colocho

## Slide 16: OCELOT - DESY
Multiphysics simulation toolkit
Online control framework for FEL and storage rings based light sources
Open source (Python)
Modules for online beam control and machine performance optimization are available.
https://github.com/iagapov/ocelot

## Slide 17: Ocelot tuning @LCLS
Mitch McIntire
Mitch McIntire

## Slide 18: Ocelot
The one-sentence summary of Bayesian hyper-parameter optimization is: Build a probability model of the objective function and use it to select the most promising hyper-parameters to evaluate in the true objective function. https://towardsdatascience.com/a-conceptual-explanation-of-bayesian-model-based-hyperparameter-optimization-for-machine-learning-b8172278050f
1 - Probability model from:
Past performance data (now)
Genesis simulation (future)
Neural Net Prediction (future)
2 - Bayes Rule to Select next point

## Slide 19: Free Electron Laser Probability Model(s)
Mitch McIntire

## Slide 20: Ways to build a training model
Mitch McIntire

## Slide 21: Bayes Rule

## Slide 22: Ocelot Performance, May 2018
846 files in May (~9 per shift)
Mean scan time: 1.7 minutes
Mean scan gain: 

## Slide 23: Ocelot Performance, May 2018, 846 Scans
Gain / (Gain+Loss) in 0.012 mJ to 0.2 mJ window is
59%

## Slide 24: Neural Network + Extremum Seeking
http://ipac2018.vrws.de/papers/thygbe1.pdf
Transition to Operations planned for end 2018

## Slide 25: LINAC Coherent Light Source - FEL

## Slide 26: Catching Photosynthesis in the Act
“Photosynthesis is one of the most important chemical reactions on Earth, yet most aspects are not fundamentally understood. With the LCLS, researchers can directly observe the natural processes that convert the sun’s light into useable energy, with promising implications for America’s energy future.”

## Slide 27: Facility for Advanced Accelerator Experimental Tests
FACET: Scientists have shown that a promising technique for accelerating electrons on waves of plasma is efficient enough to power a new generation of shorter, more economical accelerators. This could greatly expand their use in areas such as medicine, national security, industry and high-energy physics research.

## Slide 28: Conclusion
There is a community interested in applying ML to accelerator challenges
ML techniques are beginning to be used at SLAC
At least one ML technique has been transitioned to operations at LCLS and SPEAR3

## Slide 30: References
https://www6.slac.stanford.edu/news/2018-04-13-scientists-use-machine-learning-speed-discovery-metallic-glass.aspx
https://www.energy.gov/eere/amo/articles/artificial-intelligence-future-new-materials-discovery
https://conf.slac.stanford.edu/icfa-ml-2018/
https://cds.cern.ch/record/2305965/files/tupha204.pdf
https://cds.cern.ch/record/2309558/?ln=en
https://confluence.slac.stanford.edu/display/AI/AI+Seminar
http://accelconf.web.cern.ch/AccelConf/ipac2017/papers/wepab031.pdf
http://ucanalytics.com/blogs/bayes-theorem-monty-hall-problem/