## Slide 1: Computing on GPUs Loren Schwiebert Department of Computer Science Wayne State University loren@wayne.edu
Jetscape Winter School 2018

## Slide 2: DESKTOP GPU – GTX 970
1664 Processor Cores
1050 MHz/1178 MHz Clock Rate
4 GB GDDR5 Memory
256-bit Memory Bus Width
224 GB/s Memory Bandwidth
List Price: $449 in Dec. 2017
13 Streaming Multiprocessors
Each has:
  128 Processor Cores
  32 Special Function Units
  64 KB of Shared Memory
  24 KB of L1 Cache
  64K 32-bit registers
  8 Instruction Issues/Cycle

## Slide 3: HIGH-END COMPUTE GPU – Kepler K40
2880 Processor Cores
745 MHz Clock Rate (+Boost)
12 GB DDR5
384-bit Memory Bus Width
288 GB/s Memory Bandwidth
List Price: $3400 in Dec. 2017
15 Streaming Multiprocessors
Each has:
  192 Processor Cores
  32 Special Function Units
  48 KB of Shared Memory
  16 KB of L1 Cache
  64K 32-bit registers
  8 Instruction Issues/Cycle

## Slide 4: MEMORY CONFIGURATION

## Slide 5
GPU VS. CPU FP PERFORMANCE

## Slide 6
GPU VS. CPU MEMORY BANDWIDTH

## Slide 7: GPU PROGRAMMING
CUDA: https://developer.nvidia.com/cuda-zone
  Programming API.
  NVIDIA GPUs only. Not an open standard.
  Offers many advanced features.
OpenCL: https://www.khronos.org/opencl/
  Open Standard.
  Also supports other multicore and many-core architectures: AMD-ATI GPUs, Xeon Phi.
OpenACC: https://www.openacc.org/
  Open Standard.
  Programming based on directives: #pragma

## Slide 8: GPU PROGRAMMING
A multi-threaded many-core model of computation
  Threads are lightweight processes
  Each thread solves part of the problem – data parallel apps
The threads can all run simultaneously – massively parallel
  You can create millions of threads
A grid contains all the threads
The grid is divided into blocks
Each block has many threads
  Each block runs independently
  Blocks are assigned to streaming multiprocessors (SM)
  Can have more than one block on the same SM
  Run as many blocks simultaneously as possible
Threads are grouped into warps

## Slide 9: THREAD MODEL
Block 1 Warps
…
t0 t1 t2 … t31
…
…
t0 t1 t2 … t31
…
Block 2 Warps
…
t0 t1 t2 … t31
…
Block 3 Warps
The Grid

## Slide 10
Consider three separate instruction streams on one streaming multiprocessor: warp1, warp3, and warp8
warp 8 instruction 11
warp 1 instruction 42
warp 3 instruction 95
warp 8 instruction 12
. . .
warp 3 instruction 96
t=k
t=k+1
t=k+2
t=n>k
t=n+1
Warp | Current Instruction | Instruction State
Warp 1 | 42 | Ready to write result
Warp 3 | 95 | Computing
Warp 8 | 11 | Computing
… |  | 
Schedule
at time k+1
WARP SCHEDULING EXAMPLE
OK, but why warps??
. . .

## Slide 11: IT’S NOT THIS

## Slide 12: AND IT’S NOT THIS

## Slide 13: IT’S THIS!

## Slide 14: CUDA
Acronym for Common Unified Device Architecture
  An API for General-Purpose GPU (GPGPU) Programming
Version 9.1 released in December 2017
  Runs on Linux and Windows
  Comes with Software Developer’s Kit – (Code examples)
Supports programming in C/C++ and Fortran
  Supports a large subset of C++
Includes additional functionality
  Debugging tools
  Mathematical libraries
  Image Processing libraries
  Deep Learning libraries
Its Free – See https://developer.nvidia.com/cuda-downloads

## Slide 15
CUDA PROGRAMMING
To call the GPU kernel, you call it like a function, but between the function name and the parameters, you enclose the number of blocks and number of threads per block in triple angle brackets <<< and >>>.
//The function call
Kernel<<<BlocksPerGrid, ThreadsPerBlock>>>(params);

## Slide 16
__global__ void compute(int *d_in, int *d_out, int *d_sum) {
d_out[threadIdx.x] = 0;
for (i=0; i<SIZE/BLOCKSIZE; i++) {
int val = d_in[i*BLOCKSIZE + threadIdx.x];
d_out[threadIdx.x] +=
compare(val, 6);
}
}
if (threadIdx.x == 0) {
for (i=0; i<BLOCKSIZE-1; i++)
*d_sum += d_out[i];
}
NEED TO MAKE SURE THINGS ARE DONE IN THE RIGHT ORDER
If there are two steps that share variables, we have to make sure that the first is done before the second starts.
This makes every thread in the block stop until all threads reach this point.
__threadfence();

## Slide 17: PERFORMANCE TIP #1
  Premature optimization is the root of all evil – Donald Knuth
“Maximize” Simultaneous Threads on each SM
SM Resource Bottlenecks
  Number of Registers
  Number of Threads
  Number of Blocks
  Shared Memory
Compile-Time Directives
  __launch_bounds__(Max Threads per Block, Min # Blocks)
  Advanced Idea

## Slide 18: PERFORMANCE TIP #2
  Coalesced Memory Accesses
Global Memory Accesses are Expensive
  Tens or hundreds of clock cycles
  Can access up to 128 consecutive bytes in one memory operation
  Combine reads/writes of threads to adjacent memory locations
Thread 0
Thread 1
…
Thread n-1
Option 1: Load elements
into shared memory
Option 2: Redistribute array elements

## Slide 19: CODING CONSIDERATIONS
Single Codebase Approach
  GPU Functionality Embedded in an Object-Oriented Framework
  Interface should remain consistent
  Multiple Parallel APIs could be supported
    CUDA, OpenCL, OpenMP, OpenACC, etc.
  #ifdef __NVCC__ … #endif
Gradual Implementation
  Simple loops with many iterations
  Compute intensive functions

## Slide 20
GPUs have a great deal of computing power
Software tools like CUDA, OpenCL, and OpenACC make GPUs easier to use for non-graphics apps
Performance depends on the GPU architecture
  Data parallel applications
  You have to think parallel
  You often need different algorithms
  At least, if you want to get good performance
Good performance is possible with some effort
SUMMARY

## Slide 21: THANKS!!!
For some of the Slides and Figures Courtesy of:
Mary Hall – University of Utah
NVIDIA Corporation Documentation

## Slide 22: QUESTIONS??
Picture courtesy of Google Images