## Slide 1
Simulation tools
and eRHIC detector geometry
for EIC VMP studies
Alexander Kiselev
“GPD studies with exclusive mesons at EIC” Workshop
Stony Brook University June,4-6 2018

## Slide 2: Outline
BeAST main detector geometry and modeling tools
eRHIC Interaction Region (IR) modeling environment ...
... and a couple of selected results
Outlook

## Slide 3: EicRoot framework in one slide
Interface to GEANT, ROOT, …
EicRoot
PandaRoot
FopiRoot
FairBase
“Ideal” track finder,
Interface to GenFit
…
TPC R&D stuff, …
eic-smear
MC generated evts import
Fast smearing codes
solenoid
modeling
CbmRoot
RICH stuff
IR design
configuration

## Slide 4: Available functionality
Flexible MC event import
Various generator ASCII output files (MILOU, PYTHIA, ...), binary formats: (TPythia, ...)
Vertex smearing, kinematics adjustment (22mrad crossing angle), ...
Modular geometry
Reasonably good track reconstruction ...
... and much less functional calorimetry codes
Several advances in the IR description
Main detector and forward-acceptance detectors are treated at once
Recoil proton goes to B0 silicon tracker or to the RPs
Scattered electron (& say p+p- pair) - to the main detector

## Slide 5: BeAST model detector in EicRoot
hadronic calorimeters
RICH detectors
silicon trackers
GEM trackers
3T solenoid cryostat
-3.5 < h < 3.5: Tracking & e/m Calorimetry (hermetic coverage)
magnet yoke
up to 9.0m
Micromegas barrels
TPC
e/m calorimeters
hadrons
electrons
Momentum resolution
An update incorporating IR vacuum system design is in progress

## Slide 6: Simulation usage options
-> MC points
simulation
digitization
PID; assembly
reconstruction
-> Hits
-> Tracks, clusters
-> Events
1) Download & compile EicRoot from scratch
2) Download pre-packaged EicRoot Docker container
3) Wait until “EIC Sandbox” framework grand-unification environment is set up
4) Use EIC smearing generator package (eic-smear) instead?
-> first version as early as June this year?

## Slide 7: EIC smearing generator
“Smearer” defines some element of performance
+ acceptance
Smearer
Smearer
Smearer
Smearer
Smearer
“Detector”
NOT a “physical detector”:
represents the overall performance in measuring a quantity.
  Built-in standard smearers provided with eic-smear
  Users can define own smearers using inheritance
  Apply all smearers to an MC event
  Yield smeared event
  Optionally recalculate derived values e.g x, Q2
Think of it as a parametric filter, which acts on imported MC events

## Slide 8: EIC smearing generator
Easy to install & use
No external dependencies other than ROOT
ASCII generator file import is readily available
The main idea: once detector acceptance regions and resolutions of kinematic variables are determined via complete GEANT simulation & subsequent reconstruction (by somebody else), for rough basic estimates it may suffice to use a collection of “parameterized detectors” rather than running the full simulations

## Slide 9: EIC smearing generator
Smearer:
Perform fast detector smearing
MC generator
ASCII output
Tree code:
Build ROOT tree containing events
Djangoh
PEPSI
Rapgap
PYTHIA
Milou
LEPTO
DPMJet
gmc_trans
Large number
of EIC Monte
Carlo generators
with standard
ASCII format
NB: both event import and smearing functionality is supported in EicRoot

## Slide 10: eRHIC IR hadron-going direction
Will focus on B0 magnet, RPs & ZDC
Back to the full GEANT simulations

## Slide 11: eRHIC IR simulation environment
Beam line element apertures and magnetic fields (.madx files)
Vacuum system engineering drawings (ground CAD .stp import)
Either boolean decomposition or STL->tetrahedrons dump or just a “ghost” shape
B0 large-acceptance dipole design (COMSOL .mphtxt import)
e
Q2E
Q1H
p
B0
Main tracker
B0 Si tracker
ROOT event display
Pump stand “ghost” volume

## Slide 12: Pt acceptance for DVCS protons
Gap between RP and B0 will be further optimized
Low-Pt part can be filled in with HA-running
achieve at least 0.3 GeV < pt < 1.3 GeV range
RP
B0
275 x 18 GeV
41 x 5 GeV
100 x 10 GeV
~10s away from beam line
first quad aperture & beam pipe
vacuum system ~20mrad cone
B0 Si tracker
20mrad vacuum pipe
vacuum chamber exit window
p
Q2E
B0
Plots: HD (high divergence) case

## Slide 13: Angular acceptance for charged tracks
~[ 0 .. 5] mrad: Roman Pots
~[ 5 .. 7] mrad: “gray zone”
~[ 7 .. 20] mrad: B0 forward large-acceptance spectrometer
~[20 .. 50] mrad: “gray zone”
From ~50 mrad or so (h ~ 3.5): main tracker

## Slide 14: Pt resolution for recoil protons
B0 magnet [100 GeV/c beam energy @ pt ~ 1.3 GeV/c (worst case)]
(~1.3T field, ~1.2m long; 4 Si stations with ~20mm resolution; Kalman fllter)
~30 MeV/c without IP vertex constraint
~15 MeV/c with reasonable assumptions about beam envelope size at the IP
Roman Pots [275 GeV/c beam energy]
(2 stations ~30m from IP, 20cm apart, ~20mm resolution; matrix transport)
~20 MeV/c at f ~ 0 degrees (recoil in horizontal plane)
~10 MeV/c at f ~ 90 degrees (recoil in vertical plane)
NB: these estimates do not include beam divergence at the IP

## Slide 15: Angular acceptance for neutrons
B0
Q2H
B1
B2A
Main tracker
p
Q1H
Q2E
Q3E
ZDC
e
NB: here particles generated flat in q
ZDC is handled as a “black hole” volume
Achieve the 4 mrad acceptance requirement
ACCEPTED
4mrad
NB: space for ZDC needs to be increased for better hadronic shower containment

## Slide 16: Summary & Outlook
Main detector geometry and IR geometry bits a pieces (basic vacuum chamber blocks, quad & dipole volumes, simplified magnetic fields, etc) can be imported in a full GEANT environment and used at once ...
... otherwise smearing generator fast simulation tool is available
Recently the GEANT codes were used for eRHIC IR design validation
Eventually: use unique source of geometry & other input info for
Physics simulations
Detector performance benchmarks
Beam-gas machine background studies
Synchrotron background studies
Neutron flux and radiation dose estimates