## Slide 1: Microphonics and Resonance Control from the Cryo-Mechanical Perspective
Based on the TTF-XFEL experience
Kay Jensch
Brooklyn, 25th October 2018

## Slide 2: Summary
01 Introduction
Microphonics VS vibrations
Vibrations in TTF (TESLA Technology Facility, e.g. FLASH,…..)
02 Main sources of microphonics
Mechanical design
Cryogenic
Vacuum
RF
03 Conclusions
Subheading, optional

## Slide 3: Introduction

## Slide 4: Microphonics or vibrations?
Is there any difference?
In the cryo and mechanical world we call them mainly vibrations
Wider range of amplitude
Looking mainly at low frequencies -> up to 100 Hz
Consider also very low frequency (<1 Hz)
Subheading, optional

## Slide 5: Vibrations in the TTF cryomodule design
TTF based accelerators @ DESY
FLASH (7 cryomodules, different design stages)
XFEL (97 cryomodules, final “evolution” of the TTF design)
Impact of vibrations
Not a primary issue for the RF control
  Pulsed machine, main detuning effect from Lorenz Force
At the early stage of the design (first FLASH modules)
  Stability concerns at the quadrupole -> possible alignment issue
  Possible effect of cryo-operation conditions
For the XFEL 1.3 km machine
  Concerns on the stability of the new hanging supports
 see Serena later today
Where did we cross them?

## Slide 6: Main sources of vibrations

## Slide 7: Main sources of vibrations
Environment
Ground vibrations
Surroundings -> highways, traffic, construction sites,….
Mechanical design
Resonances of subcomponents
Support system
Connections to the environment
In an accelerator environment
Cryogenics
Valves
Cryoplants
Vacuum
Pumps
Clean rooms
RF sources
Cooling system

## Slide 8: Environment

## Slide 9: The environment
Ground vibration
Can’t be change, once the site is chosen
Not constant, mainly daily fluctuations
Surroundings and occasional events
Highways, railroads, big cities, constructions
Earthquakes
Mitigation possible?
E.g. LCLS and ILC (Japan) build on one tectonic plate
From the vibration point of view

## Slide 10: Examples
Picture from N. Meyners
Von Sebastian Heimann, Institut für Geophysik; Universität Hamburg
1. earthquake
4. Concert (120bpm)
3. Building (stimulated by technic?)
2. Ocean Waves (4sec)
5. Human made (vertical Subway)
50sec
20sec
10sec
(Sonntag)
Sebastian Heimann

## Slide 11: Mechanical design

## Slide 12: A foreword: why do we need cryomodules?
Mechanically support the cavity string, allowing thermal shrinkage of parts from 300 K to 2 K without introducing stresses during cool down and warm up
Guarantee the cavity string alignment with a precision less than 0.5 mm
Supply the cavity string with 2 K liquid helium
Thermally isolate the cavity string at 2K from the 300 K environment
Bring high power RF to the cavity string (coupler)

## Slide 13: 1. Mechanical design
Sources of vibrations
Resonances of subcomponents
  Reduction -> e.g. optimize design with modal analysis
  Limitation -> cavity design optimized for performances, no much play
Position of the support “feet” and brackets
  Reduction -> e.g. move the components
  Limitation -> design to minimize movement of inner components (quadrupole/BPM)
Cavity supports
  Reduction -> e.g. make them as stiff as possible
  Limitation -> alignment requirements special for warm/cold
Module to module connection
  Reduction -> e.g. reduce coupling of vibration between consecutive components
  Limitation -> more complicated cryo destribution (e.g. valves, boxes, …..)
From the vibration point of view

## Slide 14: 1. Support of the cavity string
Cold Mass: includes all service pipes and the cavity string support structurs
Cavity-String: 8 SCRF cavities (with helium tank, 2 phase line, tuner with piezos,…, 1 quadrupole and 8 RF-cold couplers
Vacuum Vessel: Cold Mass with Cavity-String and on the outside 8 RF-warm couplers and the whole wave guide system

## Slide 15: 2. Support of the cavity string
The vacuum vessel is either hanging from the ceiling of the XFEL tunnel or supported on the floor in the AMTF a. CMTB
The cold mass is supported via the bracket + post assembly to the vacuum vessel. The center bracket is fixed to the vacuum vessel, while the 2 lateral ones are free to slide longitudinally, to allow the thermal shrinkage of the cold mass without introducing stresses.

## Slide 16: Examples: supports
FLASH – Ground
Support position
XFEL - Ceiling
AMTF a. CMTB
- Ground

## Slide 17: Examples: subcomponents
Coupling of modules
coupler modal analysis
inside and outside
Dressed XFEL Cryomodule:
Wave Guide System with Water Cooling, Cabling, Patch Panel

## Slide 18: Cryogenics

## Slide 19: The XFEL cryogenic system
A very quick overview
SC
SC
SC
SC
SC
SC
SC
SC
Distribution Box
DB54
Cold Compressors
CB44
Distribution Box
XLVB
XRTL
Cryo Plant
L1
L2
L3
Distribution Box
XLVB
Shaft
Distribution Box
XLVB
FB
CM
FC
EC
3,9 GHz
Injector
FB
CM
FC
EC
3,9 GHz
AMTF
Main Linac
XLTL1
XLTL3
XLTL2
CMS
FC
EC
CMS
FC
EC
CMS
SCB
EC
CMS
FC
SCB
Coldbox 41
Coldbox 43
Purifier XLTP
Distribution Box
XIVB
Warm
He-Pumps
cw-upgrade
Option

## Slide 20: 2K princip of XFEL
Coldbox and Cold Compressors are for standard 2K operation
Warm compressors are a backup -> only for the static losses
    Remark: The Test Benches and FLASH are operated only with warm compressors
Cold/Warm compressors is there an difference in case of vibration?
Cold and warm compressors
31mbar/2K return flow
1000mbar
Cold Compressors
CB44
Coldbox 41
Warm Compressors
1000mbar
JT-valve
2K-supply

## Slide 21: 2K-He for one cold string
Flow scheme for one cold string
JT-valves only in the boxes
Boxes directly attached to the modules
Vacuum pumps attached only to the boxes

## Slide 22: Main cryogenic components
High Pressure Compressors 300K/18bar
Cold Box Turbines
Cold Compressors 2K/31mbar
Warm Pressure Compressors 300K/31mbar
Valves
Flow meters
Bellows in the He circuits warm and cold
LHe-Heaters
From the vibration point of view

## Slide 23: Vacuum

## Slide 24: Main vacuum components
Pumps
Rotating components -> vibration source
Fundamental for beam and isolation vacuum -> Cannot be removed!
Mitigation:
  Isolating the supports from ground (like for the washing machine)
  Decouple: use flexible hoses, avoid direct connection to the module (boxes, transfer lines)
Clean rooms
Needed during assembly work
Mitigation:
  Can be turned off during vibration studies
  Can be a problem during preliminary studies
From the vibration point of view

## Slide 25: Examples
The XFEL vacuum pumps and the Injector clean room
XFEL Main Linac
XFEL Injector

## Slide 26: RF cooling

## Slide 27: Main RF cooling components
Water circuit
Cooled phase shifter support fixed at the cryomodules
Cooling water pumps
Mitigation:
  No support on the Cryomodules
  Isolating the supports from ground (like for the washing machine)
From the vibration point of view

## Slide 28: Examples
RF cooling system on the Cryomodules

## Slide 29: Conclusions

## Slide 30: Conclusions
Not an easy task?
Many sources, some can be reduced modified, but difficult to isolate
Many “interference” with other design requests
Not the typical experties in the cryo environment?
Usually affected by much slower events (see the 2KF pipe vibration in S. Barbanotti, later today)
Inter-group topic, need the close interaction of Cryo, Mechanical, RF, Control People
From the cryo - mechanical point of view

## Slide 31: Thank you

## Slide 32
Kay Jensch
MKS1
Kay.Jensch@desy.de

## Slide 33: Backup Slides

## Slide 34: 2. Guarantee string alignment (1/2)
Only one fixed point: the middle post (no stresses due to shirinkage)
Coupler longitudinal flexibility (in the mm range)
Cavity string fixed to an invar bar (integral shrinking coefficient 300 K – 2 K = 0.04 mm/m)
Pins between GRP and post and post and brackets, to reproduce exact position after multiple assemblies
Cavity string support system with rollers: very low friction

## Slide 35: 2. Guarantee string alignment (2/2)

## Slide 36: 4. Thermally isolate the cavity string
Design of the support post: - thin pipe of G10 material to reduce conduction; - shirink-fit assembly tecnique to guarantee strength
Thermal intercepts at 4K and 80K to readuce direct conduction 2 K -> 300 K
Multi Layer Insulation (MLI)
Image cortesy of N. Ohuchi

## Slide 37: Inside a cryomodule
A cryomodule has 3 main components
Cold mass: includes all the service pipes, and the cavity string support structure
Cavity string: 8 SCRF cavities (with helium tank, 2 phase line, tuner, … ), 1 quadrupole and 8 couplers
Vacuum vessel

## Slide 38: Let‘s see a bit more inside…
BPM + magnet + gave valve unit

## Slide 39: Let‘s see a bit more inside…
The cavity hanging system:
Post, brackets and GRP with C-clamps

## Slide 40: Let‘s see a bit more inside…
The cavity supports

## Slide 41: Let‘s see a bit more inside…
Thermal shields

## Slide 42: Let‘s see a bit more inside…
Cross section of the piping