## Slide 1: Superconducting radio-frequency virtual cavity for Hardware-In-the-Loop testing
J. Jugo1
P. Echevarria2, E. Aldekoa1, J. A. Neumann2, A. Ushakov2, J. Knobloch2, I. Badillo1
        (1) University of the Basque Country (UPV/EHU) , (2) Helmholtz Zenrtrum Berlin
Science And Technology Faculty
LEIOA
GAUDEE Research group
Experimental Automatic Control
Second Topical Workshop on Microphonics, LLRF Workshop Series
24-26 October 2018

## Slide 2: Superconducting radio-frequency virtual cavity for HIL testing Outline
Introduction
  Collaboration between HZB and UPV/EHU
FPGA based simulator for SRF cavities
Hardware-In-the-Loop testing: microphonics
Conclusions and future work

## Slide 3: Superconducting radio-frequency virtual cavity for HIL testing Introduction
Collaboration between HZB and UPV/EHU
- SRF Cavity simulator, initially developed in HZB
- Microphonics compensation algorithms studies
- RF phase drifts compensation techniques
- Experimental vibration mode determination
– Mechanical transfer function fitting
Helmholtz Zentrum Berlin, internationally recognized research center, operating two large scientific facilities, BER II and BESSY II
University of the Basque Country (UPV/EHU) Laboratory of accelerator technology (IZPIlab)
in the field of LLRF control since December 2016
Collaboration topics:
Experience in modeling and control of electromechanical systems
Erasmus+ stays in HZB:
Graduate and Post Graduate students from the UPV/EHU

## Slide 4: Superconducting radio-frequency virtual cavity for HIL testing Introduction
Collaboration between HZB and UPV/EHU
- SRF Cavity simulator, initially developed in HZB
- Microphonics compensation algorithms studies
- RF phase drifts compensation techniques
- Experimental vibration mode determination
– Mechanical transfer function fitting
Helmholtz Zentrum Berlin, internationally recognized research center, operating two large scientific facilities, BER II and BESSY II
University of the Basque Country (UPV/EHU) Laboratory of accelerator technology (IZPIlab)
in the field of LLRF control since December 2016
Collaboration topics:
Experience in modeling and control of electromechanical systems
Erasmus+ stays in HZB:
Graduate and Post Graduate students from the UPV/EHU
First Collaboration Result:
Superconducting radio-frequency virtual cavity for control algorithms debugging
P. Echevarria, E. Aldekoa, J. Jugo, A. Neumann, A. Ushakov, J. Knobloch,
Review of Scientific Instruments, Volume 89, Issue 8 ,(2018)

## Slide 5: Superconducting radio-frequency virtual cavity for HIL testing FPGA based simulator for SRF cavities
Simulator for SRF cavities
Main purpose: Hardware-in-the loop prototyping
- Test of different LLRF control techniques
- Microphonics compensation algorithms studies
Example in this session :
Control system design for SRF cavity based on Kalman Filter observer
Andrey Ushakov

## Slide 6: Superconducting radio-frequency virtual cavity for HIL testing Outline
Introduction
  Collaboration between HZB and UPV/EHU
FPGA based simulator for SRF cavities
Hardware-In-the-Loop testing: microphonics
Conclusions and future work

## Slide 7: Superconducting radio-frequency virtual cavity for HIL testing FPGA based simulator for SRF cavities
Implementation details
LabVIEW based using PXI and FlexRIO technology
Reconfigurability
Rapid prototyping
Compatible with the technology used in la UPV/EHU lab
Image: From National Instruments

## Slide 8: Superconducting radio-frequency virtual cavity for HIL testing FPGA based simulator for SRF cavities
Implementation details
Communication between host (LabVIEW APP) and FPGA -> DMA based FIFO
Computation clock (FPGA) , 10MHz
Sampling clock (ADC) , 100MHz
LabVIEW based using PXI and FlexRIO technology
Reconfigurability
Rapid prototyping
Compatible with the technology used in la UPV/EHU lab

## Slide 9: Superconducting radio-frequency virtual cavity for HIL testing FPGA based simulator for SRF cavities
Implementation details: cavity model
  Electric part model
  Lorenz force detuning + microphonics effects
  Mechanic part model

## Slide 10: Superconducting radio-frequency virtual cavity for HIL testing FPGA based simulator for SRF cavities
Implementation details: GUI
Host VI
Electric model parameters
Mechanical model parameters
Non linear effects
  Q slope
  Quench

## Slide 11: Superconducting radio-frequency virtual cavity for HIL testing FPGA based simulator for SRF cavities
Individual functionalities
  Electric model
  Mechanic model
  Microphonics
  Lorenz Force Detuning
Full model
Extensive simulation tests
Test of TESLA (9 cells) cavity voltage with different

## Slide 12: Superconducting radio-frequency virtual cavity for HIL testing FPGA based simulator for SRF cavities
Individual functionalities
  Electric model
  Mechanic model
  Microphonics
  Lorenz Force Detuning
Full model
Test of TESLA (9 cells) cavity:
    Amplitude and phase with different detuning
Extensive simulation tests
Results from Eukeni Aldekoa’s Master Degree

## Slide 13: Superconducting radio-frequency virtual cavity for HIL testing FPGA based simulator for SRF cavities
Individual functionalities
  Electric model
  Mechanic model
  Microphonics
  Lorenz Force Detuning
Full model
Test of TESLA (9 cells) cavity:
    Detuning effect observed in the oscilloscope
Extensive simulation tests

## Slide 14: Superconducting radio-frequency virtual cavity for HIL testing FPGA based simulator for SRF cavities
Host VI
Modelo eléctrico
Modelo mecánico
Efectos no-ideales
  Q slope
  Quench

## Slide 15: Superconducting radio-frequency virtual cavity for HIL testing Outline
Introduction
  Collaboration between HZB and UPV/EHU
FPGA based simulator for SRF cavities
Hardware-In-the-Loop testing: microphonics
Conclusions and future work

## Slide 16: Superconducting radio-frequency virtual cavity for HIL testing HIL testing: microphonics
- Amplitude and phase
- Resonance frequency
      Feedforward  LFD
HIL testing of control techniques, possibilities
and microphonics?
- Test of different disturbances:
  impulse, step, sinusoidal signals, white noise

## Slide 17: Superconducting radio-frequency virtual cavity for HIL testing HIL testing: microphonics
Analysis and active compensation of microphonics in continuous wave narrow-bandwidth superconducting cavities
A. Neumann, W. Anders, O. Kugeler, and J. Knobloch
PHYSICAL REVIEW SPECIAL TOPICS - ACCELERATORS AND BEAMS, 13
Motivation

## Slide 18: Superconducting radio-frequency virtual cavity for HIL testing HIL testing: microphonics
New functionalities: Piezoelectric actuator model
  New possibility: HIL testing of control techniques against microphonics effect
Piezoelectric actuator model (discrete version)
New possibility: HIL testing of control techniques against microphonics effect

## Slide 19: Superconducting radio-frequency virtual cavity for HIL testing FPGA based simulator for SRF cavities
Initial pure simulation test
- Amplitude and Phase control
- Feedforward control for LFD
– Active vibration control
Matlab/Simulink

## Slide 20: Superconducting radio-frequency virtual cavity for HIL testing FPGA based simulator for SRF cavities
Initial pure simulation test
- Amplitude and Phase control
- Feedforward control for LFD
– Active vibration control
Matlab/Simulink

## Slide 21: Superconducting radio-frequency virtual cavity for HIL testing FPGA based simulator for SRF cavities
Initial pure simulation test
- Amplitude and Phase control
- Feedforward control for LFD
– Active vibration control
Matlab/Simulink
Active control using adaptative feedforward
algorithm

## Slide 22: Superconducting radio-frequency virtual cavity for HIL testing FPGA based simulator for SRF cavities
Active control using adaptative feedforward algorithm
Transmitted voltage:
Amplitude (V)
Phase (º)
Results from Eukeni Aldekoa’s Master Degree

## Slide 23: Superconducting radio-frequency virtual cavity for HIL testing Outline
Introduction
  Collaboration between HZB and UPV/EHU
FPGA based simulator for SRF cavities
Hardware-In-the-Loop testing: microphonics
Conclusions and future work

## Slide 24: Superconducting radio-frequency virtual cavity for HIL testing Conclusions and future work
Reconfigurable simulator
    FPGA: real time.
    Realistic functionalities
      Reflected wave, Quench, LFD, some disturbances
      Piezoelectric actuator
Applications
    HIL Simulations
    Teaching
    Kalman filter debugging
Microphonics: Future improvements
    HIL test of active control techniques
    New disturbances simulated and real
    Non colocated control