## Slide 1: Potential Application of Advance Control Algorithm for Fast Tuner Control
Shen Zhao Low Level Radio Frequency Team Leader

## Slide 2: Outline
Tuner Types
Control Strategy
  PID
  Observer based control
Simulation Study
  Model
  Results
  Parameter tuning
Summary

## Slide 3
Slow Tuner vs. Fast Tuner
Piezo Tuner
  Pros:
    Fast response
    Fine resolution
 | Slow Tuner |  | Fast Tuner
Frequency Range | < 1 Hz |  | > 10 Hz
Tuner Types | Stepper Pneumatic Temperature |  | Piezo Variable reactance
Detuning Sources | Bath pressure variation |  | Microphonics Lorenz force detuning
  Cons
    Hysteresis
    Creep
    Nonlinear gain

## Slide 4: Control of Choice
Category | Analysis Method | Method | Model Dependency | 
Classical Control Theory | Frequency Domain (TF) | PID Lead-lag compensator Loop-shaping | No System TF System TF | 
Modern Control Theory | Time Domain (SS) | State observer Disturbance observer | Yes Yes / No | Advanced control?
Other |  | Robust control Adaptive control Fuzzy logic Neural network … | Yes Yes No No | 

## Slide 5
PID Controller
Pros
  Simple structure
  System can be treated as black box
  Only three parameters to tune
  Transfer function analysis
Cons
  One degree of freedom
    Tracking y(s) / r(s) => 1
    Disturbance rejection y(s) / d(s) => 0
  Ignoring knowledge of system
  Performance
C(s)
G(s)
r
y
di
do
G-1(s)
+
-
+
+
+
+

## Slide 6
Observers
  Luenberger observer
    Estimate system states
  Unknown input observer
    Estimate external disturbance
  Extended state observer
    Estimate external disturbance and unknown dynamics
Equivalent Transfer Function Representation
  Two degree of freedom
  Observer performance determines disturbance rejection performance
  Controller performance determines tracking performance
Reference
Observer
Observer based Control

## Slide 7
Simulation Model
Notes
  Hysteresis is treated as disturbance and its effect is estimated by the ESO (z2) and then cancelled in the controller
  The ESO does not include any model information of the hysteresis; the estimation performance is mainly determined by the observer bandwidth, which is limited by sampling rate and noise level.
ADRC
Hysteresis
30 Hz

## Slide 8: Simulation Results
The nonlinear effect of the hysteresis will distort the perfect sinusoidal input and create higher order harmonic components in the system output.
With feedback control, the third harmonic in the system output signal is greatly suppressed.
residue nonlinear effect

## Slide 9
Parameter Tuning
Parameters | Case #1 | Case #2 | Case #3 | Case #4
Sine Wave Frequency (Hz) | 30 | 60 | 60 | 60
Controller Bandwidth (rad/s) | 2000 | 2000 | 2000 | 4000
Observer Bandwidth (rad/s) | 10000 | 10000 | 20000 | 10000
Tracking Error (%) | 10 | 20 | 19 | 10

## Slide 10
Summary
Traditional PID controller is still dominant, but performance may be limited for challenging problems
The disturbance observer based control design may be an effective solution to deal with the hysteresis effect in the piezo fast tuner
Looking for collaborations if interested