## Slide 1: CW studies at DESY’s cryomodule test bench.
R&D effort towards continuous wave operation of the European XFEL
Julien Branlard, for the LLRF team
New York City, 25.10.2018

## Slide 2: CW studies at CMTB
CW upgrade of the European XFEL
Feasibility study
Possible beam energy = 8 GeV
CW in addition to pulsed mode
Long pulse also an option
Motivations for CW
Collaboration with other Helmholtz institutes (Germany)
HZDR (Dresden)
  ELBE: SRF FEL
  Single cavity regulation LLRF system
  Shared, HW, FW, server development
  Possibility to test with beam
HZB (Berlin)
  bERLinPro: SRF ERL
  BESSY-VSR, storage ring
  LLRF, single cavity regulation
  Shared, HW, FW, server development
Accelerator R&D program funded by Helmholtz
Talks tomorrow by
A. Neumann and P. Echevarria

## Slide 3: CW studies at DESY
Simple overview
CW studies
High QL
CW RF source
Vector sum operation
Microphonics
Q0 and dynamic heat load
CW SRF gun
Single cavity operation
CW cryomodule
…
Coupler modifications
What QL can be achieved?
What’s reasonable?
Thermal effects?
What are the sources?
Cavity transfer function?
Passive, active compensation
Piezo feedback
Is large grain important?
Nitrogen infusion
Operation at 1.8K? at 1.6K?
High QL, high gradient
Lorentz force detuning
Static drops
RF controls
100 kW IOT
Linearization
Transients
Larger 2 phase return pipe
CW cavities
Are microphonics an issue?
New SRF design
Avoid cathode exchange
Next talk (Wojtek C.)
This talk
High QL, high gradient
Lorentz force detuning
Static drops
RF controls

## Slide 4: OUTLINE
Microphonics and cavity modes measurements
With piezo, with RF
Frequency and stability analysis
Suppression of microphonics
Active noise cancellation
Automation of parameter optimization
Microphonics in the scope of CW studies at DESY
Lorentz Force detuning and microphonics
Static drops
Piezo feedback
Outlook
Summary
Future tests at CMTB

## Slide 5: Microphonics measurements
Sources of microphonics
Natural vibrations (i.e. earthquakes)
Human factors (i.e. trucks, foot steps)
Accelerator operation (i.e. pumps, cryo bath)
  RF
  Piezo
Measuring microphonics
With beam
With external sensors (i.e. accelerometers)
With internal sensors (i.e. piezo)
With RF (i.e. cavity probe)
For particle accelerators

## Slide 6: Measuring cavity mechanical modes
Measurement
RF is off
Excite piezo with sine waveform
2 periods at 300 Hz
FFT of piezo sensor waveform
Outcome
Dominant resonant modes are found
Here XFEL cryomodule ~ 260 Hz
Transfer function: piezo  piezo
Courtesy A. Bellandi

## Slide 7: Measuring cavity mechanical modes
Measurement
RF is on
Excite piezo with sine waveform
FFT of RF phase waveform
Sweep sine frequency
Outcome
Dominant resonant modes are found
Here XFEL cryomodule ~ 260 Hz
Transfer function: piezo  RF
Courtesy A. Bellandi
260 Hz

## Slide 8: Measuring microphonics – with RF
Measurement:
RF is on, different gradients
FFT of cavity RF phase signal
Outcome
CMTB: main freq: 30 Hz, 49 Hz (well known)
Independent of gradient
As a function of gradient
Courtesy A. Bellandi

## Slide 9: Measuring microphonics – without RF
Measurement
XM-3 at CMTB
Data taken with piezos
FFT amplitude of piezo sensor
Spectrogram over 1 day
Outcome
Stable background conditions (in this example)
As a function of time
FFT amplitude [a.u.]
Courtesy A. Bellandi

## Slide 10: Measuring microphonics – with RF
Measurement
XM-3 at CMTB
Data taken with RF
FFT amplitude of probe phase
Spectrogram over 1 day
Outcome
Stable background conditions (in this example)
As a function of time
Courtesy A. Bellandi
[deg]
IOT OFF (interlock)

## Slide 11: Microphonics suppression
Source of microphonics
Main contributor are vacuum pumps (essential for operation)
Dominant frequencies around 30 Hz and 49 Hz for most cavities
Impact increased with higher QL
Microphonics suppression
Active Noise Cancellation (ANC) techniques were applied to notch these frequencies (adjusted for individual cavities)
> 20 dB suppression can be achieved
Using Active Noise Cancellation (ANC) techniques
Courtesy A. Bellandi
Reference: R. Rybaniec et al. “FPGA-Based RF and Piezo controllers for SRF Cavities in CW Mode”, IEEE TRANSACTIONS ON NUCLEAR SCIENCE, VOL. 64, NO. 6, JUNE 2017

## Slide 12: ANC: power consumption
The impact of noise cancellation on forward power
Courtesy A. Bellandi
ANC also helps with power consumption
Gradients between 6 MV/m and 13 MV/m
ANC decreased the power consumption by 6% to 12%
For low gradients the consumption for the ANC measurements approaches the theoretical minimum value

## Slide 13: ANC: parameter optimization
x800 for XFEL !
Courtesy A. Bellandi
ANC optimization
Done manually  not scalable
Based on experience
Likely change with time
Automation
First attempt
  Bayesian optimization algorithm
  Time consuming
  Positive outcome but not as optimal as manual tuning
Work on-going
  Improve optimization algorithm
  Improve ANC scheme to include microphonics measurements

## Slide 14: Microphonics and LFD
1 / 3
Microphonics can/will make the cavity experience a static drop
Effect is worsened for higher QL and higher gradients

## Slide 15: Microphonics and LFD
2 / 3
Microphonics can/will make the cavity experience a static drop
Effect is worsened for higher QL and higher gradients
Courtesy A. Bellandi

## Slide 16: Microphonics and LFD
Microphonics can/will make the cavity experience a static drop
Effect is worsened for higher QL and higher gradients
In practice, piezo integrator feedback works against this effect
Choose your working point wisely
3 / 3
phase set point

## Slide 17: Microphonics and LFD
Microphonics can/will make the cavity experience a static drop
Effect is worsened for higher QL and higher gradients
In practice, piezo integrator feedback works against this effect
Choose your working point wisely
3 / 3
phase set point

## Slide 18: Cavity tuning
What the cavity phase spectrum can tell you
Static drop
Courtesy A. Bellandi
forward scan
[ deg ]
Frequency [ Hz ]
Microphonics: 49 Hz and harmonics
Cavity main mechanical mode: 260 Hz
Piezo DC bias
Cavity RF resonance peak

## Slide 19: Summary
Understand microphonics signature and how to measure them
Characterize the cavity/tuner mechanical transfer function
Good results in CW in terms of
  RF stability (0.01%, 0.01 deg.)
  At high QL (6-8x107)
  At high gradient (>20 MV/m)
BUT
Understand the limitations and how to go beyond
Limitations of current active noise compensation approach (ANC)
  Automate settings
  Scale to 800 cavities
  Adapt settings to changing environment
On going work towards CW operations
Next talk by W. Cichalewski

## Slide 20: Summary
Upcoming tests at CMTB
XM50 and XM46
XFEL series cryomodules
Modified with extended iso-vac flange for higher QL
Difference with XM-3 (fine versus large grain, series versus prototype)
What heat load / Q0 to expect
Extremely relevant for a CW upgrade of the XFEL (main linac)
On going work towards CW operations
Courtesy D. Kostin

## Slide 21
Julien Branlard
MSK
julien.branlard@desy.de
+49 (0) 40 8998 1599
Thank you for your attention!
Special thank to my CW colleagues at DESY
Valeri Ayvazyan, Andrea Bellandi, Wojciech Cichalewski, Jürgen Eschke, Çagil Gümüş, Denis Kostin, Rüdiger Onken, Sven Pfeiffer, Konrad Przygoda, Jacek Sekutowicz, Christian Schmidt

## Slide 22: BACK UP SLIDES

## Slide 23: MOTIVATION FOR CW OPERATION
Benefits of Continuous Wave (CW) operation
Flexible beam patterns for detectors Almost any macro pulse structure can be offered
Slower repetition rate lasers
Fill-transients no longer an issue
Benefits of Long Pulse (LP) operation
Still high duty factor (DF = 10-50%)
Higher gradients than CW with same heat load
*up to 500 kHz for 20pC
*up to 1 MHz for 20pC
*
*

## Slide 24: OPERATING THE XFEL IN CW
A2
A3
A4
A5
A6
A1
AH1
SASE1
SASE2
SASE3
A25
Linac section L3
operated at moderate CW gradients
lengthened by former A2 … A5
80 + 12 modules
24 RF stations
Expected energy 8 GeV !
L1
4 modules (1 RF station)
L2
12 modules (3 RF stations)
L3
80 modules (20 RF stations)
Injector
1.3 GHz module 3.9 GHz 3rd harm.
A2
A3
A4
A5
A1
AH1
1 Module
cw optimized modules
1 – Replace the front-end cryomodules (17x)
  Larger cooling capability
  CW cavities
2 – Install CW capable RF sources
  1x IOT per RF station
3 – Double the cryo plant (cost driver)
  2.5  5kW
4 – Install CW capable gun:
  RF gun upgrade
The former front-end cryomodules can be installed at the end of the linac to lengthen L3 (+4 RF stations)
No further action required in L3 (>1km)
The upgraded XFEL would be capable of short pulse long pulse AND continuous wave operation
A6
A29

## Slide 25: Coupler modifications
Cavity | QL max (before) | QL min (after) | QL max (after)
C1 | 2.8E7 | 0.6E7 | 8.4E7
C2 | 1.9E7 | 0.5E7 | 6.8E7
C3 | 2.2E7 | 0.8E7 | 11.0E7
C4 | 2.0E7 | 0.6E7 | 9.1E7
C5 | 2.0E7 | 0.5E7 | 7.5E7
C6 | 1.9E7 | 0.4E7 | 6.6E7
C7 | 1.8E7 | 0.5E7 | 3.0E7
C8 | 2.0E7 | 0.5E7 | 3.0E7
Modified iso-vac flange
Courtesy D. Kostin
Example of XM-3

## Slide 26: Control of acceleration field and cavity resonance
RF feedback
Applied around individual cavities or to the vector sum
Proportional / integral feedback controller
Goal is to maintain gradient amplitude and phase
  dA/A  0.01%
  dP  0.01 deg.
Piezo feedback
Each cavity is equipped with a dual piezo frequency tuner
Applied around individual piezo electric element
Proportional / integral feedback controller
Goal is to keep cavity on resonance to meet phase stability requirements
  f << cavity half bandwidth

## Slide 27: Results: RF Stability example
Vector sum regulation (CW)
EACC = 15 MV/m QL = 1.5-3x107 (43-22 Hz half bandwidth)
Regulation performance (May 2017)
  dA/A = 0.008 % dP = 0.008 deg.
EACC = 16 MV/m QL = 3x107 (22 Hz half bandwidth)
Regulation performance (Dec. 2017)
  dA/A = 0.007 % dP = 0.010 deg.
Single cavity regulation (CW)
EACC = 16 MV/m QL = 8.2x107 (8 Hz half bandwidth)
Regulation performance (Dec. 2017)
  dA/A = 0.015 % dP = 0.017 deg.
3 hours
Vector sum amplitude stability (dA/A)
3 hours
Vector sum phase stability (deg.)
goal
goal
RMS jitter [ % ]
RMS jitter [ deg. ]
World Record !

## Slide 28: Heat load measurements
The goal was to investigate the potential benefit to operate large grain cavities at temperatures lower than 2K. In these measurements Q0 is computed by measuring the difference in helium mass flow when one (or several) cavities are in operation.
Cryomodule heat load measurements
Single cavity heat load measurements
Q0 vs Eacc for the whole cryomodule at 2K, 1.8K and 1.65K. The gain in Q0 for 1.8K operation compared to 2K operation is about 80%. Further investigation is required to find out if operation at 1.8K will be more efficient for the first 136 cavities (17 cryomodules in the injector section of the European XFEL accelerator)
The main linac, extended from 84 to 96 cryomodules, could operate in CW around 8 MV/m. The dynamic heat load at this lower gradient is very low and operation at 1.8K would not be beneficial due to the static heat load

## Slide 29: LFD and static drops
The “delay” between the forward and the reverse scans are due to the hysteresis induced by the tuner backlash.
Hysteresis behavior when tuning the cavity
If the scan is stopped just before the static drop, one can see the classic hysteresis curve.

## Slide 30: Cavity mechanical modes
The coupling between the excited cavity (C4) and the neighboring cavities (C3 and C5) become dominant around the cavity mechanical resonant frequency (~260 Hz)
Mechanical cross talk between cavities