## Slide 1
High-Performance DIRC Detector for future EIC Detector
Greg Kalicy
April 4th, 2018
Outline:
Simulations
3-layer lens prototypes

## Slide 2
High-Performance DIRC Activities
Simulation studies:
  Studies of design using stand alone Geant4 package.
  Implementing High-Performance DIRC into the sPHOENIX and BeAST simulation.
Hardware activities:
  The prototype of 3-layer spherical and cylindrical lens validation in the test beam.
  Mapping focal plane of the lenses.
  Radiation hardness test of candidates for middle layer of the lens.
Preparing next prototype lens

## Slide 3
High-Performance DIRC Simulation
Studies of design using stand alone Geant4 package.
Implementing High-Performance DIRC into the sPHOENIX and BeAST simulation.

## Slide 4
High-Performance DIRC Simulation
Studies of design using stand alone Geant4 package.
Implementing High-Performance DIRC into the sPHOENIX and BeAST simulation.
BNL ePHENIX EIC central detector

## Slide 5
3-layer Lens Performance verification
Readout
electronics
Supporting
structure
Readout section
Optics section
Full system PANDA barrel DIRC prototype
New cylindrical lens tested!
Polar angle 90O
Azimuthal angle 0O

## Slide 6
Lens
3-layer Lens CERN Beam Test 2017

## Slide 7
3-layer Lens CERN Beam Test 2017
25 degree polar angle
beam data with pion tag @ 7 GeV/c
bar + 3 layer spherical lens
bar + 3 layer cylindrical lens
plate + 3LC lens
Roman Dzhygadlo

## Slide 8
3-layer Lens CERN Beam Test 2017
geant
simulation
Photon yield:
data ~82 photons
sim ~80 photons
data 3.9 s.d.
sim 4.2 s.d.
data ~93 photons
sim ~90 photons
Preliminary
Preliminary
data 3.1 s.d.
sim 3.4 s.d.
π/p separation power @ 7 GeV/c (~ π/K @ 3.5 GeV/c):
bar + 3 layer spherical lens
plate + 3 layer cylindrical lens
good agreement with simulations
Roman Dzhygadlo

## Slide 9
DIRC@EIC Prototype 3-component lens
Geant4 simulation of focal plane:
Standard lens 3 component lens
R. Dzhygadlo, G. Kalicy, C. Schwarz
Simulated data
Limitations of standard focusing lenses:
Significant photon yield loss around 90° particle track
Aberration for photons with steeper angles
Spherical 3-layer lens prototype

## Slide 10
3-layer Lens Performance verification
Mapping focal plane of 3-layer lens:
Lens holder designed to rotate in two planes for the 3D mapping of the focal plane and shifts of lens in horizontal plane.
L. Allison, R. Dzhygadlo, G. Kalicy, C. Schwarz
Laser setup to map the focal plane
3D lens holder

## Slide 11
Mapping focal plane of 3-layer lens:
Lens holder designed to rotate in two planes for the 3D mapping of the focal plane and shifts of lens in horizontal plane.
Spherical 3-layer lens:
Results of measurements confirm desired flat focal plane for centered laser beams on the lens
Off-center laser beams in agreement with simulation
L. Allison, R. Dzhygadlo, G. Kalicy, C. Schwarz
Measured and simulated focal plane of
spherical 3-layer lens
3-layer Lens Performance verification

## Slide 12
Cylindrical 3-layer lens:
3-layer Lens Performance verification

## Slide 13
3-layer Lens Radiation Hardness
Radiation hardness tests of NLaK33 material at CUA
Measurements using X-Ray source show the transmission at 420 nm drops by over 1% per 100 rad.
Annealing process of the transmission observed, is being further investigated.
NLaK33 sample
in CUA setup
Measured transmission (not Fresnel corrected ) through the NLaK33 irradiation dose for 420 nm.
Spherical 3-layer lens

## Slide 14
3-layer Lens Radiation Hardness
Radiation hardness tests of at BNL:
Irradiation with Co60, possibility of testing with neutrons later.
Monochromator to measure transmission.
  PbF2, two glasses from Schott , NLaK33, and material for Fresnel Lens will be tested.
  Annealing process of the materials has to be understood as the measurement will take 1-2 weeks.
Co60 Chamber
Monochromator

## Slide 15
High-Performance DIRC Activities
Simulation studies:
  Studies of design using stand alone Geant4 package. (in progress)
  Implementing High-Performance DIRC into the sPHOENIX and BeAST simulation. (early stage)
Hardware activities:
  The prototype of 3-layer spherical and cylindrical lens validation in the test beam. (analysis in progress)
  Mapping focal plane of the lenses. (already started)
  Radiation hardness test of candidates for middle layer of the lens. (scheduled for May or August)
Preparing next prototype lens:
  Candidate to polish PbF2 (waiting for the quote)
  Discussion with RMI on 20th of April

## Slide 16
Backup

## Slide 17
High-performance DIRC Reaching Performance
Prototype:
Improving focusing: 3-layer spherical lens
Optimizing pixel size:
6 cm
6 cm

## Slide 18
High-performance DIRC Design
11 narrow bars in each section
1 wide bar (plate) in each section
16 section design with one prism in each as expansion volume
Simplified view of one section:
GEANT4 visualization of the designs:

## Slide 19
High-performance DIRC Narrow bar design
Radiator bars
  17 x 35 x 4200 mm
  11 bars per box
  16 bar boxes, 1m from IP
3 component lens
  14 x 35 x 50 mm
  radiuses: 47 mm, 29 mm
Expansion volume
  Prism with 38° opening angle
  285 x 390 x 300 mm
Sensors
  208k pixels, each 3 mm2
Geant4 simulation of High-Performance DIRC detector

## Slide 20
High-performance DIRC Performance
~4.2 s.d. separation at 6 GeV/c,
30O polar angle
17x32x4200 mm3 bars
3-layer spherical lens
3x3 mm2 pixels
100 ps time resolution
π
K
blue: 1 mrad track resoution
red: 0.5 mrad track resoution
black: ideal tracking
Configuration:
polar angle [deg]
polar angle [deg]
design meets the requirements for PID in the barrel region