## Slide 1: EIC machine backgrounds
Latifa Elouadrhiri
Jefferson Lab
CFNS workshop on Forward Physics And Instrumentation
From Colliders To Cosmic Rays
Oct. 17-19, 2018

## Slide 2: Introduction
EIC IR and Detector concepts are designed to best enable the physics of the EIC whitepaper and made in close collaboration with the accelerator design
EIC High Luminosity performance is mandatory in order to start the nucleon nuclear structure measurements on Day 1
This requires thorough quantitative background studies to ensure the high luminosity and full acceptance reach

## Slide 3: Goals of the Proposal
Study background generated by machine operation in simulation:
  Synchrotron radiation
  Beam-gas interactions
  Beam halo effects and beam losses
  Neutron flux
  Others
Quantify background rates and radiation doses in order to assess the impact on
  Detectors’ operation, electronics, beamline components, etc.
Provide input
  Machine lattice, IR design: beam pipe, magnets, vacuum/pumping
  Detector design, technology choices & Support structures, etc.
It is critical to perform a thorough study of the type/dose and distribution of machine induced background NOW that the IR is being designed

## Slide 4: Main Background Sources
Electron beam
  Synchrotron radiation
    Backscattering
    Photo desorption -> degradation of vacuum
  Beam gas interactions
    Off momentum electrons
  Higher order mode losses
    Local heating at injection
    and ramp (short bunches)
    -> degradation of vacuum
Proton\Ion beams
  Beam gas interaction, large hadronic cross section
    Background in detector
    Secondary interactions with aperture limitations, i.e. with magnets, beam pipe, masks
Need:
Careful design of the IR
SR masks
Excellent vacuum system

## Slide 5: Tools and Methods
GEANT4/GEMC, GEANT3 and Fluka
  Detector and beam pipe modeling
Beam distribution/emittance
  Input to GEANT4
Synchrotron Radiation tools developed at SLAC (SR code)
  Input to GEANT4
Molflow+
Synrad
Vacuum Modeling
Installed at JLab
GEANT4
Input

## Slide 6: SR- Photon Generation (SR-Code)
A gaussian transverse electron beam profile with wide gaussian tails
Each electron is traced through the given magnetic elements and a photon critical energy is calculated based on the trajectory curvature
The SR fan start and stop points of each magnetic element are also found and traced through a series of beam pipe apertures where the fraction of the fan hitting each aperture is recorded
A generator of scattered photons is built from of SR photons found in the energy ranges for a give aperture: the result is the number of scattered photons from the mask tip for example
Each photon (energy, position and direction) are then saved to a file that can be read in by a GEANT
Number of incident photons on this mask tip per beam bunch: 6.9e7.
The actual number of scattered photons per beam bunch : 9751

## Slide 7: Vacuum Modeling Tools
Molflow+ and Synrad modeling software developed by Roberto Kersevan & Marton Ady
  Molflow+: static vacuum modeling
  SynRad: model of vacuum events due to beam
Jason Carter, ANL, used Molflow+/Synrad to model static and dynamic vacuum for APS upgrade
Jason Carter, ANL, and Marton Ady, CERN, used Molflow+/Synrad for SuperKEKB interaction region
CAD designs of beamline are combined with pumping speeds and outgassing rates of elements yield expected pressure becomes input to our GEANT simulations.

## Slide 8: Background Studies Workflow
Magnets and Machine Layout
Vacuum Pumping System Design
Intensity
Distribution of SR
Vacuum Quality
Beam/gas interactions (both ion and e beam)
Machine &
Detector Background
Notes: Interior Page Design 1

## Slide 9: Lessons from HERA II Upgrade
Severe background problems in the year 2002 significantly delayed startup of HERA after luminosity upgrade
  No detailed simulations prior to the upgrade
Most of the background came from proton-beam gas interactions where vacuum deteriorated due to synchrotron radiation.
Al (100%)
10-8 mbar
10-10 mbar
10-10 mbar
We used HERA II data to benchmark our tools and procedures

## Slide 10: HERA Configuration Simulated in our Framework
Click to add title
Click to add subtitle
Beam current 100 mA
E0=900GeV
In GEMC
GEMC C5
HERA C5

## Slide 11: BG rate ~ 66kHz (33kHz from Charge particles)
BG rate ~ 31kHz
BG rate ~ 13kHz
BG rate ~ 7kHz
BG rate ~ 3kHz
BG rate ~1.3kHz
10-8mbar
10-10mbar
10-8mbar
0.5*10-8mbar
0.2*10-8mbar
0.1*10-8mbar
0.05*10-8mbar
0.02*10-8mbar
0.01*10-8mbar
BG rate ~0.4kHz
Results of our
simulation
of HERA

## Slide 12
The rate of the particles in the simulated C5 detector was calculated for HERA parameters and measured 33 kHz for charged particles in agreement with ZEUS data
For more systematics, additional studies were made, varying the vacuum region length, physics model and beam pipe material composition, whish showed the expected dependence on each parameter
HERA Data as Benchmark for our Simulation Tools
Validation and benchmarking of our simulation
tools and procedures
Good agreement of our simulation rate to the
measured rate at HERA!
From measurement at HERA
From our simulation of HERA
C5 rate as a function of HERA e beam current for different p beam current
Results of our simulations

## Slide 13
$ gemc file.gcard –SYNRAD=1
$ gemc file.gcard –SYNRAD=2
Synchrotron Radiation in Vacuum
procID = 13
Synchrotron Radiation in Material (air)
procID =14
Synchrotron Radiation available in GEMC
Electron Upstream Dipole BXSR2L
Strength ~ 0.320 T/m
Length ~ 2.00 M
Bending angle = 0.038397244 rad
Z = 4.0 m (at center)
SR options 1 and 2 are mutually exclusive!

## Slide 14
Photon Critical Energy
εc = 0.665* E [GeV]2* B [T]
~ 5.22 keV
Expect to see peak at 0.3*εc , or 1.57 keV
Peak approximately correct.
Next Steps: currently verifying that integrated photon density = 6.49 keV
Verifying Energy Spectrum

## Slide 15: Beam Pipe Conceptual Design Updated
Minimum multiple scattering in the beam pipe material
Synchrotron radiation collimation
L. Elouadrhiri et al. (JLab), C. Hyde (ODU), M. Sullivan (SLAC)

## Slide 16: Development of IR Magnet Specifications
IR magnet engineering design/analysis
  Heat and radiation loads on IR magnets
  Perform magnetic analysis and initial optimization design
  Mechanical and magnetic design of an optimized IR quadrupole
  Incorporate optimized IR quadrupole lessons/features and finalize JLEIC IR layout

## Slide 17
From Drawing to GEANT
Start with stp file which contains full design
Save each object as a separate file
Assign material to each object
Put into the GEMC/GEANT4
Example of EIC beam pipe implementation
Technical note will be written, as part of making our procedure accessible

## Slide 18: JLEIC Interaction Region
Beam Pipe

## Slide 19: Original gcard from the EIC gemc, interaction regions from CAD

## Slide 20
Collimator
Electron Up Tube
Electron Down Tube
Ion Up Tube
Ion Down Tube
Beam-pipe in GEANT Simulation: View

## Slide 21
Beam-pipe in GEANT Simulation: another view
Collimator
Electron Up Tube
Electron Down Tube
Ion Up Tube
Ion Down Tube

## Slide 22: Synchrotron Distribution at IP
Vertex Tracker (SVT):
6 Layer Si Pixel Detector
1st layer +0.5 cm from central beam pipe
Input: 5 GeV e beam (matched distribution + halo) at (0, 0, -7.21)m towards IP
GEMC (stable release) now interfaced with GEANT4 SR Code

## Slide 23: Synchrotron Distribution at IP
Transverse profile of SVT in GEMC simulation
SR photon occupancy +/- 30 cm around IP
indicates detector structure
Silicone Vertex Tracker

## Slide 24: Synchrotron Distribution at IP
Synchrotron Spot at IP
(no pipe nor detector)
Synchrotron in SVT at IP
Shape of photon distribution consistent in both plots*
*Graphs generated from different # of beam statistics

## Slide 25: Ion Beam/Gas Background at IP
GEMC model of central vacuum chamber imported from CAD
1st Iteration GEMC model of interior “balloon” imported from CAD
To determine the rate of ion beam/gas background as a function of vacuum for EIC geometry, we need a CAD model of the internals of the beam pipe and interaction region.
The detailed interior imported into GEMC to simulate specific gas compositions and densities determined by vacuum engineers’ simulations.
This yields the geometry-dependent effects of ion beam/gas background halo interacting with beam pipe and IP elements.

## Slide 26
All lines warm, outgassing estimated at standard 304 SS: 5x10-12 TorrLs-1cm-2
Pumps simulated within beamline at ends of IR chamber
  2400 L/s in 6.2 cm ID electron lines
  1200 L/s in 3 cm ID ion lines
  Pump speeds feasible using arrays of NEXTorr compact getter/ion pumps
Expected static vacuum in this scenario ~5x10-10 Torr
Highest pressures in long electron and ion source lines, room temp
  ~7x10-9 Torr – additional pumping locations to be identified
Molflow+ investigations of static vacuum

## Slide 27: Initial Synrad calculations
Input parameters
  e- line: 3 quadrupole field strengths and positions
  Beam parameters (emittance, coupling, βx,y, εx,y as a function of position
  Geometry of collimator and interaction region
  10 GeV beam, 3000 mA current
Output synchrotron radiation
  Max. collimator: 300 W/cm2
  Max chamber: 3 mW/cm2
Refinements needed
  Refined beam parameters
  Surface roughness analysis for reflection
  Beryllium window properties determined and added
  Photon heat load due to beam/gas interaction from GEMC
  Synchrotron induced heating and outgassing to input to Molflow+ for dynamic vacuum calculations

## Slide 28: Neutron Flux and Radiation Dose at eRHIC
Background from primary interactions at the IP is simulated
Neutron Flux = “a sum of neutron path lengths”/“cell volume” for N events
Radiation dose: “a sum of dE/dx”/”cell volume” for N events
-> forward EmCal: up to ~5*109 n/cm2 per fb-1 (inside the towers); perhaps ~5
less at the SiPM location;
-> backward EmCal: ~250 rad/year
(at a “nominal” luminosity
~1033 cm-2 s-1)
-> just a basic EicRoot Monte-Carlo pass using BeAST geometry

## Slide 29: Synchrotron Distribution at IP
Accomplished
Benchmarked GEANT4 SR code against validated SR code from SLAC;
Interfaced GEMC with both SR codes;
Implemented full chain JLEIC IR configuration;
Automated workflow between simulations and lattice design with magnet script;
Modeled e beam halo based on work at SLAC;
Generated SR photon distribution in SVT around beam pipe.
Next Steps
Calculate SVT occupancy based on current knowledge of thresholds, geometries, estimated granularity (in progress);
Refine SVT occupancy calculation with:
  Next iteration of CAD beam pipe to include gold coatings,
  Maturation of SVT design, especially granularity;
Add additional IP elements as appropriate (detector, support structure, etc).

## Slide 30: Ion Beam/Gas Background at IP
Accomplished
Benchmarked GEANT4 beam/gas interactions against data from HERA;
Modeled simplified IR based on JLEIC parameters;
Simulate beam/gas background events using 100 GeV proton beam from internal GEMC generator
Next Steps
Complete analysis of beam/gas background vs vacuum level (in progress);
Refine beam pipe interior for both JLEIC and eRICH;
Model proton beam matched distribution with halo;
Refine results by implementing density distribution from vacuum engineers around IP.

## Slide 31: Simulation Frame Work – SR – Next Steps
Optimize the machine lattice and track matched beam to evaluate changes in background carried to IR and detectors.
Develop an efficient method to streamline the transfer design between Lattice and GEANT4
Design and optimize the collimation of the synchrotron radiation to minimize the background rate
Import detailed engineering model of machine lattice magnets and IR design from CAD to GEMC.
Evaluate quantitatively the background type and distribution due to the SR radiation, giving feed back to the machine and IR designer towards design optimization.

## Slide 32: Beam Gas Interaction Next Steps
Use Molflow+ and Synrad to realistically simulate vacuum conditions.
Design vacuum system based on requirements of the IR vacuum tube and vacuum vessels and its translation into the simulation.
Use SR level to determine the level of dynamic vacuum.
Evaluate the background type and distribution due to the beam gas interaction giving feed back to the vacuum engineer and IR designer towards design optimization.
Estimate rates, due to both beam gas interaction and SR, in the detectors and beam pipe in the configuration including realistic lattice, vacuum levels and IR. This will serve as an input to the iterative procedure of the lattice and vacuum system optimization.

## Slide 33: Neutron Flux – Next Steps
Develop an interface to Fluka and GRANT3 to evaluate neutron flux from our simulation framework.
Benchmark comparison of neutron flux from Fluka, GEANT3 and GEANT4 by checking the list of all the relevant physics processes.
Evaluate neutron flux from Fluka/GEANT3 by comparison with GEANT4 in the EIC configuration. This is critical task as it has severe impact on detector and electronics lifetime.

## Slide 34: Team
Latifa Elouadrhiri (Thomas Jefferson National Accelerator Facility)
Yulia Furletova (Thomas Jefferson National Accelerator Facility)
Charles Hyde (Old Dominion University)
Alexander Kislev (Brookhaven National Laboratory)
Vasiliy Morozov (Thomas Jefferson National Accelerator Facility)
Nikolay Markov (University of Connecticut)
Christoph Montag (Brookhaven National Laboratory)
Christine Ploen (Old Dominion University)
Marci Stutzman (Thomas Jefferson National Accelerator Facility)
Mike Sullivan (SLAC National Accelerator Laboratory)
Mark Wiseman (Thomas Jefferson National Accelerator Facility)

## Slide 35: IR/Luminosity Working Group Charge
  The EICUG IR working group’s mission is to provide an interface between the machine design / IR design and the physics needs to ensure that the EIC physics program is properly implemented with a broad range of physics measurements in particular those requiring forward / backward instrumentation. This should include challenging questions related to the measurement of nuclear fragments for a variety of processes and associated measured energy / momentum range and spatial acceptance. The requirements for the IR design should be determined from detailed simulations for proposed processes. In addition to specific aspects of the IR design, the working group should also address the scheme for luminosity measurement and its impact on the machine element layout. It is strongly suggested that the new EICUG IR working group interface directly with existing efforts at BNL and JLab. The working group will be open to all members of the EICUG. It will communicate via a new mailing list and organize regular online and in-person meetings that enable broad and active participation from within the EICUG as a whole.

## Slide 36: Summary
Created validated and benchmarked simulations tools and procedures
    GEANT simulation: complete the HERA benchmarking
    Synchrotron radiation modeling code
    Static vacuum modeling
Tools and procedures are completed or being finalized and documented
Next perform detailed simulations of the EIC machine related background for both JLEIC and eRICH configurations towards optimized beam- pipe design for both machine options
    Synchrotron radiation modeling code
    Static & dynamic vacuum modeling
    Neutron flux
Ready to perform detailed rates and occupancies due to different background sources to optimize the design – input to technology choices

## Slide 37
@latifaelou