## Slide 1: Archiving storage for Scientific Research ENVIRONMENT
David Yu
Workshop on Central Computing support for Photon Sciences

## Slide 2: BNL Scientific Data and Computing Center
RHIC Tire-0
Primary Data storage for all RHIC experiment data.
LHC ATLAS Tier-1 for the US
Secondary data storage for fraction of data (~23%).
Belle-2 Tier-1 (New)

## Slide 3: Amount of Data Archived in BNL
2004
2005
2006
2007
2008
2009
2010
2011
2012
2013
2014
2015
2016
2017
2018
~60 PB
50 PB
100 PB
150 PB
HOT
COLD
~145 PB

## Slide 4: Long Term Storage
Keeping 100+ PB data for a long time
Reliability
Performance
Life Expectancy
Scalability
Tape: 30+ years
T10K, LTO-7, LTO-8, IBM JD: 1 x 1019
Bit Error Rate (BER): Number of user bits transferred between two unrecoverable error events
1 error event in 1.25 exabytes *
Just add more tape cartridges.
Add more tape libraries.
T10K | LTO-7 | LTO-8 | IBM JD
250 MB/s | 300 MB/s | 360 MB/s | 360 MB/s
* https://www.lto.org/wp-content/uploads/2014/07/LTO_Get_The_Facts_10_15.pdf

## Slide 5: Scalability
- Add Tapes
Library Capacity: 10,000 Tapes
LTO-7: 60,000 TB or 60 PB
39 tapes per load
Tape initializing:
1 min/tape-drive
Fill 1 PB storage
LTO-7: 3.5 hours
LTO-8: 1 hr 42 min
LTO-8: 120,000 TB or 120 PB
39 LTO-7 = 234 TB
Will take ~ 7 minutes
Increasing Capacity

## Slide 6: scalability
Library Full?
Add Library

## Slide 7: Scalability
- Add Tape Drives
Library Capacity: 64 Tape Drives / Library
LTO-7: 64 x 300 MB/s = 19.2 GB/s
LTO-8: 64 x 360 MB/s = 23 GB/s
Increasing Bandwidth
Bandwidth can be expanded easily by adding more drives
Bandwidth can be controlled easily by allocating number of drives.

## Slide 8: Tape Storage in BNL
2004
2005
2006
2007
2008
2009
2010
2011
2012
2013
2014
2015
2016
2017
2018
HOT
COLD
Tape Storage
50 PB
100 PB
150 PB
145 PB
Other Research Institutes
BNL Data Center

## Slide 9: High Throughput Active Archiving System
RHIC Experiment data directly go to tape storage (archive as primary copy)
Disk cache
STAR
Detector
RHIC detectors:
Streaming data

## Slide 10: High Throughput Active Archiving System
Reprocessing data, retrieving data from tape archival storage
Disk cache
Data processing
Streaming data

## Slide 11: High Throughput Active Archiving System
Write 1.5 GB/s
N files
Read X MB/s
80 Gb NIC
FC
FC
Write 200 MB/s/drive
Data Reprocessing
Data movers with disk cache
Automatic Tape Library
Need 8 drives = 1.6 GB/s
HPSS
N/4 files
N/4 files
N/4 files
N/4 files
~400 MB/s
~400 MB/s
~400 MB/s
~400 MB/s
Read X MB/s

## Slide 12: Staging vs network transfer

## Slide 13: Transfer out of sync

## Slide 14: RHIC run 18 data rate
Scientific experiment data
Green: Data acquisition (RAW and DST)
Blue: Data Access (RAW and DST)
2.7 GB/s
1.6 GB/s
~1.1 GB/s
1 week
~1 GB/s

## Slide 15: RHIC run 18 Data Acquisition Rate
RHIC Run 18 Data (new data only)
Over all average rate: 591 MB/s
Allocated 5 drives: Real time average 829 MB/s
20 hours
50 hours

## Slide 16: HPSS Resource control
HPSS
core
STAR Gateway
PHENIX Gateway
ATLAS HAProxy
Gateway
Gateway
Gateway
Belle-II Gateway
STAR RAW Disk
STAR DST Disk
PHENIX RAW Disk
PHENIX DST Disk
ATLAS Disk
Belle-II Disk
STAR Tape Drives pool
PHENIX Tape Drives pool
ATLAS Tape Drives pool
STAR RAW Tapes
STAR DST Tapes
PHENIX RAW Tapes
PHENIX DST Tapes
ATLAS Tapes
Belle-II Tapes

## Slide 17: Data ownership

## Slide 18: Tape Storage Usage
In 2017
20.8 PB
24.8 PB
Archived to tape:
  19,412,702 files – Average 53,185 files/day
  20.8 PB – Average 58.4 TB / day
Restored from tape:
  11,693,141 files - Average 32,036 files/day,
  24.8 PB - Average 69.5 TB/day

## Slide 19: Accessing Data From Tape Storage
Tape is sequential access media
Tape is designed for streaming data
We have observed files recall at average 132 MB/s/drive for LTO-5 in production.
All files were compressed. All overhead (mount and seek) included.
LTO-5 max speed: 140 MB/s
Minimized redundant tape-mounts.
Large files works better.
LTO-7
300 MB/s
LTO-5
140 MB/s
LTO-6
160 MB/s
Use File Family to keep the dataset together, to reduce the file positioning/seeking time

## Slide 20: File Recall Performance
15:00 – 21:00 sample: 1.3 GB/s
1.3 / 10 Drives = 132 MB/s/drive
All overheads included
(mount/dismount, seek … )
42,196 files requested
Average file size: 10 GB
Destination disk limit: <1.5 GB/s
Need to adjust staging drives, to keep @ <1.5 GB/s
6 hours
1.3 GB/s
Limited 10 drives

## Slide 21: Conclusions
We have implemented an active tape-storage data archive currently holding near 150 PB of scientific data and serving scientists from multiple collaborations worldwide
The archive and the underlying tape storage complex are managed in a very efficient way by a suite of in-house developed optimization and monitoring tools
The data archive volume can grow infinitely with the addition of relevant tape storage resources (media, libraries and tape drives)
Tape is still the leader in cost per GB and power efficiency. The implementation concept is based on the most cost-effective and energy efficient (green) memory model available today