## Slide 1: Low Energy RHIC electron Cooling (LEReC): Status and Commissioning Progress
Alexei Fedotov
on behalf of the LEReC team
BNL NPP 2019 PAC Meeting
June 10, 2019

## Slide 2: LEReC Project Overview
The goal of the LEReC project is to provide luminosity improvement for RHIC
operation at low energies to search for the QCD critical point.
LEReC is first RF linac-based electron cooler (bunched beam cooling).
To provide luminosity improvement with such new approach requires:
Building and commissioning of new state of the art electron accelerator 
Produce electron beam with beam quality suitable for cooling
RF acceleration and transport maintaining required beam quality
Achieve required beam parameters in cooling sections
Commissioning of bunched beam electron cooling
Commissioning of electron cooling in a collider (in process)
2

## Slide 3: RHIC @ BNL, Long Island, New York
RHIC
NSRL
LINAC
Booster
AGS
Tandems
6:00 o’clock
8:00 o’clock
10:00 o’clock
12:00 o’clock
4:00 o’clock
LEReC
2:00 o’clock
EBIS

## Slide 4
LEReC inside RHIC tunnel at
Interaction Region @ 2 o’clock (IR2)
Cooling sections
Injection Section
(DC photocathode Gun,
SRF Booster cavity)
Laser
Transport beamline

## Slide 5: LEReC electron accelerator (100 meters of beamlines with the DC Gun, high-power fiber laser, 5 RF systems, including one SRF, many magnets and instrumentation)
COOLING
in Blue RHIC ring
COOLING
in Yellow RHIC ring
High-Power Beam Dump
Extraction beam line
DC e- Gun
704 MHz SRF
Booster Cavity
2.1 GHz Cu Cavity
9 MHz Cu Cavity
704 MHz Cu Cavity
Injection beam dump
RF Diagnostic Beamline
RHIC TRIPLET
RHIC DX
180°
Bending
Magnet
e-
e-
e-
* NOT to scale
Cathode
loading system
LF solenoid
HF solenoid
Transport solenoid
ERL solenoid
Quad corrector
Trim corrector
Corrector 3.8 ID
Corrector 6.0 ID
BPM 2.4 ID
BPM 4.8 ID
Bellows
Ion pump
Merger
Beamline
Transport
Beamline
704 MHz Cu Deflector Cavity

## Slide 6: LEReC cooling sections

## Slide 7: LEReC electron beam parameters
Electron beam requirement for cooling |  |  | 
Kinetic energy, MeV | 1.6 | 2 | 2.6
Cooling section length, m | 20 | 20 | 20
Electron bunch (704MHz) charge, pC | 130 | 170 | 200
Effective charge used for cooling | 100 | 130 | 150
Bunches per macrobunch (9 MHz) | 30 | 30 | 24-30
Charge in macrobunch, nC | 4 | 5 | 5-6
RMS normalized emittance, um | < 2.5 | < 2.5 | < 2.5
Average current, mA | 36 | 47 | 45-55
RMS energy spread | < 5e-4 | < 5e-4 | < 5e-4
RMS angular spread | <150 urad | <150 urad | <150 urad

## Slide 8: Bunched beam electron cooling for LEReC
Electron bunches suitable for cooling are generated by illuminating a multi-alkali (CsK2Sb) photocathode inside the high-voltage DC Gun with green light using high-power laser (high-brightness in 3D: both emittances and energy spread).
The 704MHz fiber laser produces required modulations to overlap ion bunches at 9MHz frequency with laser pulse temporal profile shaping using crystal stacking.
Such electron bunches are accelerated using 704MHz SRF cavity. RF gymnastics (several RF cavities) is employed to achieve energy spread required for cooling. Electron beams of required quality are delivered to cooling sections.
Electron bunches overlap only small portion of ion bunch. All ion amplitudes are expected to be cooled as a result of synchrotron oscillations of ions.

## Slide 9: LEReC beam structure in cooling section
110 nsec,
f=9 MHz
Ions structure:
120 bunches
f_rep=120x75.8347 kHz=9.1 MHz
N_ion=5e8, I_peak=0.24 A
Rms length=3 meters
1.42 nsec
30 electron bunches per ion bunch
Electrons:
f_SRF=704 MHz
Q_e=100 pC, I_peak=0.4 A
Rms length=3 cm
9 MHz bunch structure
Ion bunches
with new 9MHz RF
Electron Macro-bunch

## Slide 10: Attainment of “cold” electron beam suitable for cooling
LEReC is based on the state-of-the-art accelerator physics and technology:
Photocathodes: production and delivery system
High power fiber laser and transport
Laser beam shaping to produce electron bunches of required quality
Operation of DC gun at high voltages (around 400kV) with high charge and high average current
RF gymnastics using several RF cavities and stability control
Energy stability and control
Instrumentation and controls

## Slide 11: Transverse phase space measurements of electron beam
Movable slit and downstream beam profile monitors are installed at the beginning of each cooling section.
Bunch charge 75 pC

## Slide 12: Longitudinal phase space measurement of electron beam
1 macro-bunch of electrons (total charge 3nC)
6 macro-bunches, 3 nC each.
704MHz RF vertically
deflecting cavity
First dogleg merger dipole is off
Beam goes to RF diagnostic line
20 degree dipole produces dispersion
Deflecting cavity produces time dependent vertical kick
In pulsed mode, subsequent electron macro-bunches have lower energy due to beam loading in RF cavities.

## Slide 13: LEReC: First observation of electron cooling using bunched electron beam, April 5, 2019
Ion bunch #2 is being cooled
Bunch length time evolution
for two Au ion bunches in RHIC
Energy of electrons and ions matched
Ion bunch #4 which is not being cooled
Longitudinal profiles
of six ion bunches

## Slide 14: Simultaneous cooling in Yellow and Blue rings (76kHz mode, 6 ions bunches: bunch #1 is being cooled; bunch #6 does not see electrons)
cooled and non-interacting bunches
Yellow
Blue
Blue
Yellow
Cooled, heated and non-interacting bunches
Blue
Yellow
bunch length
bunch intensity
loss rate
Longitudinal bunch profiles
cooled
cooled
cooled

## Slide 15: Simultaneous cooling (in Yellow and Blue RHIC rings, 6 bunches in each) using high-current 9 MHz CW electron beam
Bunch length (FWHM, nsec)
BLUE
YELLOW
All 6 RHIC bunches are cooled
no cooling
with cooling

## Slide 16: Potential benefits from cooling
lifetime
bunch length
lifetime
bunch length
Cooled bunch is kept shorter, more useful events within trigger window
Minimize ion beam de-bunching and losses from the RF bucket
Peak current significantly higher for cooled bunch
Emittance cooling with possible reduction of beta-function at collisions
Cooled
Non-interacting
Cooled
Non-interacting
Ion bunch profiles
Ion lifetime
Cooled bunch
Ion bunch profiles
Ion lifetime
Cooled bunch
BLUE
YELLOW

## Slide 17: LEReC roadmap to cooling
Production of 3-D high-brightness electron beams 
RF acceleration and transport of electron bunches maintaining “cold” beam 
Control of various contributions to electron angles in the cooling section to a very low level required for cooling 
Cooling commissioning milestones:
Demonstrated first electron cooling using bunched electron beams
Demonstrated cooling in 6-D
Matched electron and ion energy in both Yellow and Blue RHIC rings
Cooling was achieved in both Yellow and Blue Rings simultaneously using the same electron beam
Demonstrated longitudinal and transverse cooling of several ion bunches (high-current 9MHz CW e-beam operation) simultaneously 
Cooling in both Yellow and Blue RHIC rings simultaneously using CW electron beam 

## Slide 18: LEReC timeline and integration with RHIC Physics (unchanged, as presented in 2015)
Installation is complete
Hardware commissioning is complete
Commissioning of electron accelerator at 1.6 MeV is complete
Bunched electron beam cooling commissioned
Present focus is on operational aspects of e-cooling in RHIC
 | FY2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
design and construction |  |  |  |  |  |  |  | 
Installation |  |  |  |  |  |  |  | 
hardware commissioning |  |  |  |  |  |  |  | 
e-beam commissioning |  |  |  |  |  |  |  | 
cooling commissioning |  |  |  |  | interleaved |  |  | 
physics operation |  |  |  |  |  |  | contingency | 
today

## Slide 19: LEReC Physics integration: BES-II required events
General strategy to maximize integrated luminosity:
Cooling at the 2 lowest energies, no cooling at the 3 highest energies
Started BES-II at highest energies (machine ready w/o cooling)
Interleave cooling commissioning with physics operation
Finish BES-II at lowest energies (largest gain in Lavg and time)
center-of-mass energy √sNN | GeV | 7.7 | 9.1 | 11.5 | 14.6 | 19.6
events BES-I, actual | M | 4.3 |  | 11.7 | 24 | 36
events BES-II, min goal | M | 80 | 100 | 150 | 200 | 300
events BES-II, full goal | M | 100 | 160 | 230 | 300 | 400

## Slide 20: Summary
We designed, built and commissioned state-of-the-art electron accelerator LEReC which provides beam quality suitable for electron cooling using bunched electron beams.
Electron cooling using bunched electron beams based on the RF acceleration was successfully demonstrated.
Such cooling approach is new (previous electron coolers all used DC beams), and opens the possibility of electron cooling at high beam energies.
Cooling of ion bunches in both RHIC rings simultaneously using the same electron beam was successfully demonstrated.
An optimization of cooling and effects on ion beam lifetime is in progress.
The next step will be to show that the cooling enhances collision rates in next year’s RHIC low-energy collisions.

## Slide 21: Acknowledgement
LEReC project greatly benefits from help and expertise of many people from various groups of the Collider-Accelerator and other Departments of the BNL.
As well as FNAL, ANL, JLAB and Cornell University.
Thank you!