## Slide 1: AMPX Status
Dorothea Wiarda
Andrew M. Holcomb
Goran Arbanas
Friederike Bostelmann

## Slide 2: Overview
Processing ENDF/B-VIII.0
AMPX and GNDS
Future plans to share code with SAMMY

## Slide 3: Processing of ENDF-B/VIII.0 library
In order to process ENDF-B/VIII.0 an AMPX patch is needed. It will be available in the next SCALE beta. For previous versions the patch is available via email.
In order to use the new moderator data in SCALE, a new Standard Composition Library is needed. It will be available in the next SCALE beta.
Experimental libraries discussed in this talk will be available in the next SCALE beta.

## Slide 4: Thermal moderators
In SCALE each moderator is bound with a suitable fast reaction and a unique ID. For example:
Unfortunately there is no easy pattern to:
Automatically assign the nuclides to use in the fast region
To assign a SCALE ID number.
New ID numbers have been assigned and an appropriate configuration file has been written for use in generating inputs for AMPX.
Thermal | Fast | Scale ID
Zr in ZrH | 90Zr | 1040090
 | 91Zr | 1040091
 | … | …

## Slide 5: ENDF/B-VIII.0 libraries
CE library
252 neutron groups with homogenous f-factors.
302 neutron groups for use in fast systems
1597 neutron group library.
Covariance library (see Covariance session for more details)
Verification and Validation for these libraries is in progress.

## Slide 6: Some VALID calculations
Experiment | Measurement | CE | 252g | 302g (new p-tables) | Δk (252g vs. CE) [pcm] | Δk (302g vs. CE) [pcm]
HEU-MET-FAST-021-001 | 1.0000(24) | 0.9963(1) | 1.0069(1) | 1.0006(1) | 1067 | 431
HEU-MET-FAST-040-001 | 0.9991(11) | 1.0045(1) | 1.0081(1) | 1.0057(1) | 362 | 117
PU-MET-FAST-026-001 | 1.0000(24) | 0.9969(1) | 1.0053(1) | 1.0005(1) | 834 | 360
IEU-MET-FAST-005-001 | 1.0000(21) | 1.0012(1) | 1.0124(1) | 1.0054(1) | 1127 | 423
IEU-MET-FAST-006-001 | 1.0000(23) | 0.9961(1) | 1.0016(1) | 0.9972(1) | 549 | 111
LEU-COMP-THERM-002-004 | 0.9997(20) | 0.9986(1) | 0.9986(1) | 1.0652(1) | -2 | 6652
LEU-COMP-THERM-002-005 | 0.9997(20) | 0.9974(1) | 0.9972(1) | 1.0713(1) | 16 | 7402

## Slide 7: The “Onion” principle at work for GNDS access
File access:
  API for file access, implementation for XML reading using QT XML parser
General data containers:
  Classes for all the general data containers used in GNDS
GNDS structure:
  Classes for GNDS structures (Cross section, Resonance data, etc.) needed by AMPX. These will be expanded as needed.
AMPX and SAMMY in-memory structures:
  Classes that fill AMPX in-memory structures from the classes in the GNDS layer and vice-versa.
GNDS Access in AMPX

## Slide 8: 1-D data including resonance reconstruction
Polident
(ENDF formatted file)
Polident
(GNDS formatted file)
Compare
Compare pointwise
X10
(MG with only 1D)
X10
(MG with only 1D)
Camels
Compare MG results
Prude
(ENDF formatted file)
Prude
(GNDS formatted file)
Compare
Compare pointwise
URR only
Generate a custom template for EXSITE that allows for generation of input files for all incident neutron evaluations
Compare module makes a comparison of pointwise data on a union grid, but it does not signal missing reactions
Camels module is used to catch missing reactions of grouped data
Prude module processes unresolved resonance region (URR) data, whether for shielding only or also for point-wise cross section data

## Slide 9: Test of covariance neutron data
Puff_iv
(ENDF formatted file)
Puff_iv
(GNDS formatted file)
Covcomp
Compare covariance data
Generate a custom template for EXSITE that allows the user to generate input files for all covariance data
Puff_iv module can generate:
    Cross section covariance data from pointwise data (File 31/33)
    Cross section covariance data from resonance parameter (File 32)
    Covariance data for CHI (File 35)
    Each can be selected separately
Covcomp module shows differences and missing covariance data

## Slide 10: AMPX and SAMMY
  Since many of the same people are involved in AMPX and SAMMY development, we want to make code sharing easy.
  SAMMY and AMPX/SCALE will still be distributed as different codes, but contain the same code.
  Internally both codes are still in different source repositories, but shared code will only be contained in one of the repositories.

## Slide 11: ENDF I/O
SLBW and MLBW parameter are stored in the same class with a flag indicating which formalism to use
Resonance parameters for Reich-Moore for LRF=3 are initially stored in a different class, but are converted to a LRF=7 class before calculation
If derivatives are desired, all formalisms (except URR) are converted to LRF=7
All resonance parameter classes can contain a covariance matrix. If converting to a different formalism, the covariance matrix is re-organized accordingly
ENDF
Resonance parameters
and
Covariance matrix
MLBW
Reich-Moore LRF=3
Adler-Adler
Reich-Moore LRF=7
URR –
SLBW only
AMPX already has a C++ ENDF I/O reader and (in many cases) writer
API access to the ENDF data is independent of the ENDF file format (ENDF-6 or GNDS)
We want to change SAMMY to use the AMPX ENDF API
This will include extending the ENDF API as needed.

## Slide 12: Resonance processing as currently done in AMPX
Class describing incident particle and target
API to calculated cross section and derivatives at a given energy
+
some method to determine grid structure
Implementation for MLBW
Implementation
for Reich-Moore
Implementation for
Adler-Adler
New C++ implementation for cross-section and double differential
SAMRML for derivatives
Note: SAMRML is a simplified version of SAMMY where unneeded features are stripped.

## Slide 13: Resonance processing as we want to do it
Class describing incident particle and target
API to calculated cross section and derivatives at a given energy
+
some method to determine grid structure
SAMMY
  Advantage:
  One resonance processing code to maintain
  All new SAMMY features are immediately available in AMPX
  New ENDF format enhancements and algorithm changes are available in AMPX and SAMMY.

## Slide 14: Doppler broadening
AMPX has an NRC task to modernize Broaden this year, our code to do Doppler broadening.
Work on developing a suitable API has started.
We plan to connect different algorithms to the API
  Traditional Solbrig’s kernel broadening
  Leal-Hwang
We hope to use the same API and the connected methods in AMPX and SAMMY.

## Slide 15: Summary
New ENDF-B/VIII.0 CE and MG libraries have been produced and tested
Work on implementing GNDS reading in AMPX progressed. Currently we are working on kinematic data.
We plan more code sharing between AMPX and SAMMY