## Slide 1: Uncertainty reduction without using integral data
A. Trkov and R. Capote
Nuclear Data Section, International Atomic Energy Agency
Department for Nuclear Sciences and Applications

## Slide 2
Summary
Issues in propagated ENDF/B-VIII.0 evaluation
uncertainties for applications
Basic knowledge of criticality and
typical experimental (integral) uncertainties
Bayesian approach leading to reduced uncertainties for applications
Definition of extreme neutron spectra:
  thermal Maxwellian
  fast (taken as U-235 PFNS at the thermal)
  14 MeV is possible, but can not benefit from this approach (not constrained by exp.)
Possible applications and outlook

## Slide 3
Well known: Evaluated uncertainties in general purpose libraries lead to large uncertainties for keff
+1%
0
-1%
See INDC(NDS)-0597, IAEA 2011, Fig. 4 by O. Iwamoto
But keff(exp) ~ 0.2% ! Can we do something?
Fast assemblies ICSBEP, JENDL-4 (similar for ENDF/B-VIII.0)

## Slide 4
Proposed solutions:
Data adjustment considering integral data (+ reaction rates + …) lead to adjusted library (GLSQ or TMC)
(we know we need adjusted libraries for applications)
Advantages: low uncertainties for applications
Disadvantages:
  1) Resulting biases due to compensation effects, if not all relevant quantities have uncertainties & cross-correlations defined in the adjustment input.
The adjusted library is valid for selected benchmarks;
however, due to biases, extrapolations generally fail
=> Repeated warnings by experienced evaluators to avoid “contaminating” evaluations with integral data
(since the very beginning of evaluations)

## Slide 5
A new solution to reduce uncertainties (1)
Use additional knowledge to reduce the uncertainties
1) TOY MODEL: 1-group 0-D transport equation
(Universally valid and independent of integral data )
  2) Uncertainty of keff measurements (0.2-0.4%)
Using 1) and 2) we can derive “universal” (anti) correlations (due to the constraint keff=0.2-0.4%)
Derive those correlations for typical spectra:
Maxwellian(<E>=0.0253eV), U-235 PFNS (<E>=2 MeV)
Assume NO correlations between energy regions
f=fission; c=capture; i=other, L=leakage

## Slide 6
Use additional knowledge about ALL critical systems
Straightforward implementation in existing general-purpose libraries
- Only (anti)correlations between , for 2-4 spectral groups need to be added (3N numbers, being N the number of energy groups)
- We may also add uncertainty reduction for
Typically we add (anti) and/or correlations
No use of the integral data is made, universally valid within the given spectral region, safe extrapolation
Significant reduction of the predicted uncertainty for integral quantities: keff~0.6-0.8% (in progress)
Derived anti-correlations appear to be independent of the spectrum but short-range
A new solution to reduce uncertainties (2)

## Slide 7
DICE sensitivities: HST042.008 &HMF001
HST042.008
(1 of Hardy set)
HMF001
Godiva
0.00001 0.0001 0.01 0.10 1.0 10 100 1000 10000 10^5 10^6 10^7

## Slide 8
A new solution to reduce uncertainties:
Thermal Maxwellian spectrum (no integral data)
 | ν | f | C | L
ν | 100 |  |  | 
f | -82 | 100 |  | 
C | 5.9 | 14 | 100 | 
L | 0 | 0 | 0 | 100
 | ν | f | C | L
ν | 100 |  |  | 
f | -0.04 | 100 |  | 
C | 0.02 | -0.06 | 100 | 
L | 0 | 0 | 0 | 100
ν | 2.425 (.45%)
f | 587.3 (1.2%)
C | 99.5 (1.3%)
dkeff unconstrained
dkeff = 400 pcm
INPUT SAMPLED
Propag. keff = 861 pcm (smaller !!)
Small red. unc.
Strong in keff
(-600 pcm)
ν | 2.425 (.45%)
f | 587.3 (1.2%)
C | 99.5 (1.3%)
ν | 2.425 (.39%)
f | 587.3 (0.7%)
C | 99.5 (1.3%)

## Slide 9
ν | 2.63 (.8%)
f | 1.223 (1.2%)
C | 0.094 (10%)
ν | 2.63 (.8%)
f | 1.223 (1.2%)
C | 0.094 (10%)
ν | 2.63 (.6%)
f | 1.223 (0.9%)
C | 0.094 (9.7%)
A new solution to reduce uncertainties:
Fast spectrum 235U(nth,f) PFNS (no integral data)
dkeff unconstrained
INPUT SAMPLED
Propag. keff = 1100 pcm
dkeff = 200 pcm
 | ν | f | C | L
ν | 100 |  |  | 
f | -0.04 | 100 |  | 
C | 0.02 | -0.06 | 100 | 
L | 0 | 0 | 0 | 100
 | ν | f | C | L
ν | 100 |  |  | 
f | -85 | 100 |  | 
C | 25 | 24 | 100 | 
L | 0 | 0 | 0 | 100
Small red. unc.
Strong in keff
(-1000 pcm)

## Slide 10
A new solution is proposed to reduce uncertainties in general-purpose libraries introducing
Numerically similar to Rochmann et al (EPJ n 2017, 2018) and
similar approaches but conceptually is very different.
Approach based on the following assumptions:
1) 1-group 1D transport equation is valid to describe critical assemblies
2) Experimental keff=0.2-0.4%
No integral data are used, assumptions applied are universally valid !!
From these two assumptions, correlations are derived
Straightforward implementation in existing general-purpose libraries (only (anti)correlations between , for selected spectral groups are added)
Estimated significant reduction of the predicted uncertainty for integral quantities (in progress)
Summary