## Slide 1: Clearing a path through fog droplets using a short-pulse (sub-nsec) CO2 laser Proposal # 304285
Rich Fischer, Ted Jones, Bahman Hafizi, Dan Gordon,
Yu-hsin Chen, and Joe Penano
Naval Research Laboratory, Washington, DC
2019 ATF Users Meeting: New Proposal
Funding source and status (submitting to ONR)
Tony Ting
University of Maryland
Victor Hasson
University of Arizona

## Slide 2: Scientific Case – Laser vaporization and shattering of fog droplets
IR radiation is strongly absorbed by liquid water (but weakly absorbed by atmospheric gasses)
- Water at λ = 10 um, Lα = 10 um
- Water at λ = 3 um, Lα = 1 um
IR lasers can be used to vaporize and explosively shatter fog droplets
- slow heating: vaporization, cw lasers [1]
- fast heating: vaporization + shattering, shock waves, hot spots, superheat limit (305 deg C) [2]
Typical fog droplets: 1-30 um diameter, 0.1 g/m3 mass loading, -65 dB/km extinction
Droplet scattering can shift from Mie regime to Rayleigh  less scattering along path
- large droplets, Mie σ ~ a2
- small droplets, Rayleigh σ ~ a6 / λ4
Shattering experiments using pulsed IR lasers
- long pulse (20 usec)
- moderate pulse lengths (80 – 400 nsec)
[2] Kafalas and Ferdinand, “Fog droplet vaporization and fragmentation by a 10.6-um laser pulse,” Appl. Optics, 1973.
[1] Mullaney et al., “Fog dissipation using a CO2 laser,” Appl. Physics Letters, 1968.

## Slide 3
Laser transmission through a single water droplet
Kwok et al., “Enhanced transmission in CO2-laser-aerosol interactions,” Optics Letters, 1988.
Droplet shatter threshold intensity = 20 MW/cm2
At 1 GW/cm2  laser-induced gas breakdown
SLM CO2 laser
80 nsec pulse length
650 mJ
50 um FWHM at focus
Transmission improves as laser intensity increases
Droplet diameter = 53 um

## Slide 4
Benefits of short-pulse (sub-nsec) laser-droplet shattering
Reduced energy to shatter droplet (~ J/cm2)
Longer cleared path
Improved transmission
Faster shattering (use a train of pulses?)
Nonlinear channeling of short IR laser pulses (balance diffractive spreading)
Evaluate ultrafast absorption and heating of liquid water (non-thermal)

## Slide 5: Past Experiment at NRL – cw vaporization of aerosols
Aerosol Generator
L = 100 cm
ID = 10 cm
CW Probe Laser
1.07 um, 2 kW
0.53 um, 100 mW
Scattering Diagnostics
Beam Dump
Aerosol Flow (down)
16 um dia
700 droplets / cm3
Aerosol Sizer
0.3 – 20 um dia
filter
CW Heater Laser
Fischer et al., “Absorption and scattering of 1.06 um laser radiation from oceanic aerosols,” Appl. Optics 48, 2009.

## Slide 6: BNL Experiment – short-pulse (sub-nsec) shattering of water droplets
Aerosol Generator
L = 100 cm
ID = 10 cm
CW Probe Laser
Scattering Diagnostics
Beam Dump
Aerosol Flow (down)
Aerosol Sizer
0.3 – 20 um dia
Pulsed CO2 Laser
LWIR, MWIR, SWIR, visible
Use collimated beam through interaction tube

## Slide 7
Program Plans – droplet shattering using OPA
NRL Topas OPA laser
Perform single-droplet shattering experiments at different IR wavelengths
Pulse length 50 fs - psec

## Slide 8: Program Plans – droplet shattering using IR lasers
Year 1
Year 2
Vary aerosol parameters at NRL 1-2
Test probe lasers and diagnostics
Conduct laser-aerosol tests at BNL 3-4
Modify set-up as needed
Generate single droplets at NRL 1-4
Shatter single droplets using OPA laser
Quarter

## Slide 9
The following options are available at the laser source.
OPTION 1 (full power, ~1 shot per minute) isotopic gas in final amplifier 2 TW max (2 ps, 4 J, single pulse) 9.25 um M^2 ~ 2 linear polarization OPTION 2 (regen only, 1.5 or 3 Hz) 3 GW max (2 ps, 6 mJ) 9.25 um M^2 ~ 1.5 linear polarization (circular available at slightly reduced power)
** Please note any specialty laser configurations here **
Pulse length: 60 psec (2 psec)
Vary fluence ~ J/cm2
Beam diameter ~ few cm
Interaction Point location: Laser room
CO2 Laser Requirements

## Slide 10
2019 Experiment Time Estimates
Run Hours (include setup time in hours estimate):
Number of CO2 laser hours delivered to laser experiment hall (”FEL room”): 120 hours
Overall % setup time: 20%
Hazards & installation requirements:
Large installation (chamber, insertion device etc…): N
Laser use (other than CO2): Yes
Cryogens: N
Introducing new magnetic elements: N
Introducing new materials into the beam path: N
Any other foreseeable beam line modifications: N
Please describe further where necessary
Possible probe lasers for aerosol shattering experiments
- LWIR (9-11 um)
- SWIR (1.5 um)
- visible (0.5 um)

## Slide 11
Back-up Slides

## Slide 12
Kafalas and Ferdinand, “Fog droplet vaporization and fragmentation by a 10.6-um laser pulse,” Appl. Optics 12 (1973)
Scientific Case – Laser vaporization and shattering of fog droplets

## Slide 13: Scientific Case – Laser vaporization and shattering of fog droplets

## Slide 14: Scientific Case – Laser vaporization and shattering of fog droplets
V. Chimelis, “Extinction of CO2 laser radiation by fog and rain,” Appl. Optics, 1982.
σ = 147 W / km
W = 0.1 g/m3 typical fog mass loading
σ = 14.7 x 4.34 = 63.8 dB/km agrees with measurements
fog mass loading can be higher than 0.1 g/m3
mass loading often increases with altitude (NASA aircraft measurements)

## Slide 15: Experimental Setup