## Slide 1: 21st ATF Users’ Meeting
Operations Status

## Slide 2: Outline
2018 recap
  Availability
  User activities
  Operations activities
Operations Status: What is available in 2019?
  Capability operational status update
  Available parameters
  Available facilities
Recap of user resources and responsibilities
  Time requests
  Beam scheduling
  Run reports

## Slide 3: Availability
Resource | Planned Hours | Delivered Hours | % of Planned
Electron Beam | 830 | 751 | 90
CO2 Laser | 700 | 849 | 121
UED | 830 | 929 | 112
Total | 2360 | 2529 | 107
Resource | Planned Hours
Electron Beam | 640
CO2 Laser | 640
UED | 740
Total | 2020
2019
2018
Chart: 12 Experiments Served
| Electron Beam | Laser | Combined | UED
Experiments Served | 3 | 2 | 3 | 4
Availability

## Slide 4: User Activities Breakdown
Chart: Accelerator
| Run | Setup
Column1 | 349 | 402
Chart: CO2 Laser
| Run | Setup
Column1 | 495 | 354
Chart: UED
| Run | Setup
Column1 | 743 | 186
UED now set up for turn-key materials science operations
Most setup time for accelerator focused experiments
Advanced accelerator experiments have a wide range of complex requirements

## Slide 5: FY18 Summary (hours)
Chart: Laser Operations Activities
| User Experiment | Scheduled Down | Unscheduled Down | Scheduled Maintenance | Unscheduled Maintenance | Facility Development
Accelerator Operations Activities | 849 | 337 | 128 | 116 | 56 | 623
Chart: 
| User Experiment | Scheduled Down | Unscheduled Down | Scheduled Maintenance | Unscheduled Maintenance | Facility Development
Accelerator Operations Activities | 751 | 356 | 732 | 60 | 106 | 160
Chart: UED
| User Experiment | Scheduled Down | Unscheduled Down | Scheduled Maintenance | Unscheduled Maintenance | Facility Development
Distribution of Operations Activities Relating to UED | 929 | 529 | 6 | 32 | 49 | 500
92 Users
Down time:
Ebeam – klystron replacement and commissioning
Laser – R&D
UED – Cathode cleaning and gun optimization

## Slide 6: Operational Status: Available User Time
2019 Resource | Planned Hours | FY18 Delivered | FY19/FY18 (% Ratio)
Electron Beam | 640 | 751 | 85%
CO2 Laser | 640 | 849 | 75%
UED | 740 | 929 | 80%
Total | 2020 | 2529 | 80%
Planning currently underway to try to bring FY19 hours in line with FY18.

## Slide 7: Operational Status
Electron Beam
  Linac Klystron replacement and commissioning complete
  Presently approved for operations up to 60 MeV
  Safety approval will be sought for higher energies as needed
  Gun klystron maintenance complete
CO2 Laser
  Mixed isotope CO2 gas now in main amplifier
  Plasma shutter installed to allow higher power delivery to experiments
  CPA optimization for mixed isotope setup continues
  Vacuum delivery system in commissioning to deliver higher power to laser experiments and BL1 interaction points
UED
  Routine turn-key operation for materials science experiments
  Cathode cleaning complete and further gun optimization underway

## Slide 8: Electron Beam
Parameter | Nominal | Requested
Beam Energy (MeV) | 50-65 | Full range is ~ 15-75 MeV with highest beam quality at nominal values
Bunch Charge (nC) | 0.1-2.0 | Bunch length & emittance vary with charge
Compression | Down to 100 fs (up to 1 kA peak current) | A magnetic bunch compressor available to compress bunch down to ~ 100 fs. Beam quality is variable depending on charge and amount of compression required.
Transverse size at IP (sigma, um) | 30 – 100 (dependent on IP position) | It is possible to achieve transverse sizes below 10 um with special permanent magnet optics.
Normalized Emittance (um) | 1 (at 0.3 nC) | Variable with bunch charge
Rep. Rate (Hz) | 1.5 | 3 Hz also available if needed
Trains mode | Single bunch | Multi-bunch mode available. Trains of 24 or 48 ns spaced bunches.
Special Equipment:
  Please indicate any special equipment that you expect to need, including (but not limited to) the transverse deflecting cavity, shaped bunch using mask technique, plasma capillary discharge system, bolometer/interferometer setup etc.
User Slide

## Slide 9
The following options are available at the laser source. Note that the maximum power available at your experiment interaction point will depend on the laser transport method.
OPTION 1 (full power, ~1 shot per minute) isotopic gas in final amplifier 2 TW max (2 ps, 4 J, single pulse) 9.25 um M^2 ~2 linear polarization OPTION 2 (regen only, 1.5 or 3 Hz) 3 GW max (2 ps, 6 mJ) 9.25 um M^2 ~1.5 linear polarization (circular available at slightly reduced power)
** Please note any specialty laser configurations here **
Interaction Point location: Laser room/electron experiment hall - delete as necessary (the highest peak power can be delivered to the laser room chamber and 2 beamline #1 chambers. CO2 laser delivery to beamline #2 will see lower power due to necessary transport in air.)
CO2 Laser
User Slide

## Slide 10: UED
Parameter | Nominal | Requested
Beam Energy (MeV) | 3 MeV | 3 MeV is the maximum beam energy available. Higher energies may be considered
Bunch Charge (pC) | 4.0 | Range 0.05 – 4.0. Bunch length & emittance vary with charge
Rep. Rate (Hz) | 5 | 1 - 5 Hz at present
Special Equipment:
  Please indicate any special equipment that you expect to need.
Sample Materials:
  Please provide a list of materials that you will install in the beam path.
User Slide

## Slide 11: 6 Available IPs
FEL room – high power CO2 delivered to ion chamber with gas jet capability
BL1 – 3 chambers.
  IGS chamber for electron beam-only experiments
  LWFA chamber for laser–ebeam experiments plus gas jet capability
  Compton chamber for laser-ebeam interaction
BL2 – 1 chamber + 1 insertion device IP
  Plasma chamber with capillary discharge capability and laser delivery
  Designated area for wiggler structures etc. with laser interaction capability
  Laser delivery to both IPs at reduced power – vacuum transport does not extend beyond BL1
  Deflecting cavity diagnostic

## Slide 12: Time Request
For new experiments and experiments wishing to continue into 2019, a time request must be submitted at pass.bnl.gov

## Slide 13: Beam Scheduling and Planning
  Check the online schedule from the Operations tab on the ATF homepage
  Submit a beam time request https://surveys.external.bnl.gov/n/ATFShiftRequest.aspx
  Check that your experimental safety review is in place, email Karl Kusche (kusche@bnl.gov)
  Submit installation and run plans to atf@bnl.gov
  Read the Users’ Place section of the ATF website
  Attend the 9 am Monday planning meeting, during your run, to coordinate technical support and experiment requirements

## Slide 14: Run Reports
The lead experimenter should attend the ATF weekly meeting at 4 pm each Friday, during their run, to report that week’s progress.
PI’s should inform the ATF if they wish to designate a second person to be the main point-of-contact or lead experimenter
Submit an end-of-run survey form within 2-weeks of the run end, at https://surveys.external.bnl.gov/n/ATFUsersRunReport.aspx