## Slide 1: IFEL Acceleration with Optical Energy Recovery
Alex Murokh1 and Pietro Musumeci2,
1RadiaBeam Technologies, LLC.
2UCLA Department of Physics and Astronomy
2019 ATF Users Meeting: Future Proposals
Funding source and status: Proposals in progress to multiple agencies

## Slide 2: Scientific Case
High intensity, compact (< 10 m), 10 MeV class gamma ray source:
150 MeV injector
~ 10 TW igniter laser (i.e. 1064 nm)
IFEL 1 GeV energy booster stage
ICS interaction chamber
TESSA decelerator for laser power recovery
Injector SRF Linac
Gamma-rays

## Slide 3: Scientific Case
TESSA decelerator
~ 100 MeV
High intensity, compact (< 10 m) 10 MeV class gamma ray source:
150 MeV injector
~ 10 TW igniter laser (i.e. 1064 nm)
IFEL 1 GeV energy booster stage
ICS interaction chamber
TESSA decelerator for laser power recovery
photoinjector
linac
2 x Prebuncher
IFEL accelerator
Igniter laser
ICS
Beam dump
Pockels cell
Gamma rays
~ 150 MeV
~ 1 GeV

## Slide 4: Experimental Setup
Build another Rubicon undulator in TESSA configuration
Measure acceleration and deceleration in sequence
Demonstrate good capture
4
TESSA decelerator
~ 40 MeV
photoinjector
linac
2 x Prebuncher
IFEL accelerator
CO2 laser
Beam dump
~ 50 MeV
~ 100 MeV
Long laser pulse
Phase shifter

## Slide 5: Plans
Find funding
  new SBIR proposals (DOE and DOD)
  AFRL proposal
  Phase IIB for AE76, etc.
Design the experiment in detail
  Model the dynamics and optimize for longer laser Rayleigh range
  Design non-invasive energy distribution measurement in the middle section
Submit formal proposal at the next ATF Users meeting

## Slide 6
Parameter | Nominal | Requested
Beam Energy (MeV) | 50-65 | 50-55 MeV
Bunch Charge (nC) | 0.1-2.0 | 0.1-0.3 nC
Compression | Down to 100 fs (up to 1 kA peak current) | ~ 0.3 ps
Transverse size at IP (sigma, um) | 30 – 100 (dependent on IP position) | ~ 50 µm
Normalized Emittance (um) | 1 (at 0.3 nC) | 1 (at 0.3 nC)
Rep. Rate (Hz) | 1.5 | 1.5
Trains mode | Single bunch | Single bunch
Electron Beam Requirements

## Slide 7
The following options are available at the laser source. Note that the maximum power available at your experiment interaction point will depend on the laser transport method.
OPTION 1 (full power, ~1 shot per minute) isotopic gas in final amplifier 1-2 TW (1-2 ps, 2 J, single pulse) 9.25 um M^2 ~2 circular polarization
CO2 Laser Requirements
2019 Experiment Time Estimates
N/A