## Slide 1: Archiving storage
Technology meeting
Evaluation of IBM TS4500

## Slide 2: Long Term Storage
Keeping 100+ PB data for a long time
Reliability
Performance
Life Expectancy
Scalability
Tape: 30 years
T10K, LTO-7, LTO-8, IBM JD: 1 x 1019
Bit Error Rate (BER): Number of user bits transferred between two unrecoverable error events
1 error event in 1.25 exabytes *
Just add more tape cartridges.
Add more tape libraries.
T10K | LTO-7 | LTO-8 | IBM JD
250 MB/s | 300 MB/s | 360 MB/s | 360 MB/s
* https://www.lto.org/wp-content/uploads/2014/07/LTO_Get_The_Facts_10_15.pdf
9940B tapes in round silo (9-15 years old) migrated to LTO:
99.9% successful rate

## Slide 3: Scalability
- Add Tapes
Increasing Capacity

## Slide 4: scalability
Library Full?
Add Library

## Slide 5: Scalability
- Add Tape Drives
LTO-7: 300 MB/s
Increasing Bandwidth
Bandwidth can be expended easily by adding more drives
Bandwidth can be controlled easily by allocating number of drives.
To install a tape drive, about 45 minutes, ready to use.
30 minutes to put a drive into library, 15 minutes to config.

## Slide 6: Tape Reliability
Media Types | Cartridges | Average Mounts | Max Mounts
LTO-7 | 10,219 | 31.2 | 736
LTO-6 | 22,445 | 52.8 | 664
LTO-5 | 15,684 | 67.3 | 1,225
We have near zero failures with LTO-6 and LTO-7
Recalled 10,310,154 files from LTO-7
Recalled 20,510,168 files from LTO-6
Most of the IO errors were caused by excessive usage of our tape drives
Drive Types | Loaded
LTO-7 | 360 k
LTO-6 | 1,218 K
LTO-5 | 780 K

## Slide 7: Tape Reliability
Media Types | Cartridges | Average Mounts | Max Mounts
LTO-7 | 9,057 | 31.2 | 736
LTO-6 | 22,345 | 52.8 | 664
LTO-5 | 15,684 | 67.3 | 1,225
We have near zero failures with LTO-6 and LTO-7
Recalled 10,310,154 files from LTO-7
Recalled 20,510,168 files from LTO-6
Most of the IO errors were caused by excessive usage of our tape drives
Drive Types | Loaded
LTO-7 | 360 k
LTO-6 | 1,218 K
LTO-5 | 780 K
2015 LTO-6
2017 LTO-7
2012 LTO-5

## Slide 8: Change!
Oracle dropped Tape Drive Development – No T10K-E
Oracle made no any official announcement about the the future of tape business
Oracle products are expensive
LTO 7 Drive:
Rumor: Oracle will increase the support cost
Other National Labs already moved:
Oracle | IBM
~$13K | ~$8K
Organization | Library | Tape Drive
CERN | IBM TS4500 | IBM TS1155
Oak Ridge | SpectraLogic | IBM TS11xx
NERSC | IBM TS4500 | IBM TS1155
Fermilab | IBM TS4500 | LTO-8
LANL | IBM TS4500 | ?

## Slide 9: Other users
We (Tier-1) are no longer the largest tape users
The major tape users are the cloud and social media companies.
The cloud companies are switching to new libraries and new tape drives

## Slide 10: Oracle SL8500
Library Capacity: 10,088 Tapes
LTO-7: 60,528 TB or 60.5 PB
39 tapes per load
Tape initializing:
1 min/tape-drive
Provide 1 PB storage
LTO-7: 3.5 hours
LTO-8: 1 hr 42 min
LTO-8: 121,056 TB or 120 PB
39 LTO-7 = 234 TB
Will take ~ 7 minutes
Dual CAPs
78 tapes per load

## Slide 11: Oracle SL8500 - Expanding library
Max 32 silos
Basic config:
3 Modules
Drives Module
Robotic Module
Interface Module
Storage Expansion Modules (max 5)
Max config:
8 Modules
10,088 slots
Must grow to the left

## Slide 12: Oracle sl8500 expansion map

## Slide 13: Max Drive bays
64 Tape Drives / Library
LTO-7: 64 x 300 MB/s = 19.2 GB/s
LTO-8: 64 x 360 MB/s = 23 GB/s

## Slide 14: Performance
4 Levels (LSM)
All cartridges are on the same tier (Tier 0)
Cartridges can be moved to a different LSM via elevators
It will take addition time to move a tape to a different LSM. (~25 sec)
Mount a tape
Robot find the tape
Delivery the tape to a specified drive
Load the tape (positioning)
Read data
Requesting a 1 G file on LTO-7 from HPSS may take 33 sec to complete
Cartridge Slots
Robot
, dual robots on each level
Elevator

## Slide 15: IBM TS4500
Dual input/output (I/O) slots, 16 each
Tape initializing:
1 min/tape-drive
Provide 1 PB storage
JD: 1 hour 22 min
LTO-7: 3.5 hours
32 JD = 480 TB
36 LTO 7 = 216 TB
36 LTO 8 = 432 TB
I/O Station
32 JD cartridges per load, 36 LTO cartridge
2 min 5 sec to fill the 16 slot tray and place tray in library (manual effort)
1 min 5 sec for the robot to put the tapes to slots** (robotic automation)
Assume 32 tapes would need 2 x time: 3 min 10 sec x 2 = 6 min 20 sec.
Average 12 sec per tape
In theory!
We do not know the overhead due to the high density tray.
Worst case? 4x longer?
JD: 6 hours?
LTO-7: 14 hours?

## Slide 16: IBM TS4500 - Expanding the capacity
Grow either way
L Frame
S Frame
S Frame
S Frame
D Frame
S Frame
L Frame – Base unit, with drives
D Frame – with drives
Max 7 D Frame
I/O Station is optional
S Frame – no drives
Each frame can be either
LTO or TS Technologies
Maximum 18 frames
Maximum 8 “Drive” frames
1 L Frame
7 D Frame
Maximum 8 x 2 I/O stations
256 TS Tapes
288 LTO Tapes

## Slide 17: IBM TS4500 - Accessors (robots)
Drive
Frame
Drive
Frame
Dual Accessors (robots)
One for left 1/2
One for right 1/2

## Slide 18: Oracle SL8500 Space usage
Tapes can travel across libraries

## Slide 19
595.8”
47.7”
107.7”(8’11”
30” Clearance required on all sides, 36 “ recommended.
535.8”
TS4500 Floor layout with required service clearance
18 Frame Dual Accessor (HA)
TOP VIEW
1
Back
Front
Note: not drawn to scale
16
14
15
2
3
10
4
12
5
7
6
8
9
11
13
17
18
30”
30”
IBM TS4500 Space REQUIREMENT

## Slide 20: IBM TS4500 Space usage
18 Frame library
18 Frame library
18 Frame library
72”
30”
minimum
Tapes can NOT travel across libraries

## Slide 21: IBM TS4500 - cartridge slots
Tier-0 High Performance
High Density slots
Tier-0 : slots on the door
High Density slots: 4 or 5 cartridges per slot
IBM TS (J series): Tier-1 – Tier-4
LTO : Tier-1 – Tier-5

## Slide 22: IBM TS4500 - cartridge slots
Tier-0 High Performance
High Density slots
Tier-0 : slots on the door
High Density slots: 4 or 5 cartridges per slot
IBM TS (J series): Tier-1 – Tier-4
LTO : Tier-1 – Tier-5
Tier-1
Tier-2
Tier-3
Tier-4
Tier-5
Top view of High Density slots

## Slide 23: IBM TS4500 - cartridge slots
Tier-0 High Performance
High Density slots
Tier-0 : slots on the door
High Density slots: 4 or 5 cartridges per slot
IBM TS (J series): Tier-1 – Tier-4
LTO : Tier-1 – Tier-5
Tier-1
Tier-2
Tier-3
Tier-4
Tier-5

## Slide 24: IBM TS4500 - cartridge slots
Tier-0 High Performance
High Density slots
Tier-0 : slots on the door
High Density slots: 4 or 5 cartridges per slot
IBM TS (J series): Tier-1 – Tier-4
LTO : Tier-1 – Tier-5
Tier-1
Tier-2
Tier-3
Tier-4
Tier-5

## Slide 25: IBM TS4500 - cartridge slots
Tier-0 High Performance
High Density slots
Tier-0 : slots on the door
High Density slots: 4 or 5 cartridges per slot
IBM TS (J series): Tier-1 – Tier-4
LTO : Tier-1 – Tier-5
Tier-1
Tier-2
Tier-3
Tier-4
Tier-5
Cartridge in Tier-4 takes extra ~27 seconds

## Slide 26: IBM TS4500 - cartridge slots
Tier-0 High Performance
High Density slots
Tier-0 : slots on the door
High Density slots: 4 or 5 cartridges per slot
IBM TS (J series): Tier-1 – Tier-4
LTO : Tier-1 – Tier-5
Tier-1
Tier-2
Tier-3
Tier-4
Tier-5
Cartridge in Tier-4 takes extra ~27 seconds

## Slide 27: Robots vs accessor
Dual Robots
Max 8 robots
Max 8 Tapes can be mounted at the same time, if 2 tapes from each LSM
Oracle SL8500
IBM TS4500
Dual Accessors
Dual grabbers
Max 2 Tapes at once

## Slide 28: Robots vs accessors
Oracle SL8500
8 robots
IBM TS4500
2 x dual grabbers
8 tapes
4 tapes
This is in theory!
Faster?

## Slide 29: Robots vs accessor – possible scenarios 1
Need to mount a tape from level 1
Next available drive is in level 4
Oracle SL8500
IBM TS4500
2D, No elevator!
3 steps, slow!
Extra ~25 sec
Faster!

## Slide 30: Robots vs accessor – possible scenarios 2
All needed tapes are on the same LSM
Only 2 robots
Oracle SL8500
IBM TS4500
2 Accessors
About the same!

## Slide 31: Robots vs accessor – possible scenarios 3
All tapes are on Tier-0
Oracle SL8500
IBM TS4500
<40 % Full, all Tier-0 and Tier-1
Faster!
Tier-0 High Performance
High Density slots
~60 % Full, 20% tapes in Tier -2
Expect slower!
> 60 % Full,
Tier-3 and 4 are used
Expect much slower!

## Slide 32: MOUNT + read: SL8500+LTO7 vs TS4500+JD
Read 1 GB (1st file)
SL8500 (Tier-0): 34 sec (2,0,26,2,1 -> 2,0,1,3)
TS4500 (Tier-0): 27 sec
TS4500 (Tier-4): 54 sec
LTO-7: 300 MB/s
TS1150 + JD: 360 MB/s
Read 10 GB (1st file)
SL8500 (Tier-0): 1 min 24 sec
TS4500 (Tier-0): 1 min 17 sec
TS4500 (Tier-4): 1 min 33 sec
Faster!
Slower! (27 secs to move a tape out of Tier-4)
Faster!
Slower!
TS4500 Read 3 tapes from Tier-4
1 G (Tier-4): 54 sec
10 G (Tier-4): 1 min 33 sec
1 G (Tier-4): 1 min 23 sec
1st tape
2nd tape Larger file!
3rd tape, slowing down
Dual grabber, can grab 2 tapes

## Slide 33: Conclusion: Tape mount
TS4500 Tier-0 vs SL8500 same LSM
TS4500 is ~7 sec faster
TS4500 Tier-4 (+27 sec) vs SL8500 across 4 LSM (+25 sec)
SL8500 is ~2 sec faster (assume SAME)
There are 4 LSM in SL8500
There are 4 Tiers in TS4500 (HD)
However, when the library is near full, TS4500 need to find room to swap the tapes out.
This might be very time consuming.
Tape mount is an issue ONLY when reading a few files per tape. When reading more files from a single tape, the weight of tape mount time becomes less important.
Mount rate maybe the same
There are 5 Tiers when using LTO
Mount rate for T-5 maybe slower
TS4500 has ”intelligent algorithm” to keep cold tape to deeper tier, frequent accessed tape in the front tier.

## Slide 34: Other TS4500 users: Tape mount
CERN do not see any tape mount issue with TS4500
No one really see any significant difference in tape mount performance
The earlier version of IBM library: TS3500 had many issues
However, the new TS4500 is much better than TS3500

## Slide 35: Max Read performance: LTO7 vs TS1150/JD
LTO-7: 300 MB/s
TS1150 + JD: 360 MB/s
Big file (10GB) | LTO-7 | TS1150 | Gain %
10% 80 files | 103.9 | 153.35 | 47.59%
50% 400 files | 156.97 | 242.47 | 54.47%
100% 800 files | 251.87 | 352.84 | 40.09%
Small file (1GB) | LTO-7 | TS1150 | 
10% 980 files | 32.33 | 73.69 | 127.93%
50% 5811 files | 120.24 | 177.04 | 47.24%
100% 9793 files | 236.03 | 343.98 | 45.74%
Aggregated Small file (1GB) | LTO-7 | TS1150 | 
10% 979 files | 35.44 | 39.82 | 12.36%
50% 4899 files | 136.35 | 177.80 | 30.40%
100% 9798 files | 252.19 | 345.61 | 37.04%
Chart: LTO-7 vs TS1150 Large File Staging Test (10 GB) Even Spacing
| 10% 80 files | 50% 400 files | 100% 800 files
LTO-7 | 103.9 | 156.97 | 251.87
TS1150 | 153.35 | 242.47 | 352.84

## Slide 36: Max Read performance: LTO7 vs TS1150/JD
LTO-7: 300 MB/s
TS1150 + JD: 360 MB/s
Big file (10GB) | LTO-7 | TS1150 | Gain %
10% 80 files | 103.9 | 153.35 | 47.59%
50% 400 files | 156.97 | 242.47 | 54.47%
100% 800 files | 251.87 | 352.84 | 40.09%
Small file (1GB) | LTO-7 | TS1150 | 
10% 980 files | 32.33 | 73.69 | 127.93%
50% 5811 files | 120.24 | 177.04 | 47.24%
100% 9793 files | 236.03 | 343.98 | 45.74%
Aggregated Small file (1GB) | LTO-7 | TS1150 | 
10% 979 files | 35.44 | 39.82 | 12.36%
50% 4899 files | 136.35 | 177.80 | 30.40%
100% 9798 files | 252.19 | 345.61 | 37.04%
Chart: LTO-7 vs TS1150 Small File Staging Test (1 GB) Even Spacing
| 10% 980 files | 50% 5811 files | 100% 9793 files
LTO-7 | 32.33 | 120.24 | 236.03
TS1150 | 73.69 | 177.04 | 343.98

## Slide 37: Max Read performance: LTO7 vs TS1150/JD
LTO-7: 300 MB/s
TS1150 + JD: 360 MB/s
Big file (10GB) | LTO-7 | TS1150 | Gain %
10% 80 files | 103.9 | 153.35 | 47.59%
50% 400 files | 156.97 | 242.47 | 54.47%
100% 800 files | 251.87 | 352.84 | 40.09%
Small file (1GB) | LTO-7 | TS1150 | 
10% 980 files | 32.33 | 73.69 | 127.93%
50% 5811 files | 120.24 | 177.04 | 47.24%
100% 9793 files | 236.03 | 343.98 | 45.74%
Aggregated Small file (1GB) | LTO-7 | TS1150 | 
10% 979 files | 35.44 | 39.82 | 12.36%
50% 4899 files | 136.35 | 177.80 | 30.40%
100% 9798 files | 252.19 | 345.61 | 37.04%
Chart: LTO-7 vs TS1150 Aggregated Small File Staging (1 GB) Even Spacing
| 10% 979 files | 50% 4899 files | 100% 9798 files
LTO-7 | 35.44 | 136.35 | 252.19
TS1150 | 39.82 | 177.8 | 345.61

## Slide 38: Max Read performance: LTO7 vs TS1150/JD
LTO-7: 300 MB/s
TS1150 + JD: 360 MB/s
Big file (10GB) | LTO-7 | TS1150 | Gain %
10% 80 files | 103.9 | 153.35 | 47.59%
50% 400 files | 156.97 | 242.47 | 54.47%
100% 800 files | 251.87 | 352.84 | 40.09%
Small file (1GB) | LTO-7 | TS1150 | 
10% 980 files | 32.33 | 73.69 | 127.93%
50% 5811 files | 120.24 | 177.04 | 47.24%
100% 9793 files | 236.03 | 343.98 | 45.74%
Aggregated Small file (1GB) | LTO-7 | TS1150 | 
10% 979 files | 35.44 | 39.82 | 12.36%
50% 4899 files | 136.35 | 177.80 | 30.40%
100% 9798 files | 252.19 | 345.61 | 37.04%
Chart: LTO-7 vs TS1150 Aggregated Small File Staging (1 GB) Even Spacing
| 10% 979 files | 50% 4899 files | 100% 9798 files
LTO-7 | 35.44 | 136.35 | 252.19
TS1150 | 39.82 | 177.8 | 345.61
Chart: LTO-7 vs TS1150 Large File Staging Test (10 GB) Even Spacing
| 10% 80 files | 50% 400 files | 100% 800 files
LTO-7 | 103.9 | 156.97 | 251.87
TS1150 | 153.35 | 242.47 | 352.84
Chart: LTO-7 vs TS1150 Small File Staging Test (1 GB) Even Spacing
| 10% 980 files | 50% 5811 files | 100% 9793 files
LTO-7 | 32.33 | 120.24 | 236.03
TS1150 | 73.69 | 177.04 | 343.98
84%
98%
LTO Tapes drives supports offset ordered recalls (Sequentially Access)
The serpentine nature of tape may still result in long seek times between file reads
This example illustrates 5:16 of tape movement without tape I/O
File 1
File 2
File 3
File 4
File 5
39 sec
48 sec
45 sec
19 sec
93 sec
Enterprise tape drives now support Recommended Access Ordering (RAO)
Multiple tape recalls are properly ordered by the tape drive to reduce recall time
Tests show that RAO improves multiple file recalls by 30% to 60%
This SAME example illustrates 2:06 of tape movement without tape I/O
File 2
File 4
File 1
File 5
File 3
21 sec
13 sec
14 sec
58 sec
8 sec
12 sec
Reference: HPSS An overview, Jim Gerry (IBM)2
72 sec

## Slide 39: Recommended Access Order (RAO)
File 1
File 2
File 3
File 4
File 5
LTO Tapes drives supports offset ordered recalls (Sequentially Access)
The serpentine nature of tape may still result in long seek times between file reads
This example illustrates 5:16 of tape movement without tape I/O
File 1
File 2
File 3
File 4
File 5
39 sec
48 sec
45 sec
19 sec
93 sec
72 sec
21 sec
13 sec
14 sec
58 sec
8 sec
12 sec
Reference: HPSS An overview, Jim Gerry (IBM)2
Enterprise tape drives now support Recommended Access Ordering (RAO)
Multiple tape recalls are properly ordered by the tape drive to reduce recall time
Tests show that RAO improves multiple file recalls by 30% to 60%
This SAME example illustrates 2:06 of tape movement without tape I/O

## Slide 40: Max Read performance: RAO Test
LTO-7: 300 MB/s
TS1150 + JD: 360 MB/s
Big file (10GB) | No RAO | RAO | Gain %
10% 80 files | 153.35 | 244.61 | 59.51%
50% 400 files | 242.47 | 311.2 | 28.35%
100% 800 files | 352.84 | 332.39 | -5.80%
Small file (1GB) | No RAO | RAO | 
10% 980 files | 73.69 | 105.57 | 43.26%
50% 5811 files | 177.04 | 174.53 | -1.42%
100% 9793 files | 343.98 | 334.72 | -2.69%
Aggregated Small file (1GB) | No RAO | RAO | 
10% 979 files | 39.82 | 20.18 | -49.32%
50% 4899 files | 177.80 | 56.48 | -68.23%
100% 9798 files | 345.61 | 132.08 | -61.78%
Chart: TS1150 Large File Staging Test (10 GB) Even Spacing
| 10% 80 files | 50% 400 files | 100% 800 files
No RAO | 153.35 | 242.47 | 352.84
RAO | 244.61 | 311.2 | 332.39
Chart: TS1150 Small File Staging Test (1 GB) Even Spacing
| 10% 980 files | 50% 5811 files | 100% 9793 files
No RAO | 73.69 | 177.04 | 343.98
RAO | 105.57 | 174.53 | 334.72
Chart: TS1150 Aggregated Small File Staging Test (1 GB) Even Spacing
| 10% 979 files | 50% 4899 files | 100% 9798 files
No RAO | 39.82 | 177.8 | 345.61
RAO | 20.18 | 56.48 | 132.08

## Slide 41: Drive read Perf Conclusion: LTO7 vs TS1150/JD
LTO-7: 300 MB/s
TS1150 + JD: 360 MB/s
Big file (10GB) | LTO-7 | TS1150 | Gain %
10% 80 files | 103.9 | 153.35 | 47.59%
50% 400 files | 156.97 | 242.47 | 54.47%
100% 800 files | 251.87 | 352.84 | 40.09%
Small file (1GB) | LTO-7 | TS1150 | 
10% 980 files | 32.33 | 73.69 | 127.93%
50% 5811 files | 120.24 | 177.04 | 47.24%
100% 9793 files | 236.03 | 343.98 | 45.74%
Aggregated Small file (1GB) | LTO-7 | TS1150 | 
10% 979 files | 35.44 | 39.82 | 12.36%
50% 4899 files | 136.35 | 177.80 | 30.40%
100% 9798 files | 252.19 | 345.61 | 37.04%
84%
98%
TS1150 is much faster than LTO-7
TS1150 can reach 98% efficiency
LTO-7 can only reach 84% the most
Both media can reach max capacity
IBM 3592 JD Media (15 TB): $195
$13/TB
LTO-7 (6 TB): $56
$9.6/TB
Per TB cost, 35% more,
performance is ~50% gain
JE will be released in Nov 20, 18-20 TB

## Slide 42: Proposed config
Back
Front
ATLAS RUN 4: 350 PB/year, ~ 1 PB/day, 43 TB/hr, 12 GB/s
IBM 1155, LTO-8: 360 MB/s, Assume real speed: 250 MB/s.
Need 50 Drives for write
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
Tier-0
Tier-1
Tier-2
Tier-3
Tier-4
Cold (old) data
New data
New data
Should reserve 96 Drives for read + write
Max # of drive/frame: 16, max drive frames: 8, max number of drives: 16x8=128
L
D
D
D
D
D
D
D
Capacity: L: 660, D+IO:660, D:740, S: 1000/798 (end frame)
18 Frames: 15,196 slots (1L + 3xD+IO + 4 x D + 2Send + 8 S)
IO
IO
IO
IO
This config: HP slots: 3280+3080=6,360, HD slots: 8,836
If use JE media: HP slots: 127 PB, HD slots: 176 PB
12 Drives per L/D Frame
1 L, 7 D, Evenly distributed
4 with IO, 4 no IO

## Slide 43: What other Sites doing?
Organization | Library | Qty | Tape Drive | Qty
CERN | IBM TS4500 | 1 (+1 soon) | IBM TS1155 LTO-8 | 46xTS1150, 2xTS1155
Oak Ridge | SpectraLogic |  | IBM TS115x | 
NERSC | IBM TS4500 | 2 | IBM TS1155 | 
Fermilab | IBM TS4500 | 2 (10 frame) | LTO-8 | 56 LTO-8 36 LTO-8
LANL | IBM TS4500 |  |  | 
J-Lab | IBM TS3500 |  | LTO-8 | 8 LTO-8
CSCS | IBM TS4500 |  | IBM TS115x | 30

## Slide 44: Thanks
A special THANK YOU for everyone involved in setting up the IBM loaner library
Guangwei Che
Tim Chou
Ognian Novakov
Frank Burstein
Mark Lukasczyk
John McCarthy
Alexandr Zaytsev