## Slide 1: Accelerator Physics EXperiment
Highlight of RUN 12
M. Bai, C-A Dept., BNL

## Slide 2: Outline
Statistics
Highlights
Summary for RUN12 APEX
Suggestions/plans for future

## Slide 3: APEX Statistics
RUN | Scheduled/Planned[%] | Beam Availability [%]
RUN-3 | 80 | 65
RUN-4 | 90 | 84
RUN-5 | 84 | 83
RUN-6 | 89 | 86
RUN-7 | 92 | 72 (physics: 49%)
RUN-8 | 97 | 83.4 (physics: 59%)
RUN-9 | 98 | 82.9 (physics: 54%)
RUN-10 | 79 | 82.5 (physics: 83%)
RUN-11:pp | 42 | 92 (physics: 37%)
RUN-11:Au | 63 | 78.5 (physics: 59%)
RUN-12:pp | 134 | 86.8
RUN-12:ion | 61 | 93.7

## Slide 4: Detailed Statistics
Courtesy of P. Ingrassia
Run12 | scheduled | scheduled | APEX | APEX | actual | APEX | Failure | APEX/scheduled
date | interval | duration (h) | START | END | duration (hh:mm:ss) | hours(OpLog) | hours | %
22-Feb | 0800-2400 | 16 | 2/22/12 8:00 | 2/22/12 23:35 | 15:35:00 | 11.67 | 3.45 | 72.9%
7-Mar | 0800-2400 | 16 | 3/7/12 7:55 | 3/7/12 22:45 | 14:50:00 | 10.53 | 4.27 | 65.8%
21-Mar | 0800-2000 | 12 | 3/21/12 8:00 | 3/21/12 19:10 | 11:10:00 | 9.87 | 1.30 | 82.3%
27-Mar | 2000-0800 | 12 | 3/27/12 20:00 | 3/28/12 7:40 | 11:40:00 | 11.05 | 0.62 | 92.1%
4-Apr | 0800-2000 | 12 | 4/4/12 8:25 | 4/4/12 19:50 | 11:25:00 | 9.7 | 0.00 | 80.8%
12-Apr | 0800-2000 | 12 | 4/12/12 8:00 | 4/12/12 22:00 | 14:00:00 | 11.27 | 2.67 | 93.9%
18-Apr | 1330-0900 | 19.5 | 4/18/12 13:20 | 4/19/12 8:15 | 18:55:00 | 17.33 | 0.82 | 88.9%
2-May | 0800-1900 | 11 | 5/2/12 8:20 | 5/2/12 18:20 | 10:00:00 | 8.7 | 1.13 | 79.1%
30-May | 0800-2300 | 15 | 5/30/12 8:00 | 5/30/12 22:15 | 14:15:00 | 14.22 | 0 | 94.8%
13-Jun | 0800-2400 | 16 | 6/13/12 8:00 | 6/13/12 23:30 | 15:30:00 | 14 | 1.5 | 87.5%

## Slide 5: Studies during RUN12
Study # | title | Studiers | priority | Total time [h]
12-05,06,02 | Beam-beam | White, Luo | 0A | 15
12-07 | V dispersion | Liu | 0A | 5.5
12-12,13 | High intensity proton | Montag | 0A | 19
12-09 | BBA | Beebe, Zieger |  | 10
11-30 | Beam-beam and space charge | Fedetov | 0A | 3
10-15 | Phase shifter | Montag | 1A | 4.5
 | Local coupling | Marusic |  | 4
11-33 | IP transfer matrix | Tepikian, Ptitsyn | 0A | 4.5
11-21 | Off-momentum beta beat | Luo | 0A | 2
 | Polarization lifetime | Bai |  | 8

## Slide 6: Studies during RUN12
Study # | title | studiers | priority | Total time [h]
12-17 | Long. Matching w.o. gammaT | Montag | 0A | 4
12-07 | V dispersion | Liu | 0A | 10
11-17 | Spin flipper | Bai, Oddo, Roser, Dawson | 0A | 5.5
11-16 | Optics correction | Bai, White, GRD | 0A | 5.5
11-18 | PoP of CeC | Igor, Wang | 1A | 2
12-10 | 9MHz cavity bunch intensity limit | Bai,Hao,Blaskiewicz, Brennan | 0A | 1

## Slide 7: RUN 12
A total of 19 proposals submitted before the start of run 13. 4 proposals received during the run with one proposal received closed to the end of run
19 beam studies were carried out
  11 from 2012 proposal and 8 on-going from previous proposals
Still a mixture of APEX and MD
  which compensated the reduction of MD during this pp run

## Slide 8: Highlights from APEX-12
Effect of spin harmonic: Vahid
  Developed a technique to use a set of correctors to change the imperfection resonance strength at a certain location, spin harmonics
  This was implemented during the ramp in both rings, one at Ggamma=411-nu and another at Ggamma=393+nu

## Slide 9: Highlights from APEX-12
Polarization lifetime without collisions
  Evaluate the effect of snake resonance at 11/16
  Evaluate beam-beam contribution to polarization lifetime
Qx=0.69
Qy=0.68
Qx=0.695
Qy=0.6875

## Slide 10: Highlights from APEX-12
Polarization lifetime without collisions
  11/16 snake resonance is not the dominant source of
  polarization lifetime for physics store
  Data indicates the polarization lifetime is affected by
  beam-beam.

## Slide 11: Highlights from APEX-12
Phase shifter: Montag, Bai, Simon, Minty, etc.
  Motivation: to see whether one can measure phase advance change induced by phase shifter
  Phase shifter:
    To provide integer multiple of pi phase advance between IP8 and IP10 to compensate the beam-beam at IP8 with e-lens at IP10
    two shunt power supplies to main quads in arc IP8 – IP10
Blue at injection
A vertical betatron
phase different of
~32 degrees with
phase shifter at 10A
was measured

## Slide 12: Highlights from APEX-12
Beam-beam: Simon, Yun
  Tune scan for pi-mode suppression
    BTF measurements of store with split tune shows significant suppression of pi mode

## Slide 13: Highlights from APEX-12
Beam-beam: Simon, Yun
  Tune scan for pi-mode suppression
    BTF measurements of store with split tune shows significant suppression of pi mode
    However, it is proven to be non-operational due to emittance blowup. Poor polarization lifetime also confirmed the observation in RUN2004
  Understand why coherent bb mode missing in the horizontal plane
    Impact of coupling
    Impact of 10 Hz feedback
    Impact of white noise
  Understand the effect of coherent modes on beam lifetime
    Excite coherent mode with BBQ kicker. Emittance blowup and deterioration of beam lifetime were observed when BBQ kicker was excited as high as 35dB. No instability was observed

## Slide 14: Highlights from APEX-12
Commissioning of spin flipper/tunemeter
  A group of 5 AC dipoles interwined with DC dipoles to provide rotating field oscillating at a frequency
  Goal this year is to demonstrate whether we can excite rotating field
x
y
z
Only one resonance is excited

## Slide 15: Highlights from APEX-11
Commissioning of spin flipper/tunemeter

## Slide 16: Highlights from APEX-12
Optics Correction: Bai, GRD, Joe, Simon
  SBST was successfully implemented during APEX
Blue pp @ 255 GeV
Yellow Au @ 100 GeV

## Slide 17: Highlights from APEX-12
Beam-based alignment: Joanne, Jordan
  Motivation: Automated (or faster) BBA application for RHIC to determine difference between electrical center of BPM and mechanical center of nearby quadrupole in the IRs
  Had a long history
    Limited dipole correctors.
    Very large ring. When all the BPMs in all arcs are used, some BPMs contribute to noise more than to signal.
    Signal/Noise ratio is low
  This new effort is to
    Take advantage of improved bpm performance
    Choose subgroup bpms
    minimize the frequency of quadrupole changes
    Automate the measurement

## Slide 18: Highlights from APEX-12
Beam-based alignment: Joanne, Jordan
Q1 & Q3 Completed in both ring (48 BPMs in each ring).
tQ4 in IR 6, 8, 12 in both ring (24 BPMs in each ring).
3. Confirmed some of large offsets. Results are generally good.
Script ready and tested.
Was also implemented to operation
BPM at Q1 & Q3 completed in both rings(24 horizontal, 24 vertical in each ring).
Confirmed some of large offsets(8 in Blue, 10 in Yellow)

## Slide 19
Beam-based alignment: Joanne, Jordan

## Slide 20: Highlights from APEX-12
Local coupling: Marusic
  Automated technique developed by Vadim. Data-taking and analysis are now done in ~15 mins

## Slide 21: Highlights from APEX-12
CeC PoP: Igor, Gang
  Goal: Measure beam parameters critical for CEC POP (jitter, beam spectrum, orbit stability, bunch profiles)
  Set-up
    100 GeV/u gold ions in the yellow ring (left after the previous session with blue ring dumped)
    No re-bucketing, Landau cavity ramped down, no stochastic cooling
    10 Hz orbit feedback on
    Utilized IP4 WCM (used for cogging observation)
    Signal observed on LeCroy WaveRunner 640Zi

## Slide 22: Highlights from APEX-12
CeC PoP: Igor, Gang
  Goal: Measure beam parameters critical for CEC POP (jitter, beam spectrum, orbit stability, bunch profiles)
  Conclusion
    Beam orbit stability and bunch jitter were successfully measured
    We do not expect that the observed beam motion will affect CEC POP experiment, but real data will be used for simulations
    Oscilloscope noise level is above the beam spectrum power in the region of interest, measurement with spectrum analyzer can be done in background mode

## Slide 23: Summary of Run 12 APEX
Beam studies biased towards polarized proton run
  Switched to 12 hour-weekly mode from 16 hour-biweekly mode during pp-255GeV
  Driven by more issues we need to find out
    The limit on intensities
    Look forward to significant intensity increase from e-Lens in the next couple of runs
    Polarization performance
Bridge between APEX outcome and operation
  The goal of APEX is to transfer the benefit to operations
  BBA results were first time applied to operations later in the CuAu run
  Look forward to seeing more benefits to coming run
    Local decoupling
    V dispersion and coupling correction
    Optics correction

## Slide 24: Prepare for RUN 13
Workshop
  Mid-Nov as the primary candidate.
Challenges for the coming RUN
  E-Len commissioning
  Polarization improvement/understanding
  Brighter beam
    Smaller longitudinal emittance
    Smaller transverse emittance
  Instrumentation development
    Novel way of measuring chromaticity
    Polarimeter, polarimeter, …
    High precision bpm development for pEDM

## Slide 25: Process & Rules of APEX
Process
  Submit proposal at http://www.c-ad.bnl.gov/BeamEx/scripts/beform.pl
  Proposal followed by the approval by AEAC committee
    Rating Criteria
      a) relevance to RHIC performance and operation
      b) scientific merit
      c) level of preparedness
Rules
  Prepare study beforehand, including notifying personal support
  Revert changes at the end of study
  Documentation. It is required that each study should be reported in at least one of the forms of
    Informal technote
    Conference proceedings
    journals