## Slide 1: Low Energy RHIC electron Cooling (LEReC): Overview and laser requirements
Alexei Fedotov
on behalf of the LEReC team
Laser Review
November 8-9, 2018

## Slide 2: LEReC Project Goals
The goal of the LEReC project is to provide luminosity improvement for RHIC
operation at low energies to search for the QCD critical point (Beam Energy
Scan Phase-II physics program).
LEReC will be first RF linac-based electron cooler (bunched beam cooling).
To provide luminosity improvement with such approach requires:
Building and commissioning of new state of the art electron accelerator
Produce electron beam with beam quality suitable for cooling
RF acceleration and transport maintaining required beam quality
Achieve required beam parameters in cooling sections
Commissioning of bunched beam electron cooling
Commissioning of electron cooling in a collider
2

## Slide 3: RHIC @ BNL, Long Island, New York
RHIC
NSRL
LINAC
Booster
AGS
Tandems
6:00 o’clock
8:00 o’clock
10:00 o’clock
12:00 o’clock
4:00 o’clock
LEReC
2:00 o’clock
EBIS

## Slide 4
LEReC inside RHIC tunnel at
Interaction Region @ 2 o’clock (IR2)
Cooling sections
Injection Section
(DC photocathode Gun,
SRF Booster cavity)
Laser
Transport beamline

## Slide 5: LEReC Accelerator (100 meters of beamlines with the DC Gun, high-power fiber laser, 5 RF systems, including one SRF, many magnets and instrumentation)
COOLING
in Blue RHIC ring
COOLING
in Yellow RHIC ring
High-Power Beam Dump
Extraction beam line
DC e- Gun
704 MHz SRF
Booster Cavity
2.1 GHz Cu Cavity
9 MHz Cu Cavity
704 MHz Cu Cavity
Injection beam dump
RF Diagnostic Beamline
RHIC TRIPLET
RHIC DX
180°
Bending
Magnet
e-
e-
e-
* NOT to scale
Cathode
loading system
LF solenoid
HF solenoid
Transport solenoid
ERL solenoid
Quad corrector
Trim corrector
Corrector 3.8 ID
Corrector 6.0 ID
BPM 2.4 ID
BPM 4.8 ID
Bellows
Ion pump
Merger
Beamline
Transport
Beamline
704 MHz Cu Deflector Cavity

## Slide 6: Commissioning with e-beam
Phase 1: DC Gun tests (no RF acceleration)
(April-August 2017): DC Gun tests in temporary configuration
(January-February 2018): DC Gun tests in final configuration
Phase 2 (March-September 2018): Full LEReC commissioning
Goals: Meet all required Key Performance Parameters. Achieve high-current operation of accelerator. Achieve electron beam parameters suitable for cooling.
Phase 3 (2018-2019): Transition to operations
Goals: Achieve required stability (energy, orbit) of electron beam. Develop necessary stability, ripple, intensity, orbit feedbacks.
Phase 4 (2019-2020): Commissioning of cooling – requires Au ions at the same energy.

## Slide 7: Commissioning highlights
All major commissioning goals were achieved.
Various LEReC accelerator systems were fully commissioned including RF, instrumentation, controls, etc.
All project Key Performance Parameters were successfully achieved.
Cathode with initial QE around 5% were routinely delivered inside the Gun.
Established operation both with large active cathode area on centre and small active area off centre.
Performed many runs at high-currents of 20-30mA in injection section for cathode QE lifetime measurements and Gun stability studies. Measured QE lifetime was quite long. At 25 mA measured QE lifetime was 142 hours, for example.
Established stable high-current operation of 20mA CW at 1.6MeV all the way to final high power beam dump.
Measured energy spread in RF diagnostics beam line and in cooling sections are within specs for cooling commissioning.
Measured emittance values for various bunch charges in cooling sections are within specs for cooling commissioning.
Commissioned laser intensity feedback. Achieved ~ 0.6% rms laser intensity stability (measured with fast photodiode) and ~ 1% rms electron beam current stability (measured with fast current transformer) with both laser and beam intensity feedback loops.

## Slide 8: Cathode QE lifetime during high current operation
30 mA beam current, t = 87 h, QE > 4%
25 mA beam current, t = 142 h, QE > 4%

## Slide 9: Longitudinal phase space RF gymnastics (704MHz SRF Booster, 3rd harmonic 2.1GHz , 704MHz energy correction cavity and 704MHz deflecting cavity)
Commissioning of longitudinal phase space diagnostics
energy spread
time

## Slide 10: High current operation to high-power dump
20 mA, 09/11/2018
20 mA CW to final high power beam dump at 1.6MeV
With fast (~500 Hz) and slow (~10 Hz) intensity feedback, DI/I < 1% rms

## Slide 11: LEReC electron beam parameters
Electron beam requirement for cooling |  |  | 
Kinetic energy, MeV | 1.6* | 2 | 2.6
Cooling section length, m | 20 | 20 | 20
Electron bunch (704MHz) charge, pC | 130 | 170 | 200
Effective charge used for cooling | 100 | 130 | 150
Bunches per macrobunch (9 MHz) | 30 | 30 | 24-30
Charge in macrobunch, nC | 4 | 5 | 5-6
RMS normalized emittance, um | < 2.5 | < 2.5 | < 2.5
Average current, mA | 36 | 47 | 45-55
RMS energy spread | < 5e-4 | < 5e-4 | < 5e-4
RMS angular spread | <150 urad | <150 urad | <150 urad
*CW mode at 704 MHz without macrobunches is also being considered
(with even higher average current up to 85 mA)

## Slide 12: LEReC beam structure in cooling section
110 nsec,
f=9 MHz
Ions structure:
120 bunches
f_rep=120x75.8347 kHz=9.1 MHz
N_ion=5e8, I_peak=0.24 A
Rms length=3.2 m
1.42 nsec
30 electron bunches per ion bunch
Electrons:
f_SRF=703.5 MHz
Q_e=100 pC, I_peak=0.4 A
Rms length=3 cm
9 MHz bunch structure
Long ion bunches
with new 9MHz RF
Electron Macro-bunch

## Slide 13: LEReC laser requirements (October 2018)
 | Original | Updated
Power on cathode, W | 10 | 6.5
Power on Gun table before iris, W | 15-20 | 10-13
Beam diameter on the cathode, mm | 4-6 | 4-6
Transverse profile | Uniform | Truncated Gaussian (3mm sigma)
Longitudinal profile | Uniform, “flat top” | Stacking with < 40% peak-to-peak modulation
Pulse length after stacking FWHM, ps | 80 | 40-80
Time jitter rms, ps | < 1 | < 1
Intensity rms, shot-to-short. % | < 2 | < 2
Spatial stability C.O.M. on iris rms, um | 10 | 50 (<10um on cathode)
Extinction ratio (power leakage, pulsed mode) | 10^6:1 | 10^6:1
MPS extinction ratio (between MPS interlock and slow shutter closed, full current CW) | 100:1 (5 msec response) | 300:1 (15 msec)

## Slide 14: Laser challenges during commissioning
Pointing stability shot-to-shot of laser beam on the iris: remaining
Pointing stability long-term of laser beam on the iris: remaining
Intensity stability: addressed, met the specs
Transport of high-power beam: achieved about 4W on iris with good transverse profile, which was sufficient due to high cathode QE: need to get to about 10-13W on iris.
Transverse profile on the iris should be approximately Gaussian with sigma=3mm for iris diameter 4-6mm: remaining
- Transverse profile with 4 crystals: was not good
- Transverse profile with 3 crystals plus interferometer: good improvement
Laser transverse and longitudinal profile should stay the same in the Pulsed and CW mode: Transverse profile appears to be different on camera; need for on-demand longitudinal diagnostics remains
Careful alignment of crystals and interferometer was required to achieve small sliced energy spread within electron bunch: addressed

## Slide 15: Shot-to-shot pointing stability
Fast position variations (about 300 um) were observable while observing cameras (1Hz refresh rate)
X and Y laser position in mm.

## Slide 16: Long-term (hours) pointing stability on the iris

## Slide 17: Transverse profile with 4 crystals (June-July)
Laser profile on Gun table without iris

## Slide 18: 4 crystals (June-July): laser profile with iris

## Slide 19: Laser profile on Gun table without and with iris, after switching to 3 crystals plus interferometer

## Slide 20: CW operation, transverse profile on Gun table

## Slide 21: Electron beam longitudinal phase space: laser tuning using electron beam RF diagnostics line
time
energy spread

## Slide 22: Electron beam longitudinal phase space before and after laser tuning
time
energy spread

## Slide 23: Energy spread measurements
RMS momentum spread in RF diagnostics beam line: rms dp/p < 1×10-3
Image on profile monitor (left), sliced energy spread along the bunch (right).
design spec

## Slide 24: Laser intensity fluctuations before feedback

## Slide 25: Before intensity feedback

## Slide 26: Intensity feedback commissioned: 9/07/18
Feedback with two loops
(pdiode and beam current FCT)
No feedback
Single loop
(pdiode only)

## Slide 27: Summary: laser experience during commissioning
Laser supported 24/7 commissioning and worked reliably over many months!
Problems with delivering high CW laser power and good transverse profile with 6 crystals (80ps) and then with 4 crystals (40ps). Situation improved by switching to 3 crystals plus interferometer (40ps). About factor of 2 increase in power is still needed.
Intensity feedback was implemented and achieved required stability.
Remaining major tasks:
Pointing stability
Higher laser power on the cathode
More uniform transverse profile on the cathode
Same laser profiles and performance in pulsed and CW operation