## Slide 1: Low Energy RHIC electron Cooling (LEReC)
High-power Fiber Laser System for LEReC
Zhi Zhao

## Slide 2
Laser parameter review
Laser design and implementation
Conclusion
Outline

## Slide 3
Laser Parameter Review

## Slide 4
Laser Pulse Pattern for LEReC
Pulsed mode: 704 MHz, 9.1 MHz bunch rate, 10-30/bunch
CW mode: 704 MHz

## Slide 5
Stability & reliability
Green average power: 13*2.5 W
Timing jitter: 1 ps rms
“Flat-top” temporal profile
Laser Design Specifications
Spatial profile: M^2<1.2
Pointing stability: 50 µm rms

## Slide 6
Laser Design & Implementation

## Slide 7
Master oscillator power amplifier
Advantages for fiber lasers
High repetition-rate & average power
Excellent spatial mode
Low point instability
Maintenance–free operation
Energy structure
Yb-doped Fiber Amplifier

## Slide 8
Yb-doped Fiber Laser System

## Slide 9
Laser Specifications: Demonstrated
Green average power: 180 W
Point stability at 60 W
Timing jitter: 240 fs rms
Spatial mode: M^2 < 1.1 at 100W
Power stability at 100 W

## Slide 10
Layout of Laser Control for Beam Operation
Key control
Pulse pickers
Intensity control
Spatiotemporal shaping
Key diagnostics
Laser power and QE
Laser spatial profile
Point stability on cathode

## Slide 11
Final Laser System for Beam Operation
Laser MPS (done by Patrick):
temperature & pressure in chillers detected and linked to the room interlock.

## Slide 12
Laser Specifications for Beam Operation
Green average power: 72 W
Point stability at 30 W
Spatial mode: M^2 ~ 1 at 30 W
Power stability at 45 W

## Slide 13
Laser Power: Recent Performance
IR power: 36 hours
Green power: 12 hours
Measurement done by Patrick

## Slide 14
Ultrafast Pulse Picker
Major specifications
High extinction ratio: 42 dB
Variable bunch: 10-30 pulses
No change in few-months operation
Macro-bunch generator
9 MHz bunch rate

## Slide 15
High-power Pockels Cell for Bunch Pickup
Major specifications
High extinction ratio:>5*10^5 @green
Fast switch time: ~ 5 ns
High average power: 100W IR
Switch between pulsed & cw mode
MPS in the pulsed mode
Bunch pickup for beam diagnostic
30 pulses/bunch
4 bunches

## Slide 16
High-power fiber laser design specifications: demonstrated
Laser power (72W green), RMS time jitter (241 fs), excellent spatial mode (M^2<1.1), and laser point stability (<10 µm)
Ultrafast & high-power Pulse pickers
CW mode: 9 MHz bunch rate
Pulsed mode: single & multiple bunches for beam diagnostics
Laser used for 24/7 beam operation
Conclusion

## Slide 17
Laser System in the Lab