## Slide 1: Laser and Beam Intensity Feedback
K. Mernick
11/8/2018

## Slide 2: Outline
The goal of the intensity feedback is to have stable beam current. It became a high priority at the end of the run in order to study DC gun performance and separate beam loading effects from power supply ripple.
The RF group got involved because we have significant experience with feedback design and implementation, existing hardware, firmware, and software used in many different systems, and could get something running quickly.
After deciding on this approach on 8/21, we were testing feedback on the laser (without beam) by 8/30, with beam by 9/4, nested loops for laser and beam current tested on 9/7, and had a system usable without expert intervention by 9/13.
Performance of the feedback system meets the requirement of 2% rms stability with significant margin.
Some details to improve operational robustness and accommodate changes in the laser setup will be required before the next run.

## Slide 3: Laser Intensity Control
There are two devices that implement the intensity control of the laser
  A motor-controlled half wave plate provides a large dynamic range with slow response
  An electro-optical modulator provides a fast response, but has limited range
Initial attempts at feedback using photodiodes in the laser trailer were not successful – the intensity of the laser pulses delivered to the cathode did not correlate well with the measurements from the trailer
Laser source
HWP (Slow Intensity Control)
Temp. Shaping
Transport
Aperture
Gun Table
EOM (Fast Intensity Control)

## Slide 4: Laser Intensity Measurements
Initial measurements for intensity feedback were done with slow photodiodes, measuring at baseband. We looked at the 704 MHz component from 3 faster diodes to determine if we could find a good signal for the input to the feedback system.
The measurements after the shutter in the laser trailer and on the relay table in the laser transport did not correlate well with beam current. The measurement on the gun table did, so we went ahead with that signal as the input to the feedback.
Laser source
HWP (Slow Intensity Control)
Temp. Shaping
Transport
Aperture
Gun Table
EOM (Fast Intensity Control)
Laser trailer

## Slide 5: Measured Disturbances
Low frequency disturbances contributed the majority of the variations in the beam current

## Slide 6: Measured Disturbances
Same as last spectrum, zoomed in x-axis

## Slide 7: Feedback Design
Laser source
HWP (Slow Intensity Control)
Transport
Aperture
Gun Table
EOM (Fast Intensity Control)
DC Gun
FCT
Button
Pickup
Acceleration,
Transport,
Cooling
Σ
Σ
+
+
Laser
reference
Beam
current
reference
*
*

## Slide 8: Feedback Implementation
The EOM control block is basically identical to the cavity amplitude control for the 200 MeV H- LINAC (DC voltage control of a modulator on PA anode HV).
The nested loop structure for beam current and laser intensity is similar to an amplifier linearization loop inside a cavity feedback loop.

## Slide 9: Feedback Performance
Laser feedback without beam current feedback

## Slide 10: Feedback Performance
Laser feedback without beam current feedback

## Slide 11: Feedback Performance
Beam current & laser feedback

## Slide 12: Feedback Performance
Beam current & laser feedback

## Slide 13: To Do Going Forward
The EOM provides a (fast) voltage controlled attenuator. The HWP needs to be set so that there is enough headroom in the laser power for the EOM to regulate intensity.
A script automatically triggered by setpoint changes was used to send commands to the motor controller for the HWP based on an open-loop estimate of its required position.
We plan to implement feedback to set the HWP position to keep the EOM control voltage around some nominal level. This is conceptually similar to algorithms we have used for coarse and fine cavity tuners.
The technical hurdle for this is just making the pieces talk through the Control System. We need to coordinate this with the Controls and Instrumentation groups. (We have done this before for motors on various cavity tuners, but, on new systems, have taken full control of the motor with a controller integrated into the LLRF platform.)
The planned changes to the components on the laser table should not have a major impact on the feedback system.
Laser source
HWP (Slow Intensity Control)
Temp. Shaping
EOM (Fast Intensity Control)
AOM

## Slide 14: Conclusion
Intensity feedback achieved 0.3% rms beam current stability.
Minor changes are necessary for the next run, but the overall design has proven successful.